\publ\mpfet2.doc, formatted in word, 16 Feb. 2014

MINIMUM POWER FLUCTUATIONS EXTENDED TABLES

W.M. Hartman and J. Pumplin

Michigan State University, East Lansing, MI, 20 May 1991

This document was submitted to the Physics Auxiliary Publication Service

(PAPS). It has serial number PAPS JASMA-90-1986-15

This document is a supplement to the article "Periodic signals with minimal

power fluctuations" (MPF) from the Journal of the Acoustical Society of

America, volume 90, pages 1986-1999 (1991). To make sense of the tables in

this document, the reader must be familiar with the contents of the JASA

article.

Most of the tables below give phase angles for the harmonics of a complex

periodic waveform such that the power fluctuations in the waveform are

minimized, while maintaining a given power spectrum. The number of harmonics

is N. Some of the tables repeat tables from MPF. Most of the tables extend

those of MPF. Tables are as follows:

Table I. Wide-band equal-amplitude spectrum N=1-10 (from MPF).

Table IA: Wide-band equal-amplitude spectrum N=11-18.

Table IB: Wide-band equal-amplitude spectrum N=20,24,31,36,48,60.

Table II: Equal-amplitude signals: pitch/timbre studies (from MPF).

Table III: Wide-band spectra with uniformly decreasing amplitudes (from

MPF with the addition of N=40).

Table IV: Narrow-band equal-amplitude spectra N=1-10 (from MPF).

Table IVA: Narrow-band equal-amplitude spectra N=11-17.

Table IVB: Narrow-band equal-amplitude spectra N=21,24,31,36,48.

Table V: Pseudo-pulse spectra, p=1/4,1/5,1/6,1/7,1/8,1/10 (N=60).

Vowels Table: /a/, /i/, /u/, schwa (N=39).

Two tables give fourth moment, crest factor and relative peak factor

data for waveforms with known phase spectra.

Octave Table: number of octave components, N= 3-7.

Pseudo-sawtooth Table: number of harmonics, N=10.

A Figure shows the city-scape waveform that is the minimum fluctuation

waveform for a pseudo-pulse with p=1/6. The fragmentation factor is 2. For

most of the tables the harmonics have equal amplitudes. An exception is Table

III, where the amplitudes decrease with increasing harmonic number according

to the inverse first, or second, or third powers of the harmonic number. This

attenuation is approximately -6, -12, or -18 dB/octave, respectively. Inverse

first power also applies to sawtooth and pseudo-sawtooth waveforms. The

amplitudes for pseudo-pulses include a non-monotonic factor, as described in

MPF. Amplitudes for the steady-state vowels are given in the table itself.

They were calculated by Professor George Allen of Purdue University using

Klatt's synthesis algorithm (Klatt 1980).

Reference: Klatt,D.H. (1980) "Software for a parallel/cascade formant

synthesizer," J. Acoust. Soc. Am. &6&7, 971-995.

Table I Wide-band Equal-amplitude

N     3       4       5       6       7       8       9      10

Harmonic                    Phases (radians)

1   0.000   0.000   0.000   0.000   0.000   0.000   0.000   0.000

2   0.000   4.875   3  /2   5.436   5.170   5.399   5.238   5.079

3           5.363           3.373   0.242   4.729   5.201   4.921

4           1.465   3  /2   5.032   5.576   2.021   3.689   3.650

5                   0.000   0.679   2.349   5.544   0.734   0.400

6                           6.143   3.009   0.643   5.132   5.554

7                                   0.177   1.056   0.300   0.775

8                                           3.174   1.505   2.062

9                                                   3.583   4.077

10                                                           0.980

Check          11.703          20.664  16.523  22.566  25.382  27.496

Fourth   1.611   1.503   1.420   1.579   1.404   1.444   1.387   1.381

Crest   1.659   1.523   1.607   1.671   1.460   1.707   1.537   1.505

Rpeak   1.002   1.060   1.136   1.123   0.998   1.152   1.057   1.053

Caption Table I: A column of the table shows the phases that are needed to

make a waveform that has a minimum fourth moment by adding harmonics, as

defined in Eq.(1), all of the same amplitude. For each harmonic with non-zero

amplitude there is a phase angle in the table. For example, the column N=5

shows the phases to be used when the spectrum consists of the first five

harmonics. This table can be used to make waveforms that have as many as ten

harmonics, or as few as three.

Table IA Wide-Band Equal-Amplitude

N     11      12      13      14      15      16      17      18

Harmonic                      Phases (radians)

1   0.000   0.000   0.000   0.000   0.000   0.000   0.000   0.000

2   5.715   5.184   5.243   4.781   6.164   5.574   6.223   5.851

3   2.868   4.384   0.104   1.784   0.298   1.083   5.016   4.359

4   1.955   3.664   5.743   0.557   1.492   1.093   3.159   3.882

5   0.414   2.318   1.520   1.898   4.942   1.016   2.884   5.330

6   1.139   5.300   0.268   0.973   0.647   4.298   1.421   5.471

7   1.774   3.728   3.715   3.419   2.226   3.445   2.629   2.854

8   3.905   5.253   3.348   4.006   4.452   0.578   3.554   2.480

9   0.653   4.791   2.242   2.705   3.267   5.175   3.740   5.290

10   4.783   0.335   6.093   0.041   5.485   0.695   5.370   5.624

11   0.052   1.757   1.739   1.867   3.958   4.162   1.874   6.152

12           4.572   4.283   3.050   1.562   5.386   3.008   4.675

13                   5.627   0.538   1.571   2.310   0.797   1.793

14                           0.723   0.856   3.390   3.806   0.691

15                                   4.658   3.223   2.716   2.690

16                                           0.723   5.687   6.174

17                                                   2.718   2.581

18                                                           4.543

Check  23.258  41.286  39.925  26.344  41.578  42.153  54.601  70.440

Fourth   1.346   1.409   1.367   1.386   1.373   1.363   1.347   1.398

Crest   1.479   1.463   1.493   1.444   1.579   1.481   1.486   1.475

Rpeak   1.026   1.016   1.039   1.020   1.045   1.026   1.030   1.012

Caption Table IA: This table is an extension of Table I. It can be used to

make waveforms that have as many as 18 harmonics, or as few as 11. The

solutions in this table are local minima of the fourth moment that also have

small crest factors. Therefore, they are not necessarily the global minima of

the fourth moment.

Table IB Wide-band Equal-amplitude

Harms: 1 - 20, Check = 55.567, Fourth = 1.3538, Crest = 1.518

0.000  5.533  3.886  1.183  4.701  2.625  2.128  1.897

0.989  4.203  1.762  2.762  1.982  3.269  5.190  6.263

1.095  3.333  0.668  2.099

Harms: 1 - 24, Check = 68.597, Fourth = 1.3463, Crest = 1.531

0.000  4.912  3.737  0.883  3.823  2.954  3.949  0.349

1.511  0.822  3.412  4.992  2.700  0.680  5.834  6.218

0.325  1.419  5.908  1.753  2.021  5.796  0.883  3.717

Harms: 1 - 31, Check = 95.963, Fourth = 1.3402, Crest = 1.510

0.000  5.562  4.148  3.081  2.018  4.586  0.464  5.345

5.911  3.392  2.312  4.551  5.034  4.249  1.352  2.576

1.073  2.298  3.402  1.150  2.148  3.774  3.882  0.136

3.967  3.636  5.509  3.139  0.469  3.362  3.435

Harms: 1 - 36, Check = 116.599, Fourth = 1.3417, Crest = 1.560

0.000  6.054  4.327  0.477  6.195  4.811  0.841  1.431

5.255  5.485  1.205  1.068  2.562  4.539  4.650  2.115

3.643  3.337  2.739  2.429  6.145  5.742  0.268  4.778

1.665  1.374  3.566  0.186  4.093  5.082  1.895  5.869

2.588  5.448  2.404  2.334

Harms: 1 - 48, Check = 145.917, Fourth = 1.3512, Crest = 1.578

0.000  5.369  2.487  3.068  2.710  0.500  0.635  4.595

0.758  0.839  4.712  3.455  2.596  2.539  4.493  6.076

3.188  1.917  5.501  1.736  5.992  4.915  4.014  5.274

0.958  5.290  2.637  5.401  0.684  2.549  1.411  0.693

1.965  1.009  2.786  4.068  0.802  5.859  0.815  6.247

1.849  5.242  0.779  0.428  6.179  2.007  3.541  5.350

Harms: 1 - 60, Check = 194.059, Fourth = 1.3467, Crest = 1.563

0.000  5.678  3.070  1.089  3.540  0.077  4.478  3.347

1.529  6.089  3.453  1.954  6.239  0.287  6.148  3.963

4.354  4.607  5.092  4.672  2.496  0.647  2.353  5.916

5.428  5.148  2.514  2.142  4.381  1.379  4.861  0.141

3.832  1.696  2.339  4.227  3.492  4.459  3.339  4.200

4.344  0.316  2.930  3.585  0.692  3.745  5.694  1.206

1.687  4.597  0.179  1.498  4.298  3.607  5.173  5.959

0.234  5.222  0.078  4.362

Caption Table IB: An extension of Table I for a continuous band of harmonics

from harmonic number 1 to an upper limit of 20, 24, 31, ... All harmonics have

equal amplitude. A table should be read from left-to-right, top-to-bottom to

find phases in order of ascending harmonic number. Phases are given in radians.

Table II Equal-amplitude signals: pitch and timbre studies

bells      pipe

major   minor   organ      N = 5    N = 6   N = 7   N = 7

Harmonic        Phases (Radians)

1                   0.000

2   0.000           4.988        0        0       0

3                   0.585      7  /4              0     0

4   4.881           1.126      3  /2    2  /3     0     5.958

5   3.164   0.000                 /4    2  /3           1.368

6   3.452           4.921                               0.887

7                                         0       0     4.888

8   4.322           3.538                               5.960

9                                                       3.142

10   0.003   1.733

12           5.548   5.548

15           5.363

16                   4.303

20           4.606

24           2.760   2.759

Check  15.822  20.010  27.768      9  /2    10 /3    3     22.203

Fourth   1.787   2.251   1.691      1.660    1.694   1.520   1.590

Crest   1.961   2.128   1.803      1.698    1.719   1.556   1.725

Rpeak   1.222   1.482   1.247      1.201    1.215   1.074   1.214

Caption Table II: The first three columns give phases that minimize the fourth

moment for spectra, idealized from musical instrument tones, used in timbre

studies. The four columns to the right give phase angles for spectra with

missing fundamentals. For those harmonics where no phase is given the

amplitude is zero. Otherwise all amplitudes are the same.

Table III   Wide-band Spectra with uniformly-decreasing amplitudes

N     5       5       10      16      5       10      20      40

dB/8ve   -18     -12     -12     -12     -6      -6      -6      -6

Harmonic                        Phases (radians)

1                                   0.000   0.000   0.000   0.000

2                                   5.581   5.750   5.954   5.838

3                                   2.228   2.393   2.652   2.538

4                                   3.213   3.504   3.566   3.549

5                                   6.198   0.677   1.187   0.981

6                                           4.482   5.189   4.736

7                                           6.095   0.327   6.225

8                                           2.594   3.282   3.094

9                                           5.224   1.133   0.185

10                                           1.318   3.135   1.791

11                                                   5.723   5.009

12                                                   2.573   2.691

13                                                   5.150   4.304

14                                                   1.883   0.491

15                                                   4.589   0.874

16                                                   0.269   2.792

17                                                   3.891   3.502

18                                                   0.812   4.893

19                                                   2.450   6.152

20                                                   5.174   0.874

21                                                           2.774

22                                                           3.198

23                                                           4.566

24                                                           5.995

25                                                           1.100

26                                                           2.291

27                                                           2.985

28                                                           4.761

29                                                           5.948

30                                                           0.729

31                                                           2.016

32                                                           3.126

33                                                           4.692

34                                                           5.559

35                                                           0.769

36                                                           2.063

37                                                           3.022

38                                                           4.489

39                                                           5.691

40                                                           1.275

Check    2       2       4       8     17.220  32.037  58.941 127.569

Fourth   1.464   1.407   1.393   1.393   1.376   1.262   1.203   1.170

Crest   1.515   1.519   1.537   1.520   1.354   1.345   1.349   1.306

Rpeak   0.963   0.894   0.884   0.879   0.945   0.916   0.909   0.880

Caption Table III: Phases that minimize the fourth moment for amplitude

spectra having harmonics that decrease as the inverse cube, the inverse square

or the inverse first power of the harmonic number. Where no phase is given for

a harmonic the amplitude is zero.

Table IV Narrow-band Equal-amplitude Signals

N              3      4      5      6      7      8      9     10

Harmonic                            Phase (radians)

2            0.000  0.000

3            5.498  5.523  0.000  0.000

4            1.571  2.939  5.760  5.837  0.000  0.000

5                   4.815  5.236  1.621  6.200  6.010  0.000  0.000

6                          1.571  6.202  1.850  4.583  6.054  6.078

7                          4.189  0.729  1.611  5.240  0.436  4.740

8                                 4.053  5.474  0.396  0.002  4.064

9                                        0.882  2.618  3.732  0.047

10                                        4.590  0.640  2.552  6.077

11                                               3.792  5.537  2.235

12                                                      1.140  6.029

13                                                      3.919  2.411

14                                                             4.277

Check           7.069 13.277 16.755 18.441 20.608 23.279 23.372 35.959

Fourth           1.833  1.781  1.740  1.917  1.631  1.629  1.539  1.635

Caption Table IV: Phases that minimize the fourth moment for narrow-band

signals with equal-amplitude harmonics, for numbers of harmonics from 3

through 10.

Table IVA: Narrow-band Equal-amplitude Signals

N              11     12     13     14      15     16    17

Harmonic                            Phase (radians)

6            0.000  0.000

7            6.255  6.133  0.000  0.000

8            4.001  0.796  6.178  6.072  0.000  0.000

9            3.451  1.515  5.644  5.210  6.139  6.148  0.000

10            2.448  2.349  3.192  3.786  0.277  3.509  6.185

11            3.972  6.178  2.747  4.460  1.843  2.884  5.630

12            4.786  5.837  3.232  0.210  2.053  1.044  3.584

13            1.844  3.361  5.082  6.068  0.913  0.084  3.454

14            4.732  4.110  3.783  1.621  5.667  0.821  2.311

15            3.041  1.082  1.136  3.370  5.783  1.469  3.700

16            5.407  3.997  3.825  0.492  2.372  5.630  4.387

17                   1.654  4.518  3.468  4.402  0.739  4.677

18                          0.849  2.951  5.952  2.041  1.129

19                          3.876  5.919  3.310  5.040  3.466

20                                 3.267  1.547  2.637  5.102

21                                        4.883  5.301  2.988

22                                        1.932  3.697  6.144

23                                               5.871  4.930

24                                                      2.227

25                                                      5.349

Check           39.937 37.012 44.063 46.895 47.073 46.915 65.263

Fourth            1.581  1.640  1.580  1.583  1.563  1.576  1.564

Caption Table IVA: Continuation of Table IV, for total number of harmonics

between 11 and 17.

Table IVB Narrow-band Equal-amplitude Signals

21 Components, 11 - 31, Check = 75.921, Fourth = 1.553

0.000  6.220  0.924  1.232  3.678  3.834  5.461  3.745

3.202  4.520  2.800  1.716  5.235  5.392  3.692  3.009

6.088  2.918  5.324  2.001  4.931

24 Components, 12 - 35, Check = 69.954, Fourth = 1.556

0.000  6.173  0.050  0.079  1.126  1.161  1.758  5.567

4.600  5.498  3.458  1.822  2.897  0.238  4.529  1.680

0.939  4.969  3.425  5.996  2.020  3.899  5.915  2.157

31 Components, 16 - 46, Check = 80.166, Fourth = 1.537

0.000  6.205  0.105  0.801  5.919  1.733  0.053  2.334

0.590  3.096  0.012  4.567  5.556  0.315  4.318  2.139

3.223  4.408  2.271  0.186  0.820  2.809  5.490  6.140

2.762  3.348  0.156  0.226  4.719  3.442  2.423

36 Components, 18 - 53, Check = 117.890, Fourth = 1.546

0.000  6.267  6.260  0.124  1.438  1.067  1.211  1.498

5.633  5.596  4.522  4.628  1.942  2.316  5.971  3.175

3.025  6.025  1.038  6.077  3.748  1.684  5.404  3.830

6.282  1.151  3.120  4.015  0.531  5.460  1.951  3.950

0.346  3.910  0.877  3.817

48 Components, 24 - 71, Check = 135.140, Fourth = 1.548

0.000  6.218  1.027  2.040  3.011  3.739  4.410  0.727

0.524  1.238  1.016  0.204  0.641  0.261  3.158  2.765

1.939  1.454  1.598  3.279  0.581  6.013  3.626  2.519

0.002  0.038  5.399  3.816  4.894  6.242  2.733  5.610

4.931  2.357  2.848  5.780  2.053  3.710  0.519  2.966

0.855  5.072  2.441  6.011  2.758  5.506  1.595  5.017

Caption Table IVB: Continuation of Table IV for narrow-band equal amplitude

spectra. Phases are given in radians. A table should be read left-to-right,

top-to-bottom to find phases in order of ascending harmonic number.

Table V Pseudo Pulse

Duty factor 1/4, Check =  135.940, Fourth =  1.2846    ( 2.3333)

0.000  6.217  3.014         3.008  5.823  1.349         2.631  4.509

1.002         1.036  4.328  3.021         0.993  0.098  3.644

3.294  0.636  4.547         3.762  1.482  6.086         4.676  3.170

0.764         0.294  4.174  2.572         1.212  6.060  3.600

3.340  0.960  5.053         4.473  2.324  6.060         6.060  3.402

0.616         0.942  4.442  1.591         2.259  5.338  2.077

Duty factor 1/5, Check =  152.143, Fourth =  1.2369    ( 3.2500)

0.000  5.908  2.455  3.531         5.005  6.035  2.490  2.479

5.107  5.169  1.772  2.438         4.261  4.954  1.288  2.182

3.618  4.843  1.489  0.420         4.246  3.495  0.127  1.463

2.589  4.132  0.702  5.429         3.618  2.345  5.339  0.687

1.651  3.324  6.166  4.324         2.851  1.290  4.327  6.173

0.740  2.479  5.256  3.181         1.912  0.231  3.359  5.262

Duty factor 1/6, Check =  157.671, Fourth =  1.1700    ( 4.2000)

0.000  5.472  1.909  3.039  5.998         4.321  0.942  2.056  4.827

3.946         0.908  0.022  2.713  3.895  0.656         5.224  1.775

2.892  5.748  4.656         1.922  0.803  3.482  4.786  1.671

6.194  2.633  3.698  0.423  5.347         3.011  1.534  4.216  5.738

2.739         1.073  3.579  4.404  1.449  6.084         4.188  2.191

4.917  0.601  3.886         3.113  5.938  4.319  0.227  2.503

Duty factor 1/7, Check =  158.487, Fourth =  1.1094    ( 5.1667)

0.000  5.097  1.468  2.685  5.368  4.099         0.951  6.139  2.481

3.695  0.128  5.051         1.904  0.897  3.493  4.704  1.177  5.995

2.862  1.939  4.505  5.711  2.235  0.646         3.826  2.981

5.517  0.430  3.305  1.568         4.799  4.026  0.243  1.427  4.394

2.467         5.786  5.078  1.249  2.414  5.518  3.318         0.512

6.146  2.245  3.381  0.428  4.046         1.580  0.996  3.253  4.326

Duty factor 1/8, Check =  170.394, Fourth =  1.1207    ( 6.1429)

0.000  5.162  2.011  3.377  5.645  4.424  4.956         0.004  4.190

5.513  0.926  6.054  0.701  2.498         6.216  1.312  2.556  1.472

2.814  4.325  2.737         3.358  4.238  3.090  4.872  0.025  3.863

3.232         5.720  4.658  0.887  2.220  5.117  3.963  4.004

5.903  3.237  4.377  0.303  5.460  5.879  1.979         5.436  0.126

1.834  0.878  1.574  3.537  2.426         2.014  3.454  2.538  3.303

Duty factor 1/10, Check =  172.812, Fourth =  1.1109    ( 8.1111)

0.000  5.482  3.287  5.096  0.708  6.181  1.535  3.128  1.829

3.487  4.526  3.430  0.240  2.086  4.485  3.527  5.074  0.403

5.071  0.668  2.053  1.027  3.616  5.387  2.009  1.023  2.246

3.722  2.421  4.208  5.623  4.823  0.632  2.200  6.277  5.319

1.985  1.472  5.773  1.502  3.021  2.356  4.113  5.314  4.273

6.055  0.229  5.622  2.669  4.804  0.484  6.048  1.706  2.555

Caption Table V: Phases for pseudo-pulse waveforms made from 60 harmonics

of pulse waveforms with duty factors  1/4, 1/5 ... 1/10. Phases and check

sums are in radians, entries are blank where the amplitude is zero. The

fourth moment is given for the pseudo-pulse; the fourth moment for the pulse

follows in parentheses.

Octave Table: Equal-amplitude octave harmonics

N      3       4       5       6       7

Octaves    2       3       4       5       6

Top h      4       8      16      32      64

Sum of cosines with alternating sign (0,   ,0, ...)

Fourth   1.8333  1.8750  1.9800  2.0833  2.1735

Crest   1.6534  1.9464  1.9739  2.2798  2.2676

Rpeak   1.1411  1.2481  1.3805  1.4916  1.5891

Sum of sines (3 /2, 3 /2, 3 /2 ...)

Fourth   1.8333  1.8750  1.9800  2.0833  2.1735

Crest   1.8229  1.7637  1.9520  2.1509  2.2110

Rpeak   1.2890  1.2472  1.3802  1.5209  1.5634

Sum of cosines - (worst possible) ( 0, 0, 0, ...)

Fourth   3.1667  3.3750  3.4200  3.4167  3.3980

Crest   2.4495  2.8284  3.1623  3.4641  3.7417

Rpeak   1.3732  1.5453  1.7254  1.8776  2.0234

Caption Table Octave: The special case of octave spectra, where the only

non-zero harmonics are 1,2,4,8, ... The choice of phases that minimizes the

fourth moment corresponds to summing cosine terms with alternating sign, or,

equivalently, to summing sine terms. This is the correct choice no matter what

the amplitudes of the components.  The actual values of the fourth moment, the

crest factor, and the relative peak factor, given in rows Fourth, Crest, and

Rpeak, do depend upon amplitudes. They are here given for the case where all

non-zero amplitudes are the same. The final block gives these statistics for

the worst possible choice of phases, a sum of cosine terms. The five columns

show results for a total number of harmonics from 3 to 7, for a span of two to

six octaves, where the highest harmonic ranges from 4 to 64.

Table Pseudo-sawtooth Wide-band 1/N-amplitude

Harmonic  Amplitude           Phases (radians)

PS(a)   PS(b)   PS(c)  PS(d)    MPF

1     1.13601    3  /2   0.000   3  /2  0.000   0.000

2     0.56800    3  /2   0.000   0.000  3  /2   5.752

3     0.37870    3  /2   0.000   3  /2  0.000   2.395

4     0.28400    3  /2   0.000   0.000  3  /2   3.505

5     0.22720    3  /2   0.000   3  /2  0.000   0.685

6     0.18934    3  /2   0.000   0.000  3  /2   4.487

7     0.16229    3  /2   0.000   3  /2  0.000   6.100

8     0.14200    3  /2   0.000   0.000  3  /2   2.604

9     0.12622    3  /2   0.000   3  /2  0.000   5.253

10     0.11360    3  /2   0.000   0.000  3  /2   1.343

Check     3.32736     15     0.000   15 /2  15 /2  30.120

Fourth                1.951   5.783   1.507  3.742   1.262

Crest                1.939   3.327   1.708  2.462   1.345

Rpeak                1.371   1.470   1.097  1.741   0.915

Caption: Table Pseudo-sawtooth: In the first column is the amplitude spectrum

for a low-passed sawtooth, used by Plomp and Steeneken in their study of phase

perception. There are ten harmonics (n=1-10) with amplitudes proportional to

1/n, and normalization such that the total power is 1. The next four columns

give phases used by Plomp and Steeneken, the final column gives phases that

minimize the fourth moment for this spectrum. Phases are given in radians.

Vowels Table, Steady Vowels

/a/                /i/                /u/               schwa

F1 BW1  700     130        310      45        360     65         500      65

F2 BW2 1220      70       2020     200       1250    110        1500     100

F3 BW3 2600     160       2960     400       2200    140        2500     200

n    ampl.  phase       ampl.  phase       ampl.  phase       ampl.  phase

1  0.6047   0.000     0.6766   0.000     0.6587   0.000     0.4463   0.000

2  0.3739   6.202     0.8516   6.144     0.6431   5.666     0.3129   5.710

3  0.3056   0.098     0.4655   2.699     1.0206   2.393     0.3836   5.053

4  0.2865   2.290     0.1161   3.125     0.2030   3.647     1.1272   1.957

5  0.3104   0.033     0.0546   4.619     0.0960   1.179     0.2355   3.225

6  0.6210   4.097     0.0330   3.155     0.0639   4.881     0.1102   3.154

7  0.3676   2.487     0.0233   5.596     0.0534   2.020     0.0736   0.219

8  0.2397   2.583     0.0185   1.671     0.0560   1.290     0.0605   3.445

9  0.1573   5.533     0.0160   0.278     0.0814   3.287     0.0591   1.574

10  0.6016   0.604     0.0152   4.755     0.1694   5.290     0.0702   1.239

11  0.3057   3.471     0.0155   2.287     0.0615   2.876     0.1145   6.219

12  0.1411   3.962     0.0174   3.562     0.0317   5.156     0.2828   2.359

13  0.0494   3.471     0.0216   5.143     0.0223   1.828     0.1025   3.600

14  0.0351   4.863     0.0306   0.625     0.0191   4.050     0.0562   3.543

15  0.0231   1.693     0.0525   3.507     0.0194   4.006     0.0420   0.914

16  0.0554   1.884     0.1000   1.359     0.0245   0.827     0.0379   4.145

17  0.0767   1.215     0.0816   3.835     0.0435   2.788     0.0400   2.025

18  0.0688   3.804     0.0580   4.711     0.0473   0.235     0.0502   2.491

19  0.0619   0.276     0.0518   0.467     0.0208   2.713     0.0787   1.059

20  0.0645   2.377     0.0553   2.132     0.0130   5.520     0.1255   2.725

21  0.0791   2.888     0.0688   0.265     0.0101   1.326     0.0835   3.594

22  0.1389   5.156     0.0992   3.801     0.0092   1.203     0.0569   3.581

23  0.1545   4.635     0.1577   3.568     0.0095   4.108     0.0495   2.033

24  0.1345   1.311     0.2266   0.178     0.0113   1.661     0.0528   2.296

25  0.1296   1.809     0.2829   1.847     0.0161   3.096     0.0695   1.721

26  0.1150   2.188     0.3731   5.837     0.0262   0.997     0.1066   2.272

27  0.0754   5.119     0.3210   2.999     0.0270   2.202     0.1049   1.584

28  0.0624   5.482     0.2173   4.605     0.0210   1.887     0.0788   2.087

29  0.0733   3.679     0.1994   2.098     0.0215   1.708     0.0784   1.239

30  0.0209   6.115     0.2013   0.499     0.0236   1.318     0.0844   6.232

31  0.0363   2.105     0.0881   6.125     0.0111   6.267     0.0388   1.176

32  0.0476   3.814     0.0397   2.649     0.0053   1.217     0.0182   0.227

33  0.0352   0.889     0.0222   4.028     0.0031   2.461     0.0105   0.776

34  0.0159   0.611     0.0144   1.698     0.0021   0.744     0.0070   0.232

35  0.0011   2.697     0.0103   6.241     0.0015   5.637     0.0051   5.753

36  0.0028   4.510     0.0080   0.000     0.0012   3.856     0.0040   4.029

37  0.0106   5.335     0.0067   1.834     0.0010   5.938     0.0034   4.040

38  0.0197   1.330     0.0059   4.588     0.0009   2.405     0.0030   5.897

39                     0.0055   5.805     0.0009   4.624     0.0028   2.013

Check  5.9028 110.619     5.1029 118.337     3.5510 112.307     4.6671 105.436

Caption Vowels Table: Four steady-state vowel sounds with fundamental

frequency  F0 = 125 Hz. Formant center frequencies F and bandwidths BW are

given in  Hz. Amplitudes of the harmonics are from Klatt's synthesis program.

They  are normalized so that each vowel has unit power. There are 39 harmonics

(n)  for all vowels except /a/ for which there are 38. The phases (given in

radians) minimize the power fluctuation.

FIGURE CAPTION

Figure 7: The pseudo-pulse with a duty factor of 1/6, computed from 60

components with phases given by Table V, plus 196 additional components of

higher frequency. The fragmentation factor is 2. Therefore, there are 12

buildings in the city.