## Slide 1: CMX: Update on status and planning
Yuri Ermoline, Wojciech Fedorko @CERN
Dan Edmunds, Philippe Laurens, Chip Brock @MSU
Michigan State University
7-Mar-2012

## Slide 2: CMX development work on 3 fronts
VME/ACE/TTC interface “daughter card” @CERN
  Yuri
CMX input module firmware @CERN
  Wojtek and Yuri
Engineering @MSU
  Philippe, Dan, and Chip

## Slide 3: Initial CMX design studies phase
Addressed two main questions:
  FPGA choice for implementing the Base-CMX functionality
  Strategies, costs and risks for adding Topological Processing capability to the CMX platform

## Slide 4: Definition: Base-CMX functionality
All of CMM functionality (both Crate CMM and System CMM)
  Receive and process 400 JEM/CPM input signals (@4x CMM rate)
  All Crate CMXs send local summary to their System CMX through backplane connectors over LVDS cables (@higher rate than CMM)
  System CMXs form and send triggering information to CTP over LVDS cables (same as CMM)
  all CMXs send ROI and DAQ information over G-links (same as CMM)
Send JEM/CPM info out to a TP optically
  using 12-fiber ribbons
  with some level of duplication (at least 2x copies sent)
  6.4Gbps nominally sufficient for all raw data on one 12-fiber ribbon
  also possible to send zero-suppressed data on less fibers

## Slide 5: Definition: TP-CMX functionality
Topological Processing capability on CMX platform
Receive optical inputs from some/all 12x CMXs
Run multiple Topological Algorithms
Send Topological Triggering Information to CTP
TP-CMX functionality is needed if dedicated TP is not built, or availability delayed, or as additional safety/backup
The CMX platform could then be asked to provide some generic TP functionality
Or added flexibility: “TP-CMX” capability could also be used to support future upgrades e.g. new Base-CMX algorithms needing a larger volume of Crate->System communication

## Slide 6: Initial CMX design studies phase
Started with guidance from Stockholm Review
  Use Xilinx Virtex 6
  Design for 6.4Gb optical outputs
  Implement G-link encoding on FGPA
  Generally be conservative to deliver on time
Conclusions from Feb 2012 Technical Workshop at RAL
  Recommend Two FPGAs: one for Base-CMX + one for TP-CMX function
  Two CMX types: e.g. an implementation might be 1 (plus spares) with 2 FPGAs, 11 (plus spares) with 1 FPGA
  Plan for operating the Crate CMX to System CMX LVDS cables at up to 4x current speed, i.e. 160Mbps  may require new cables or RTMs
  Base-CMX function should provide 2x 12-fiber output ribbons
  TP-CMX function should receive 3x 12-fiber input ribbons

## Slide 7: Dual FPGA: Base-CMX and TP-CMX
If TP-CMX functionality is desired on CMX platform  use two FPGAs:
Base-CMX and TP-CMX are totally separate functions:
  logically don't share inputs or outputs
  operationally in separate latency time segments
TP-CMX needs access to CTP output  simply do not choose a System CMX to operate as a TP CMX
Separate Base-CMX from TP-CMX firmware  Easier commissioning, easier operation, easier firmware management and easier updates
Use smaller Virtex 6 package LX550T-FF1759 for both FPGAs
Layout made simpler by separating routing challenges
A board TP CMX capability was originally only an option.
  Accepting the RAL recommendations with Two CMX types will require only a modest increment in cost.

## Slide 8
VME-- Interface
TP-CMX FPGA
Virtex-6
LX550T-FF1759
Base-CMX FPGA
Virtex-6
LX550T-FF1759
12x Optic OUT
12x Optic OUT
12x Optic IN
12x Optic IN
12x Optic IN
DAQ
ROI
DAQ
ROI
TCM Interface
VME--
TCM
Inputs from all
JEM or CPM
processors
from this crate
LVDS cables
From Crate
To System CMX
400 single ended
@ 160Mbps
3x27 LVDS pairs
@ up to 160 Mbps
2x 12-fiber
ribbons OUT
3x 12-fiber
ribbons IN
6.4 Gbps outputs
to Standalone TP
and/or TP-CMX
2x G-Link Out
2x G-Link Out
6.4 Gbps inputs
re-bundled from
up to 12 Base-CMX
CTP output
2x33 LVDS pairs
@ 40 Mbps
(from TP-CMX
via Base-CMX)
CMX Card with Base-CMX functionality and TP-CMX capability

## Slide 9
VME-- Interface
Base-CMX FPGA
Virtex-6
LX550T-FF1759
12x Optic OUT
12x Optic OUT
DAQ
ROI
TCM Interface
VME--
TCM
Inputs from all
JEM or CPM
processors
from this crate
LVDS cables
From Crate
To System CMX
400 single ended
@ 160Mbps
3x27 LVDS pairs
@ up to 160 Mbps
2x 12-fiber
ribbons OUT
6.4 Gbps outputs
to Standalone TP
and/or TP-CMX
2x G-Link Out
CMX Card with Base-CMX functionality only
CTP output
2x33 LVDS pairs
@ 40 Mbps
(System CMX
only)

## Slide 10: Overview of possible usage options
Flexibility is illustrated in following diagrams…
CMM emulation only
Base-CMX functionality only
  Send data to Standalone TP (Raw or Zero-suppressed)
TP-CMX functionality used
  Only CMX-TP
  Both CMX-TP and Standalone TP
  In Crate to System CMX communication (not used as TP)

## Slide 11
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
LVDS
Cables
Crate
CMXs
System
CMXs
- - - - - - - -
1. CMX emulation of CMM functionality (no TP involved)

## Slide 12
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
LVDS
Cables
Crate
CMXs
System
CMXs
- - - - - - - -
to CTP
Standalone
Topological
Processor
2. Standalone TP receiving Raw CMX Inputs
12
12 x 12-fiber ribbons
1 x 12-fiber ribbon

## Slide 13
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
LVDS
Cables
Optical
Patch
Panel
Crate
CMXs
System
CMXs
- - - - - - - -
to CTP
Standalone
Topological
Processor
N x 12
3. Standalone TP receiving Zero-Suppressed CMX Inputs
12 x 12-fiber ribbons
12
1 x 12-fiber ribbon

## Slide 14
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
LVDS
Cables
Optical
Patch
Panel
TP-
CMX
FPGA
to CTP
TP-
CMX
FPGA
to CTP
Crate
CMXs
System
CMXs
- - - - - - - -
4. One (or more) CMX TP receiving Zero-Suppressed Inputs
1 x 12-fiber ribbon
12
12 x 12 fiber ribbons
3 x 12-fiber

## Slide 15
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
LVDS
Cables
Optical
Patch
Panel
TP-
CMX
FPGA
to CTP
Crate
CMXs
System
CMXs
- - - - - - - -
5. CMX TP & Standalone TP receiving Zero-Suppressed Inputs
1 x 12-fiber ribbon
12
12 x 12-fiber ribbons
3 x 12-fiber
to CTP
Standalone
Topological
Processor
N x 12-fiber ribbons

## Slide 16
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
LVDS
Cables
Optical
Patch
Panel
TP-
CMX
FPGA
to CTP
Crate
CMXs
System
CMXs
- - - - - - - -
6. CMX TP receiving Zero-Suppressed & Standalone TP raw inputs
2 x 12-fiber ribbon
24
12 x 12-fiber ribbons
3 x 12-fiber
to CTP
Standalone
Topological
Processor
12 x 12-fiber ribbons

## Slide 17
Electron
Energy
Jet
Tau
Base-
CMX
FPGA
to CTP
LVDS
Cables
to CTP
to CTP
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
Base-
CMX
FPGA
LVDS
Cables
LVDS
Cables
Optical
Patch
Panel
TP-
CMX
FPGA
to CTP
Crate
CMXs
System
CMXs
- - - - - - - -
7. Example of TP-CMX FPGA in Crate to System communication
1 x 12-fiber ribbon
4 x 12 fiber ribbons
3 x 12 fibers