## Slide 1: Atlas L1Calo CMX Card
CMX is upgrade of CMM with higher capacity
Inputs from JEM or CPM modules
  40 → 160Mbps (400 signals)
Crate CMX to System CMX Cable IO
  40 → 160Mbps (81 signals)
Output to CTP
  40 → 80Mbps (66 signals)
Bigger FPGA (Xilinx Virtex 6 VLX550T)
  e.g. for additional thresholds
Functionality new to CMX
Cluster information sent by each CMX to Topological Processor
  Two 12-fiber ribbons of optical output @6.4Gbps per fiber
Optional partial TP capability included
  A Standalone TP is being built but some TP capability is still desirable on the CMX platform
  Three 12-fiber ribbons of optical input at @6.4Gbps per fiber
  Separate Virtex 6 FPGA used for TP Functionality (optionally installed)
    Most CMX cards will be built without the TP FPGA installed
MSU 29-Aug-2012

## Slide 2: Atlas L1Calo CMX Card
Main Data Path
  Backplane Inputs, Cable IO and CTP Output all understood
    Maximized signal integrity
    Critical for 160Mbps bandwidth
    All critical signals between ground planes
    PCB trace layout optimized (no extra vias)
    Pin assigment verified for firmware routability
    24-layer card
  Working on details of Optical IO
Ancillary Functions
  Understanding Power issues
    Sizing power supplies
    Need to satisfy firmware requirements
    Investigating FPGA heat dissipation
  Working on Clock Distribution
    All clocks and IOs are synchronized to TTC
  Optimizing overall parts placement
MSU 29-Aug-2012

## Slide 3: Atlas L1Calo CMX Card
VAT card: parallel effort and study platform
VME/ACE/TTC (VAT) ancillary functions of CMX
Redesign of CMM with new components
    Most ancillary functions fit in single Support FPGA
Build a 6U VME test card
  Include a small Virtex 6
  Practice firmware configuration via System ACE
  Test bed of operating environment for CMX
  Can start design of CMX control Software
  Lessons and details to be merged into CMX
PCB done June 2012
Currently working on
  Firmware for VAT card
  Test Firmware for Virtex 6 FPGA
  Test Stand and software
MSU 29-Aug-2012