~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

                   ********************************
                   *                              *
                   *   L15CT_PROV Specification   *
                   *                              *
                   *       and User's Guide       *
                   *                              *
                   ********************************

                                                    14-NOV-1994 

This document describes the input, operation, and output of L15CT_PROV, 
the Level 1.5 Calorimeter Trigger's Pulser Run Offline Verification 
system.  

This document consists of 6 parts:

    I. L15CT_PROV Philosophy

   II. L15CT_PROV Input 

   II. L15CT_PROV Tests

  III. L15CT_PROV Output

   IV. L15CT_PROV Usage

    V. Integration of L15CT_PROV into the Pulser Special Runs


I. L15CT_PROV Philosophy
------------------------

L15CT_PROV is a testing program which is run on the Level 1 and Level 1.5
Calorimeter Trigger data which are collected during the Dan Owen Pulser
special runs.  The primary focus of L15CT_PROV testing is verification 
of the input data to the Level 1.5 Calorimeter Trigger.  This verification
is done by comparing the Level 1.5 Calorimeter Trigger input energies to
the energies expected based on the Level 1 Calorimeter Trigger ADC
Counts.

The kinds of errors that L15CT_PROV will help find are:

    - CTFE output bits stuck high or low
    - CTFE-to-ERPB cable failures
    - Data quality problems along ERPB>DC>CRC chain
    - CRC-to-C40 cable or driver problems
    - 'C40 Comm Port synchronization problems

In each Dan Owen Pulser special run, approximately 100 events are
collected.  Each event is different, but all have some fraction of the
calorimeter "lit up" with Pulser data.  Some simulate large energy
deposits, while others simulate small energy deposits.  This provides a
useful, varied range of Trigger Tower data to the Level 1.5 Calorimeter
Trigger.  

NOTE:  since pulser patterns are fixed (?), we should be careful about 
pathological problems--i.e. bit of value 128 never turns on (perhaps
only at some eta/phi), etc.  Pathological problems don't necessarily
doom L15CT_PROV, but we should not fool ourselves about what we are and
are not testing.  

L15CT_PROV is separate from the MONITOR stream-based testing (based on
Mark and Force Pass events collected during global running of the Level
1.5 Calorimeter Trigger) which is also planned for the Level 1.5 
Calorimeter Trigger.  MONITOR stream-based testing will compare the
Level 1.5 Calorimeter Trigger to the L15CT Simulator.  This will allow
the input data, intermediate results (i.e. Local Object Lists), and
final triggering decision to be verified (but on "random" beam
crossings, that typically have very little calorimeter activity). 


II. L15CT_PROV Input
--------------------

L15CT_PROV requires Crates 11 (the Level 1 Data Block) and Crate 81
(The Level 1.5 Calorimeter Trigger Data Block) to be present in the TRGR
Bank.  Additional crates and banks may also be present in the data file
without affecting L15CT_PROV.  All events captured must be Level 1.5 
Calorimeter Trigger Mark and Force Pass events (to provide the
necessary Level 1.5 Calorimeter Trigger input energy data).  Events
which do not meet the above criteria will be "skipped" by L15CT_PROV as
it processes a data file, generating an error message.  

Note that L15CT_PROV can be run on any data file (not just Dan Owen
Pulser runs) which meets this specification, but will typically be run
on Pulser data.  


III. L15CT_PROV Tests
---------------------

L15CT_PROV performs only one type of test:  it compares each Level 1.5
Calorimeter Trigger input energy (as recorded in the Type 1 Entries in
the DeBug Section of the Level 1.5 Calorimeter Trigger Data Block
produced by each Mark and Force Pass event) to the energy expected based
on the Level 1 Calorimeter Trigger ADC Counts (as recorded in the Level
1 Calorimeter Trigger Data Block).  Note that the EM and Total Et for
each Trigger Tower must be compared against BOTH copies which appear in
Type 1 Entries from adjacent Local DSP's.  

This test is done for the EM and Total Et for each Trigger Tower in
an event.  The test is then repeated for each event in the data file.


IV. L15CT_PROV Output
---------------------

L15CT_PROV needs to report the following kinds of information

    - For every event that has no data errors, an "Event OK" message

    - For every L1-to-L15 mismatch, an error message containing
        Run #
        Event #
        eta/phi
        L15 CT input energy expected (in HEX, not GeV)
        L15CT input energy found (in HEX, not GeV)
        LDSP id
        Energy type (EM or Total)
        Rack # (1 or 2)

    - File Summary
        Number of events examined
        Number of events 100% OK
        Number of events with errors

Its output is an ASCII file (similar to the TRICS LOG), with status
messages also being displayed on the user's screen.  Example status/error
message formats are:

"Event OK"

Run  85659    Event       13: OK


"L1 vs L15 mismatch (example when both copies bad)"

Run  84885    Event     7840: Data Mismatch Error
   Eta/Phi -16/ 1   LDSP A3  Total Et  Rack 1   Expected $1C   Found $18
   Eta/Phi -16/ 1   LDSP A3  Total Et  Rack 2   Expected $1C   Found $18
Run  84885    Event     7840:    2 Errors found


"L1 vs L15 mismatch (example when only one copy bad)"

Run  84885    Event     7840: Data Mismatch Error
   Eta/Phi -16/ 1   LDSP A3  Total Et  Rack 2   Expected $1C   Found $18
Run  84885    Event     7840:    1 Errors found


"Summary in log file"

Summary:    200 events processed
            195 events OK
              5 events with errors (examine log file)



IV. L15CT_PROV Usage
--------------------

L15CT_PROV is built by the Program Builder.  It uses the D0USER Frame.
For correct operation, the logical L1SIM_RCP must be defined to point to
a suitable RCP file.  Note that, at this writing (14-NOV-1994), the file
D0$LEVEL1:L1SIM.RCP is NOT suitable, as it points to an incorrect 
lookup table file.  The lookup table that is required is
D0$LEVEL1$DATA:CALORIMETER_TRIGGER.LSO, not 
D0$LEVEL1$DATA:L1SIM_COVERAGE_THRU_ETA_16.LSO as selected.  Note also 
that the appropriate LSO file is in the TEST area, so additionally
a $LIBTEST LEVEL1 must be performed before executing L15CT_PROV.  

L15CT_PROV uses the standard D0USER Frame.  To process a data file,
simply select <Auto Process> and respond to the prompts.  L15CT_PROV
will generate 2 output files:

    D0USER_<run number>.OUT     (run summary file)

    L15CT_PROV.LOG              (detailed error log)

Note also that it is possible to use L15CT_PROV to select only L1.5 Cal
Trig Mark and Force Pass Events.  Use the <Output Data Files> menu
option to select a file to contain the Mark and Force Pass Events.  If
desired, all banks except the TRGR bank may be dropped.  All events which
meet the selection criteria (i.e. contain TRGR bank crates 11 and 81,
and are L1.5 Cal Trig Mark and Force Pass Events) will be written to the
output file.  


V. Integration of L15CT_PROV into the Pulser Special Runs
----------------------------------------------------------

In order to have L15CT_PROV usable in the Dan Owen Pulser runs, several
things need to happen:

    1. The L1.5 CT must be programmed appropriately in the run
       configuration, including being read-out and having its Data
       Block included in the output file.

    2. We either need to add L15CT_PROV processing to the current Dan
       Owen executable, or build L15CT_PROV as a separate standalone
       product which would be run in addition to the Dan Owen
       executable.  

    3. Whoever runs the program needs to look at the output.  

If Dan Owen will be the designated L15CT_PROV driver and output checker,
we should make certain that he can parse the output (and is happy with
the format).  If we will be the designated drivers, we need to set up a
mechanism by which we are informed when a new data file is available.