Michigan State University,                          Revised  13-JAN-1994 

              +-------------------------------------------------+
              |    DESCRIPTION OF THE COMMUNICATION STANDARD    |
              |                  BETWEEN COOR                   |
              |        AND THE TRIGGER CONTROL SOFTWARE         |
              +-------------------------------------------------+

                                B.Gibbard, BNL.
                          D.Edmunds, P.Laurens, MSU.


1.  DECNET CONNECTIONS BETWEEN COOR
    AND THE TRIGGER CONTROL SOFTWARE

2.  REQUEST MESSAGE GENERAL FORMAT:

3.  ACKNOWLEDGE MESSAGE FORMAT:

4.  INITIALIZE:

    EXPLICIT REQUEST                                           INITIAL
    IMPLICIT REQUEST
    STATE AFTER INITIALIZATION

5.  STOP:                                                         STOP

6.  PAUSE/RESUME and BEGIN/END RUN:                                   

       a) PAUSE/RESUME:                                          PAUSE
                                                                RESUME         
       b) BEGIN/END RUN:                                      WRT_HOST  BEG_RUN
                                                              WRT_HOST  END_RUN
       c) synchronization with begin/end run:                 WRT_HOST  SYNCHRO
                                                                               
7.  SET SPECIFIC TRIGGER:

       a)  AND-OR Input Terms Programming:                    SPECTRIG ANDORREQ
       b)  Mapping of Specific Trigger                        SPECTRIG STARTDGT
           versus Start Digitize:
       c)  Mapping of Front End Busy                          SPECTRIG  FEBZDIS
           versus Disable Specific Trigger:
       d)  Global Enabling of Specific Trigger:               SPECTRIG   ENABLE
       e)  Enable Obeying Crate Busy                          SPECTRIG OBEYBUSY
           Disabling Requests:
       f)  Enable Obeying Second Level Supervisor             SPECTRIG OBEYLEV2
           Disable Requests:
       g)  Enable Prescaling and Set Ratio:                   SPECTRIG PRESCALE
       h) Enable Auto disabling of Specific Trigger:          SPECTRIG  AUTODIS
       i)  Reenable Auto-disabled Specific Trigger:           SPECTRIG REENABLE
       j) Remove a Specific Trigger                           SPECTRIG     FREE
          from the list of allocated resources:
       k)  Messages Associated with the Prescaler Tunning Feature.
          k.1)  Load Specific Triggers Readout Times          SPECTRIG  RD_TIME
          k.2) Desired Usage of Acquisition Bandwidth         AUTOTUNE ACQBANDW
          k.3) Auto-Prescale Set of Specific Triggers         SPECTRIG AUTOTUNE
       l) Clear Specific Trigger Scalers                      SPECTRIG RESETSCL
       m) Level 1.5
          m.1) Identifying Specific Trigger for Level 1.5     SPECTRIG L15_TYPE
          m.2) Programming Requirements on Level 1.5 Term     SPECTRIG L15_TERM

8.  SET GEOGRAPHIC SECTION:

    Turn off start digitize signal:                           GEO_SECT DGTZ_OFF

9. LOAD REFERENCE SET

    a) definition
    b) vocabulary
    c) TRD trigger candidate list
    d) most likely properties of reference sets
    e) wish list
    f) syntax definition                                        REFSET     EMET
                                                                REFSET   HDVETO
                                                                REFSET    TOTET
    g) Large Tile Threshold Reference Sets                      REFSET LRG_TILE
    h) examples of range specification

10. EXCLUDE ONE TRIGGER TOWER FROM ALL CONTRIBUTION:
                                                               EXCLUDE  EMTOWER
                                                               EXCLUDE  HDTOWER
11.  LOAD GLOBAL THRESHOLD:

       a)  EM Et Threshold:                                   THRESHLD  EMETSUM
       b)  HD Et Threshold:                                   THRESHLD  HDETSUM
       c)  TOT Et Threshold:                                  THRESHLD TOTETSUM
       d) Second Energy Lookup Thresholds.                    THRESHLD  EML2SUM
                                                              THRESHLD  HDL2SUM
                                                              THRESHLD TOTL2SUM
       e)  MISS-Pt-THRES:                                     THRESHLD MISPTSUM
       f)  EM Et Trigger Tower Count:                         THRESHLD  EMETCNT
       g)  Total Et Trigger Tower Count:                      THRESHLD TOTETCNT

12.  SPECIFIC TRIGGERS VERSUS REFERENCE SETS IN LEVEL 1 JET LIST TO LEVEL 2

       a)  EM Et Jet List                                     ST_VS_RS  EM_LIST
       b)  TOT Et Jet List                                    ST_VS_RS TOT_LIST
       c)  Large Tile Jet List                                ST_VS_RS LRG_TILE

13.  LEVEL 1.5 CALORIMETER TRIGGER PROGRAMMING

       a) Definitions
       b) L1.5 Cal Trig Term Reference Sets                   L15CTERM   REFSET
       c) L1.5 Cal Trig Term Local DSP Tool Definition        L15CTERM  LOC_DSP
       d) L1.5 Cal Trig Term Global DSP Tool Definition       L15CTERM GLOB_DSP
       e) L1.5 Cal Trig Term Frame Code Parameters            L15CTERM FRAMECOD
       f) Specific Trigger versus L1.5 Cal Trig Term          L15CTERM ST_VS_TM
       g) Start L1.5 Cal Trig System                          L15CTSYS    START
       h) Load L1.5 Cal Trig executables                      L15CTSYS LOADCODE


1.  DECNET CONNECTIONS BETWEEN COOR AND THE TRIGGER CONTROL SOFTWARE

    0) COOR  and the  Trigger   Control  Software use   "established  links" to
       communicate.   Connections  must be  first  explicitly  opened, then any
       number of  messages can be  exchanged.  The links  should be explicitely
       closed by COOR when communication is finished.

       The communication  consist of Request Messages  from COOR to the Trigger
       Control  Software  and of   Acknowledgement  Messages  from  the Trigger
       Control Software to COOR.

       Only reply  messages solicited by  a Request Message  from COOR are sent
       from the Trigger Control Software  to COOR. No asynchronous messages are
       sent by the Trigger Control Software to COOR.

    PROTOCOL FOR OPENING THE CONNECTION

    1) the "Request Message Link" is first initiated by the Trigger Control
       Software using ELNCON's ELN_ACCON routine.
       This is the normal waiting state before connections are made.
       The advertized object name is "COOR_REQ".

    2) COOR must  then connect to  this object  using  ELNCON's NETCON routine,
       specifying its username and password along with the node name.

       COOR's username is  "COOR", password  "PASSWORD". At D0 Hall COOR should
       thus give D0HTCC"COOR PASSWORD" to  NETCON as a paramter for the name of
       the ELN node. The  authorization service is  currently not checking this
       field but will be turned on in the  close future in order to protect the
       Trigger Control Node Disk and response time.

    3) the "Acknowledge Message Link" is then initiated by the Trigger Control
       Software using ELNCON's ELN_ACCON routine.
       The advertized object name is "COOR_ACK"

    4) COOR must  then connect to  this object  using  ELNCON's NETCON routine,
       specifying its username and password along with the node name.

    PROTOCOL FOR EXCHANGING MESSAGES

    5) The Trigger Control Software then waits for a message to be received on
       the Request Message Link (ELNCON's ELN_GETNEW).

       If a Request  Message is not  received with a  correct status at step #5
       and 6, the Trigger Control Software  immediately returns to step 1 (e.g.
       if the link is closed without explicit exit message).

    6) On reception of  a message sent by  COOR (ELNCON's  SNDNEW), the Trigger
       Control Software  satisfies internal  synchronization protocol before it
       parses the Request and executes the necessary programming actions.

       Note  that no  additional   messages from  COOR to  the  Trigger Control
       Software may be sent while a Request is being serviced.

    7) After  completing the  requested  action, the  Trigger  Control Software
       sends a reply on the Acknowledge  Message Link (ELNCON's ELN_SNDNEW) and
       returns to step #5.

       If an Acknowledge  Message is not sent with a correct status at step #7,
       the Trigger Control Software immediately returns to step #1 (e.g. if the
       Acknowledge Link is closed before the reply is sent).

    8) COOR must be waiting  for this reply (ELNCON's  GETNEW) or must have set
       an AST sub process to receive the Acknowledgement (ELNCON's ESTAT).

       COOR can  then send as  many messages as  desired on  the opened Request
       Message Link starting at step #6

    PROTOCOL FOR CLOSING THE CONNECTION

    9) COOR should  initiate the  closing of  the links to  the Trigger Control
       Software with the message:
              12121212     EXIT
       char # 1......8 10....17

   10) The  Trigger Control  Software  will reply  with a  specific Acknowledge
       message:
              43434343   ACKNOW 12121212       OK     EXIT
       char # 1......8 10....17 19....26 28....35 37....44

   11) The Trigger Control Software  disconnect the links (ELNCON's ELN_DISCON)
       and  returns to  step #1.  COOR should  also  close the  links (ELNCON's
       DISCON) at reception of the Acknowledgement.


2.  REQUEST MESSAGE GENERAL FORMAT:

         01234567 SPECTRIG REENABLE *************************** . . .****
         Message  Object   Action   description of Items to Modify
         Number   Type     Type     (further messages may include file name(s))
char #:  1......8 10....17 19....26 28......................... . . .1122
         \-------------------------/\-------------------------- . . .---/
         Fixed Format                Variable Format
         Fixed Length                Fixed Length

    a) the total  length of the Request  Messages is fixed  at 1122 characters.
       Shorter messages must be filled with trailing spaces.

    b) all keywords  in the fixed format  section of the  messages are always 8
       character long and right justified (i.e. include the necessary number of
       leading space characters).

    c) separation characters (char# 9, 18 and 27) must be ASCII space (code 32)

    d) some  messages  accept  NEGATIVE  item  numbers  implying  NEGATING  the
       requested action.

    e) as  many   individual items  as  desired  can be  specified  in a single
       Request.  The  number of  items is  only  limited by  the  fixed message
       length.

    f) optional spaces are  ALLOWED anywhere in the  message list except within
       keywords and between  digits of a same number  (in the limit of rule g).
       Spaces are NOT REQUIRED before or after parenthesis or minus signs.
       ex: 13( -23 45  ), 13 ( -23 45 ),  13 ( - 23 45 )  are all equivalent to
       13(-23 45).

    g) As soon as the  Trigger Control Software  encounters 8 consecutive space
       characters in  the variable  format  section of the  Request Message, it
       considers the rest of the string as empty and stops parsing it.


3.  ACKNOWLEDGE MESSAGE FORMAT:

         01234567   ACKNOW ABCDEF01      BAD    PARAM ********* . . .****
         Message  Message  Request  Final    Supplem  Auxiliary String
         Number   Type     Number   Status   Info     (UNUSED)
char #:  1......8 10....17 19....26 28....35 37....44 46....... . . ..561
         \-------------------------------------------/\-------- . . .---/
         Fixed Format                                  Variable Format
         Fixed Length                                  Fixed Length

    a) the total length of the Acknowledge Messages is fixed at 561 characters.
       Shorter messages must be filled with trailing spaces.

    b) all keywords  in the fixed format  section of the  messages are always 8
       characters long and  right justified (i.e.  include the necessary number
       of leading space characters).

    c)  parsing the  Final  Status Field  for the  keyword OK  or BAD is always
       sufficient  to  know  whether  the  action  requested  was  successfully
       performed.

    LIST OF POSSIBLE ACKNOWLEDGEMENT MESSAGES

             56789ABC   ACKNOW 12345678       OK     DONE
    Request legal and understood and action successfully performed.

             56789ABC   ACKNOW 12345678       OK NOCHANGE
    Request legal and understood and action successfully performed, but warning
    that the  requested configuration  already existed at  least for one of the
    specified  items  (e.g.  Request to  disable an  already  disabled Specific
    Trigger).

             56789ABC   ACKNOW 12345678      BAD  UNKNOWN
    Unrecognized keyword(s) parsed in the fixed format section of the Request
    Message.

             56789ABC   ACKNOW 12345678      BAD   FORMAT
    Illegal format parsed in the variable format section of the Request
    Message. (e.g. unclosed parenthesis)

             56789ABC   ACKNOW 12345678      BAD    PARAM
    ILLEGAL parameter values parsed in the variable format section of the
    Request Message (e.g. illegal minus sign)

             56789ABC   ACKNOW 12345678      BAD    RANGE
    Attempt to  use  unavailable  resources (i.e.  not in  COOR's configuration
    file).

             56789ABC   ACKNOW 12345678      BAD  FAILURE
    A Failure was detected while executing the requested action, the
    corresponding resource is unusable and should be removed from the
    configuration file until it is repaired.
    A Significant Event Message will also be sent to the D0 Alarm System with
    more details about the failing hardware (not yet implemented in July 89).

4.  INITIALIZE:

    EXPLICIT REQUEST

             12345678  INITIAL

    This command will place  the First Level Trigger  in its operational state.
The following is a  description of the state of the  Trigger Framework after an
initialize message.

    The following items will remain true until a stop message is sent by COOR.

    a) initialized for  normal operation of the  Trigger Framework all internal
       timing and control registers not accessed by COOR.

    b) synchronize the  internal double buffering of  the Trigger Framework and
       initialize  the data block  builder to be  ready to  build and send data
       blocks.

    The following items will remain true until a message from COOR modifies the
state of the trigger.

    c) globally  ensure that no Specific  Trigger is  enabled to send any start
       digitize signal nor build any data block.

    d) all  global  scalers  reset to  zero,  i.e  scalers not  associated with
       individual Specific Triggers. (e.g. Trigger Number Scaler)


    IMPLICIT REQUEST

    COOR implicitly  allocates a new Specific  Trigger by mentioning it for the
first time in a message. The Trigger  Control Software will place this Specific
Trigger in a  defined initial  state, before  acting on it  accordingly to this
Request Message from COOR.

    Once allocated, COOR will have full control over a Specific Trigger until a
release  message for this  Specific Trigger  or a global  initialize message is
sent to the Trigger Control Software.

    Unallocated Specific Triggers are  left for the Trigger Control Software to
privately use  to test the  operation of the  allocated  Specific Triggers. The
Trigger Control Software might utilize  spare resources and run active tests in
order  to  facilitate  and  quicken the   detection and   diagnosis of hardware
problems.

    It is however guaranteed that no start digitizing signal or data block will
ever be sent by Specific Triggers in test mode. It is also guaranteed that COOR
will  never be  denied the  use of  a  Specific  Trigger that  is advertized as
available  in  the   configuration  file. In a  case  were the  Trigger Control
Software is privately using a Specific  Trigger at the time COOR claims it, the
Trigger  Control Software  would immediately  allocate the  Specific Trigger to
COOR, initialize it, and  notify the active test  process of the new allocation
of this Specific Trigger.

    STATE AFTER INITIALIZATION

    A definition of the  initial state of a Specific  Trigger at the time it is
allocated  to  COOR  follows.  This  state is  not  guaranteed  for unallocated
Specific Triggers.

    a) the  Specific  Trigger  will  have its  Andor  Input Terms  requirements
       programmed in a manner guaranteed not to be met.

    b) The Specific Trigger is globally  disabled

    c) The  Specific  Trigger Firing  vs. Start  Digitizing  Geographic Section
       Lookup  Table is  programmed in  such a way  that this  Specific Trigger
       induces  the  digitization  of none  of the   geographic  sections. This
       includes geographic section #31 (i.e. no Start Data Block).

    d) The  Geographic  Section  Front-end  Busy vs.  Disable  Specific Trigger
       Lookup Table is  programmed in such a way that  this Specific Trigger is
       disabled by none of the geographic  section front-end busy signals. This
       includes  that it  will  not be  requested  disabled  by the  Data Block
       Builder Full signal.

    e) the prescaler is disabled

    f) the autodisable feature is disabled

    g) The decision made by  the Geographic Section  Front-end Busy vs. Disable
       Specific Trigger Lookup Table is obeyed

    h) The level 2 disable signal is not obeyed

    i) Specific Trigger Fired Scaler is zeroed, Specific Trigger Enabled Scaler
       is also zeroed. Both scaler will  remain zero since the Specific Trigger
       is disabled.

    j) each scaler  associated to a  source of veto will be  zeroed, prescaler,
       autodisable,  front-end busy, level  2.0 will not  increment. the global
       disable veto counter will start incrementing.

    k) the Specific Trigger  Andor Fired Scaler is  zeroed and will remain zero
       because the Andor Input Term condition is guaranteed not to be met.


5.  STOP:

             9ABCDEF0     STOP

    This characterizes  the end of a run, COOR  releases all resources. It will
take a new INITIALIZE message for COOR to regain control of the trigger.

6.  PAUSE/RESUME and BEGIN/END RUN commands:

       a) PAUSE/RESUME:

             9ABCDEF0    PAUSE
             9ABCDEF0   RESUME

    If a set of items  need to be  modified all at the SAME  TIME for different
objects and WHILE the  experiment clock and beam is  running, COOR will need to
force the Trigger  Framework to pause, then modify  the resources, and then let
the Trigger resume its operation. No  simultaneity can otherwise be guaranteed.
Even within a  single  message, as soon as  more than one  IO to the trigger is
neccessary   to  execute  the  action(s)   requested,  the  action  will not be
simultaneous.

    At reception of a Pause message, all 32 Specific Triggers will stop firing,
and all Data  Block  Building Cycles  (currently in  progress or  waiting) will
naturally complete. When a Resume message is received, all 32 Specific Triggers
are simultaneously  exposed to the  next beam crossings  according to their new
programming. All subsequent First  Level Data Blocks will thus also reflect the
updated programming of the First Level Trigger.


       b) BEGIN/END RUN, PAUSE/RESUME RUN, BEGIN/END STORE:

             12345678 WRT_HOST  BEG_RUN directory:file_name_with_run_number
             12345678 WRT_HOST  END_RUN directory:file_name_with_run_number
             12345678 WRT_HOST PAUS_RUN directory:file_name_with_run_number
             12345678 WRT_HOST RESU_RUN directory:file_name_with_run_number
             12345678 WRT_HOST BEG_STOR directory:file_name_with_run_number
             12345678 WRT_HOST END_STOR directory:file_name_with_run_number

    All of these commands request TCC to open and write a file on the D0::
host cluster containinig scaler count information. The framework must have
already been placed in a PAUSE state for this command to be accepted by
TCC. This is a necessary requirement for proper access to the requested
data.

    COOR will send TCC a complete file specificataion describing a
directory on the D0 cluster and a complete file name. TCC will take care of
the host decnet address field. By convention, the file name should include
a description of the file type (e.g. 'BEGIN_RUN') and the run number.
System Logical defined on the D0 cluster are accpetable for the directory
name. 


    Upon reception of a begin or end run message (or Pause/Resume Run, or
Begin/End Store message),  TCC will initiate the procedure for performing
the operation and immediately return an acknowlegement message to COOR. The
acknowledgement will be returned to COOR before the file has been written
or even opened.

             56789ABC   ACKNOW 12345678       OK INITIATE

    If the request is sent to TCC while the framework is not in a paused
state, the following acknowledgement message is returned.

             56789ABC   ACKNOW 12345678      BAD RUNGOING 


       c) synchronization with begin/end run:

             12345678 WRT_HOST  SYNCHRO

    The "SYNCHRO" synchronization message provides the means to verify the
completion status of the begin/end run requests. 

    After the begin/end run request (or Pause/Resume Run, or Begin/End
Store) has been initiated by the messages described in the previous
paragraph, TCC will open the requested file on the host cluster over
DECnet, read out and format scaler counts out of the Level 1 hardware, and
then write the file. This procedure may potentially take several seconds,
especially during the file opening step.

    The immediate acknowledgement feature described in the previous
paragraph has the advantage of releasing the ELNCON communication
subprocess of COOR, and leaving it available for communication with Level 2.  

    However further activity from COOR with Level 1 (e.g. resume the run)
and the luminosity server (e.g read the file) might depend on the
completion of the writing of the file to the host. COOR thus needs a
mechanism to verify that the operation is completed before initiating
subsequent activities.

    Upon reception of a SYNCHRO message from COOR, TCC will check 
for the completion status of the previous begin/end run (or Pause/Resume
Run, or Begin/End Store) request. If the  procedure is not yet completed
TCC will wait for up to ten more seconds. 

    If (or when) the procedure is successfully completed, TCC will return
the following acknowledgement:

             56789ABC   ACKNOW 12345678       OK     DONE

    If the procedure failed while opening the file on the host, TCC will
return the following acknowledgement:

             56789ABC   ACKNOW 12345678      BAD     OPEN ELN_message_string

    If the procedure failed while collecting the Level 1 data (hardware
failure), TCC will return the following acknowledgement:

             56789ABC   ACKNOW 12345678      BAD     DATA 

    If the procedure failed while writing a record to the file on the host,
TCC will return the following acknowledgement:

             56789ABC   ACKNOW 12345678      BAD    WRITE ELN_message_string

    If the procedure failed while closing the file on the host, TCC will
return the following acknowledgement:

             56789ABC   ACKNOW 12345678      BAD    CLOSE ELN_message_string

    If the procedure did not complete before the timeout period, TCC will 
abort it and return the following acknowledgement:

             56789ABC   ACKNOW 12345678      BAD  TIMEOUT 


7.  SET SPECIFIC TRIGGER:

       a)  AND-OR Input Terms Programming:

             01234567 SPECTRIG ANDORREQ 21(1 -4 -125) 25(13 -54 225)

    The specified  Andor Input Terms in  the parenthesis  are to be used in the
decision   made by  the  Specific   Trigger  number  specified  in front of the
parenthesis. A POSITIVE  NUMBER means that the  Andor Input Term is REQUIRED to
be ASSERTED in the Andor Input  Network, a NEGATIVE number means that the Andor
Input Term is REQUIRED to be NEGATED.

    In each list, all unspecified Andor  Input Terms will be programmed so that
they do not participate in this Specific Trigger decision.

    All unspecified Specific Triggers are not modified.

    note: in  order to remove  one Andor Input  Term from the  Specific Trigger
configuration,  it is  necessary to  re-specify the  complete  list omiting the
Andor Input Term to remove.

       b)  Mapping of Specific Trigger versus Start Digitize:

             01234567 SPECTRIG STARTDGT 21(5 7 24 31) 25(3 5 22)

    All  Geographic Sections  specified inside  the  parenthesis will receive a
Start  Digitization  Signal  after a  successful  trigger  decision made by the
Specific Trigger specified with the number preceding the parenthesis.

    In each list, all unspecifed  geographic sections will be programmed not to
receive a start digitize from this Specific Trigger.

    All unspecified Specific Triggers are not modified.

    This command does not accept negative numbers.

    note: in  order to  remove  all  sections from  the list,  an empty pair of
parenthesis must be given after the Specific Trigger number.

       c)  Mapping of Front End Busy versus Disable Specific Trigger:

             01234567 SPECTRIG  FEBZDIS 17(6 23 26 13)

    The Specific Trigger specified by  the number preceding the parenthesis may
be disabled by any of the  Front-End Busy Signals  from the Geographic Sections
specified inside the parenthesis.

    In each list, all unspecified Geographic Sections will be programmed not to
disable this Specific Trigger.

    This command does not accept negative numbers.

    Note: The crate busy enable mask must also be set for a Specific Trigger to
obey the Geographic Section Busy signal (see item 7e).

       d)  Global Enabling of Specific Trigger:

             DEF01234 SPECTRIG   ENABLE 4 23 -27

    A Specific  Trigger  specified  with a  positive number  will be enabled to
operate normally and will fire as soon as the Programmed and-or input terms are
satisfied  if  none of  the  enabled  sources  of  disabling is  asserted (e.g.
Front-End Busy, 2nd Level, Autodisable...).

    A Specific Trigger  specified with a negative  number will be programmed to
be disabled from firing.

    All unspecified Specific Triggers are not modified.

       e)  Enable Obeying Crate Busy Disabling Requests:

             01234567 SPECTRIG OBEYBUSY 12 23 -5

    A Specific Trigger  specified with a positive  number will be programmed to
obey    the      Front-End    Busy     disable    signal  that comes out of the
front-end-busy-vs-disable-specific-trigger   lookup  memory. A Specific Trigger
specified with a negative number will be programmed not to pay attention to the
output from that look up memory.

    All unspecified Specific Triggers are not modified.

       f)  Enable Obeying Second Level Supervisor Disable Requests:

             01234567 SPECTRIG OBEYLEV2 12 -7

    A Specific Trigger  specified with a positive  number will be programmed to
obey the  all-nodes-in-queue-are-busy  disable signal  coming directly from the
Level 2 Supervisor. A Specific Trigger specified with a negative number will be
programmed   not to  pay   attention to  the  signal  coming  from  the Level 2
Supervisor.

    All unspecified Specific Triggers are not modified.

       g)  Enable Prescaling and Set Ratio:

             01234567 SPECTRIG PRESCALE 23(24583) 5(17)

    The Specific Trigger specified by the number preceding the parenthesis will
be set with the prescale ratio specified inside the parenthesis. (maximum ratio
is 16777215)

    An empty  pair of   parenthesis or a  prescale  ratio of 1  will remove the
prescaling feature.

    All unspecified Specific Triggers are not modified.

    This command does not accept negative numbers.

       h) Enable Auto disabling of Specific Trigger:

             01234567 SPECTRIG  AUTODIS 12 -7

    A Specific Trigger  specified with a positive  number will be programmed to
be  automatically disabled  after firing. A  Specific  Trigger specified with a
negative number will be programmed to remove the auto-disable feature.

     SPECTRIG  REENABLE is  the  command  necessary  to reset  the auto-disable
flip-flop once a Specific Trigger programmed with autodisable has fired.

    All unspecified Specific Triggers are not modified.

       i)  Reenable Auto-disabled Specific Trigger:

             DEF01234 SPECTRIG REENABLE 28 13

    All Specific Triggers specified will be reenabled and will be ready to fire
only once more if they have been programmed to be automatically disabled.

    This command does not accept negative numbers.

    All unspecified Specific Triggers are not modified.

       j) Remove a Specific Trigger from the list of allocated resources:

             01234567 SPECTRIG     FREE 23 24

    This means that COOR will stop using  the specified Specific Triggers which
thus may   (should?) be  used by  D0TCC to  perform  the best  possible trigger
integrity tests. COOR can start using  again any one of these Specific Triggers
at any time, it will be automatically reinitialized as soon as COOR mentions it
again in a message.

    This command does not accept negative numbers.


       k)  Messages Associated with the Prescaler Tunning Feature.

                k.1)  Load Specific Triggers Readout Times

             01234567 SPECTRIG  RD_TIME 0 (30) 1(250) 4(300)

    The  readout time  specified in  milliseconds  inside  parenthesis is to be
associated with the Specific Trigger  specified with the number in front of the
parenthesis. The allowed range is 0 to 10000 ( 0-10 seconds ).

    No  modification is made at  this time to  the programming  of any Specific
Trigger.  The   parameters  given here  will  only be  used  when a request for
auto-prescaling specific triggers is received.

    The  default  value for a  newly  allocated   specific  trigger remains 100
milliseconds untill explicitly modified.

    All unspecified specific triggers are not modified.

    This command does not accept negative numbers.


                k.2) Desired Usage of Acquisition Bandwidth

             01234567 AUTOTUNE ACQBANDW 75

    The  number  specified in  the  message  represents  the  percentage of the
acquisition  bandwidth that the  Trigger Control  Software should consider as a
target when  auto-prescaling a set of  Specific  Triggers. The allowed range is
from 1 to 100%.

    No  modification is made at  this time to  the programming  of any Specific
Trigger.  The   parameter  given  here  will  only be  used  when a request for
auto-prescaling specific triggers is received.

    The default value after an  initialize framework message remains 50% of the
acquisition bandwidth untill explicitly modified.

    This command does not accept negative numbers.


                k.3) Auto-Prescale Set of Specific Triggers

             01234567 SPECTRIG AUTOTUNE  0 3 6

    The list of numbers specified  represents the set of Specific Triggers that
the Trigger Control Software is  expected to prescale for an equitable usage of
the available acquisition bandwith.

    The Specific Triggers  readout times and the  available bandwidth to use as
parameters are specified in the two messages described above (k.2 & k.3)

    The previous prescale ratios are overridden and lost. This command does not
affect the programming  nor the operation of all  unspecified Specific Triggers
and they will remain able to fire unless the framework was explicitly paused by
a previous message.

    This command does not accept negative numbers.

    The method used in finding appropriate rates requires 4 steps:

    i)   disable all Specific Triggers in the specified set
    ii)  read the average unscaled andor firing rate over a 5s sample time.
    iii) compute and program the necessary prescaling ratios.
    iv)  enable all Specific Triggers in the specified set

    The   algorithm  used by  the  Trigger  Control   Software in  step iii) to
calculate the prescaling ratio is described below. The symbols are defined as:

    N  for the number of Specific Triggers in the set (1<=N<=32)
    A  for the available acquisition bandwidth (0<A<=1)
    Ti for the readout time in seconds of the ith Specific Trigger (Ti>=0)
    Ri for the unscaled andor firing rate in Hertz (Ri>=0)
    Pi for the prescaled ratios being computed. (Pi>=1)

    The  N  Specific   Triggers  in  the set  are  first   arranged in order of
increasing Ri*Ti. The  Specific Trigger with i=1  thus has the smallest product
of rate times readout time (i.e. the smallest bandwidth requirement).

    Starting with i=1, the N prescale  ratios are successively calculated using
the formula:
                       Ri * Ti * ( N + 1 - i )
                Pi = --------------------------
                              j=i-1
                              ---    Rj * Tj
                      ( A -   >      -------  )
                              ---       Pj
                              j=1

    and Pi is  rounded to  the  nearest integer,  but set to  1 if the formula
yields a number smaller than 1.

       l) Clear Specific Trigger Scalers

             01234567 SPECTRIG RESETSCL 0 3 6

    All Specific Triggers specified will have their associated scalers reset to
zero.

    These consist of:
        the Specific Trigger Fired Scaler,
        the Specific Trigger Enabled Scaler,
        the Specific Trigger Andor Fired Scaler,
        all the Specific Trigger Veto Scalers by source of disable:
                Prescaler,
                Auto-Disable,
                Global,
                Level 2,
                Level 1.5,
                Front-End Busy

    None of the Global Scalers (Trigger Number, Beam Crossing Number,...) are
reset by this message. Only the INITIALIZE message will reset theses global
scalers.

    This command does not accept negative numbers.

    All unspecified Specific Triggers are not modified.

       m) Level 1.5

    Specific Triggers can be of two types: pure Level 1 Specific Triggers or
Level 1.5 Specific Triggers (cf. 7.m.1)

    A Level 1.5 Specific Trigger will receive 2 levels of requirements. It
rereceives normal Level 1 Requirements (as for every Specific Trigger) on
Andor Terms, Front-end Busy, Prescaler, etc... Additional Level 1.5
Requirements are set on Level 1.5 Input Terms (cf. 7.m.2)

    When Level 1 Requirements are met for any one (or more) of the pure
Level 1 Specific Triggers, the event is immediately accepted. Moreover all
Level 1.5 Specific Triggers having met their Level 1 Requirements will be
set as good. All pure Level 1 or Level 1.5 Specific Triggers that didn't
meet their Level 1 Requirements are not set.

    When all the Specific Triggers that fired were of type Level 1.5, a
Level 1.5 confirmation cycle is started for all the Level 1.5 Specific
Triggers that passed their Level 1 Requirements.

    The event will be accepted as soon as any one of the Level 1.5 Specific
Triggers for which the cycle was started receives a positive confirmation.
Moreover all other Level 1.5 Specific Triggers having met their Level 1
Requirements but still waiting for confirmation will be set as good.
All Level 1.5 Specific Triggers that either did not meet their Level 1
Requirements or that already received a negative Level 1.5 confirmation
are not set.

    A Level 1.5 confirmation cycle is aborted after a fixed timeout period
of ?200? microseconds and the event is passed. At that time all Level 1.5
Specific Triggers having met their Level 1 Requirement but still waiting
for confirmation will be set as good. All Level 1.5 Specific Triggers that
either did not meet their Level 1 Requirements or that already received a
negative Level 1.5 confirmation are not set.

    The event is not passed if all the Level 1.5 Specific Triggers that
passed their Level 1 Requirements have all received negative Level 1.5
confirmations.

          m.1) Identifying Specific Trigger for Level 1.5

         01234567 SPECTRIG L15_TYPE 12 23 - 5

    A Specific Trigger specified with a positive number will be set to
require a Level 1.5 confirmation.

    A specific Trigger preceded by a minus sign will be set to a pure
Level 1 Specific Trigger.

    All unspecified Specific Triggers are not modified.

    The Specific Trigger number is an integer in the range from 0 to 31.
COOR's configuration file will show which subset of the Specific Triggers
hold the ADDITIONAL property of allowing Level 1.5 requirements. Please
note that Specific Triggers flagged as allowing Level 1.5 Requirements
may be used as pure Level 1 Specific Triggers as well.

          m.2) Programming Requirements on Level 1.5 Term

         01234567 SPECTRIG L15_TERM 12(1 13)  5 (3)

    The Specific Trigger number specified in front of a parenthesis will
accept confirmation from either one of the Level 1.5 Terms specified in
the parenthesis.

    The Level 1.5 confirmation will be considered positive as soon as one
of the Level 1.5 Terms in the list is returned asserted. The Level 1.5
confirmation will be considered negative only after all the Level 1.5 Terms
in the list are returned negated.

    In each list, all unspecified Level 1.5 Terms will be programmed so
that they do not participate in the Level 1.5 decision for this Specific
Trigger.

    All unspecified Specific Triggers are not modified.

    note: in order to remove one Level 1.5 Term from the Specific Trigger
configuration, it is necessary to re-specify the complete list omiting the
Level 1.5 Term to remove.

    note: before the Trigger Framework can consider the Level 1.5 terms for
a given specific trigger it must have passed all of its level 1
requirements and have been flagged as being of type Level 1.5 (cf. 7.m.1)


8.  SET GEOGRAPHIC SECTION:

    Turn off start digitize signal:

             01234567 GEO_SECT DGTZ_OFF 13 25 -9

    Each Geographic Section receives two signals from the Trigger Framework.
These are the Start Digitize Signal and the Hold Transfer Signal. Their
mode of operation during normal data taking is described in D0 Note 827.

    This command will alter the normal mode of operation by preventing Start
Digitize Signals to be sent out, the Hold Transfer Signals are not affected.
This mode of operation is used for test with events downloaded into front-end
crates.

    A Geographic Section specified with a positive number will have its
Start Digitize Signal turned off. A Geographic Section specified with a
negative number will be returned to its normal mode of operation.

    If a Specific Trigger fires which is programmed to require the digitization
of a Geographic Section whose Start Digitize Signal is turned off, then this
Geographic Section will receive the Hold Transfer pulse, but will not receive
any Start Digitize Pulse.

    All unspecified Geographic Sections are not modified.

9. LOAD REFERENCE SET

    a) definition

    The Calorimeter  Trigger builds  two types of global  counts of Trigger
Towers carried  over the whole  detector. Moreover,  four separate sums are
built for each type of count.

    The first type of count concerns the Electro-Magnetic Trigger Towers. A
Trigger Tower will be included in an  EM Trigger Tower Count only if its EM
energy deposit reached or exceeded its programmed transverse energy minimum
threshold. Optional vetoes can also be programmed  for the Hadronic Trigger
Towers. A Trigger Tower will be  included in an EM Trigger Tower Count only
if its Hadronic energy  deposit did not reach or  exceed its  programmed HD
transverse energy veto.

    The Second type  of count concerns  the Total (i.e.  Electro-Magnetic +
Hadronic) Trigger Towers. A Trigger Tower will be included in a TOT Trigger
Tower Count only if its  Total (=EM+HD) energy  deposit reached or exceeded
its programmed transverse energy minimum threshold.

    b) vocabulary

    Since all three  types of  threshold can be  separately programmed for
each trigger tower, the name "Reference Set" was chosen to characterize the
set of all individual  thresholds of a given type  specified over all
Trigger Towers.

    There    are  thus   three   types  of     Reference  Sets   called the
Electro-Magnetic Transverse Energy (EM Et) Reference Set, the Hadronic Veto
(HD Veto) Reference Set, and the Total Transverse Energy (TOT Et) Reference
Set.

    Four separate Reference Sets are available for each type, numbered from
0 to 3. The EM Et  Reference Set #0 (respectively  1, 2 or 3) is associated
with the HD Veto  Reference Set #0 (respectively  1, 2 or 3) to produce the
EM Trigger Tower Count #0 (respectively 1, 2 or 3).

    c) TRD trigger candidate list

    The  EM Et  #0 and  HD  Veto #0   Reference  Sets have  the  additional
particularity  to control the  list of  Trigger Towers  passed as "electron
candidates" to  the TRD  Trigger. This  special Reference  Set may still be
used in triggering (i.e.  global thresholds can  be set on the global count
and comparisons  can be required in  the andor  programming of any Specific
Trigger).

    d) most likely properties of reference sets

    The values of the  thresholds in each  reference set are most likely to
be chosen   uniformly  constant over  the whole  detector,  or show a small
number  of    discontinuity   boundaries  in   (eta,phi)  between which the
thresholds   remain  uniformly  constant.

    It is  also most  likely  for the   thresholds to be  chosen  uniformly
constant  for all the  32 Trigger  Towers at a  given eta.

    It is also most likely  for the thresholds to  be chosen symmetric with
respect to the  z=0 plane,  that is have  identical  thresholds for eta and
minus eta.

    e) wish list

    A  special  effort is  made in the  choice  of  syntax in  order to (a)
simplify and (b) summarize the  transfer of the information and in order to
(c) enhance the meaningful information  in the message (i.e. the pattern of
the thresholds over the detector, and its eventual symmetry aspects) out of
the 32*20*2=1280 individual thresholds values in each reference set.

    The  syntax for  addressing  Trigger  Towers  should (a)  allow for the
programming of groups of towers specified as ranges in eta and phi indices,
(b)  separate the sign  and  magnitude of eta  index to  emphasize eventual
symmetry  or  asymmetry, (c)  not  prevent from  still  addressing a single
tower, (d) allow to program the most  likely cases in a single message, but
(e) also allow  a  multi-message definition  for  complicated patterns, (f)
allow omission of the sign of eta  when the specification is symmetric with
respect  to the  z=0  plane, (g)  allow  omission of  the phi  range for an
azimuthally regular range.

    f) syntax definition

01234567   REFSET     EMET SIGN_ETA(POS NEG) MAGN_ETA(1:20) PHI(1:32) 2(10500)
01234567   REFSET   HDVETO MAGN_ETA(1:5) 3(10500) MAGN_ETA(6:20) 3(8000)
01234567   REFSET    TOTET SIGN_ETA(POS) MAGN_ETA(3 5 8) PHI(8) 1(30000)

    The first keyword is REFSET, the second keyword specify the type of
reference set as above defined (EMET for EM Et, HDVETO for HD Veto, TOTET
for TOT Et). These two keywords are part of the fixed format section of the
message.

    A sign of eta is  specified by the keyword  SIGN_ETA followed by a pair
of parenthesis including  the keyword POS to  specify positive etas, or NEG
to  specify  negative  etas, or  both POS  and NEG to  specify  a symmetric
pattern with respect to the z=0 plane. The specification of the sign of eta
may be omitted when both signs are to be treated identically. The keyword
SIGN_ETA must always be followed by a parenthesis.

    A set  of  magnitudes  of eta  is  specified  by the  keyword  MAGN_ETA
followed by a pair of  parenthesis including any  combination of individual
eta magnitudes and eta magnitude  ranges. A range is specified by its upper
and lower  bounds separated  by a colon (:).  It is  required for the lower
(respectively upper) bound to appear  before (respectively after) the colon
character.  When  two eta  magnitudes  are  separated by a  colon to form a
range,  they  are  understood  as  equivalent  to the  complete  set of all
integers  between and  including the upper  and lower  bounds. When two eta
magnitudes are not  separated by a colon  character and neither one is part
of the definition  of a range, then  the two numbers  are understood as two
more discrete values to be included in the set of magnitudes defined inside
the  parenthesis. A  pair of empty  parenthesis  has no  meaning and is not
allowed. The  specification  of the eta  magnitudes may be omitted when all
existing  magnitudes are to  be treated  identically. The  keyword MAGN_ETA
must always be followed by a parenthesis.

    A set of phi values is specified  by the keyword PHI followed by a pair
of parenthesis including any  combination of individual phi values  and phi
ranges. The syntax is identical to the one allowed for the magnitude of eta
defined  above. A  pair of  empty   parenthesis has  no  meaning and is not
allowed.  The   specification  of the  phi  values may  be omitted when all
existing phi values are to be treated identically. The keyword
PHI must always be followed by a parenthesis.

    The Reference Set and  the threshold value are  specified by the number
of the Reference Set (0..3) followed by a pair of parenthesis including the
energy  value  to be   programmed. The  energy  value to  be  programmed is
specified as an integer in units of MeV of z-corrected Transverse Energies.
The   Trigger  Control   Computer  will  perform  the   translation  to the
appropriate quantified value that will be inclusive of the specified value,
as defined in the beginning of this  section. A number not appearing within
parenthesis must always be followed by a parenthesis.

    COOR can release  a given  reference set by  specifying a pair of empty
parenthesis  directly after a  reference set  number. This  means that COOR
will stop using that reference set and all the associated global thresholds
which  thus may  (should) be  used by  D0TCC to  perform  the best possible
trigger integrity tests. COOR may start using it again at any time, it will
be  automatically   reinitialized as  soon as  COOR  mentions it again in a
message.

    Several subranges for the same reference set (or several reference sets
for the same subrange) may be defined within a single message with separate
threshold  values.

    Whenever  a  Reference  Set  specification  appears  in a  message, the
threshold value is applied to the specified Reference Set and to all of the
Trigger Towers specified in the part  of the message before that point (any
range specification  appearing after that point  in the message will not be
taken in consideration for that particular threshold).

    Whenever a  specification of a range of sign  of eta, magnitude of eta,
or phi type appears in a message, then any range specification of this type
appearing  before that  point in  the message  is  overridden with this new
range specification, but any previously defined range of any other type (or
default by omission) remains in effect.

    None of these commands accepts negative numbers.

    All unspecified reference sets are not modified.

    All unspecified Trigger Towers are not modified.

    This   setting is   independent  from  the   programming of  the global
thresholds acting on the total count carried over the whole detector of the
number of towers exceeding their individual references.

    g) Large Tile Threshold Reference Sets

    In addition to the Trigger Tower 4  EM and 4 Tot Et Threshold Reference
Sets and  Trigger Tower  Counts, the  Calorimeter Trigger  also makes Large
Tile (4 x 8 Trigger Tower in eta x  phi) Tot Et Energy signals and offers 8
Large  Tile   Threshold  Reference  Sets to   produce 8  Large  Tile Counts
(independent and  separate from the Trigger Tower  based Reference Sets and
Trigger Tower Counts).

    The Large Tile Reference Sets are specified with the same syntax as the
Trigger Tower  Reference Sets (cf.  paragraph 9.f for  details). This means
that no new indexing scheme is introduced for the Large Tiles.

01234567   REFSET LRG_TILE MAGN_ETA(1:8) 3(8000) MAGN_ETA(9:20) 3(10500) 

    There is however  one additional  syntax constraint  for the Large Tile
Reference Sets which do not apply to  the Trigger Tower Reference Sets. The
constraint is  that any  boundary used to  define a range  of Trigger Tower
Indices cannot cut accross the  coverage of a Large Tile, that is the range
specified  must cover an  integral  number of  Large Tiles.  The Large Tile
segmentation  in eta  magnitude is 1..4,  5..8, 9..12,  13..16, 17..20, and
1..8, 9..16,  17..24, 25..32 in phi.  

    If an   invalid  range is   specified TCC  will  return  a  "BAD PARAM"
acknowledgement message and take no action.

    Each of the 8 Large  Tile Counts built from  the 8 Large Tile Reference
Sets is compared to 3 fixed Large  Tile Count Thresholds, namely >=1 , >=2,
and >=3. There are thus no Large Tile Count Comparators for COOR to program
(and  no  message  defined  for  it).  COOR  includes  a  Large  Tile Count
requirement for a  Specific Trigger  Definition by  directly specifying the
Andor Term hardwired to the Large  Tile Fixed Count Threshold Comparator of
choice.

    h) examples of range specification

    SIGN_ETA ( POS NEG )  MAGN_ETA ( 1 : 20 ) PHI(1:32) 2(10500)

or  2(10.5)

    specifies a  uniform threshold for  Reference Set #2  of 10.5 GeV of Et
over all values of eta  within [-20,-1] and [1,20] and phi within [1,32]

    MAGN_ETA(1:16) 0(10000) 1(15000) MAGN_ETA(17:20) 0(5000)

    Specifies   a  pattern   uniform  in  sign eta  and  phi   (omission of
specification),  but with two steps  in threshold for  Reference Set #0 and
#1. For the  reference  set #0, the  thresholds  are 10 GeV  for eta within
[-16,-1]and[1,16], and 5 GeV within  [-20,-17]and[17,20]. The reference set
#1, is here only defined for eta  within [-16,-1]and[1,16] at 10 GeV. Other
previous or subsequent  messages might define the  rest of the detector for
reference set #1 or see default thresholds defined in a separate section.

    MAGN_ETA(1:17) 0(10000) MAGN_ETA(1:4) 1(5000)

    Reference set # 0 is defined over the ranges [-17,-1]and[1,17] in eta.
    Reference set # 1 is defined over the ranges [-4,-1]and[1,4] in eta.

    2()

    Releases the resource reference set #2 and all global thresholds made
on the global count that it generates (see global threshold messages below).


10. EXCLUDE ONE TRIGGER TOWER FROM ALL CONTRIBUTION:

             01234567  EXCLUDE  EMTOWER SIGN_ETA(NEG) MAGN_ETA(20) PHI(23)
             01234567  EXCLUDE  HDTOWER SIGN_ETA(NEG) MAGN_ETA(20) PHI(23)

    This gives a "quick fix" ability by forcing to zero the contribution of
some Trigger  Towers. The energy  deposited in the  excluded Trigger Towers
will quit contributing  to any Energy or Momentum  sum, to any Tower count,
and thus to any subsequent Trigger Decision.

    The  syntax  definition  to  specify  ranges or   individual indices of
Trigger  Towers  is  identical to  the one  allowed  in the  messages about
Reference Sets.

11.  LOAD GLOBAL THRESHOLD:

    None of these commands accepts negative numbers.

    All unspecified thresholds are not modified.

    All values are interpreted as inclusive. This means that the andor term
resulting  from the   comparison of a  global  count  against the specified
threshold will be asserted as soon as the value is equal to or greater than
the specified threshold.

    This setting is  independent from the  programming of the andor network
for each specific trigger. COOR will  know from its configuration files how
the outputs from all the comparisons map onto the 256 Andor Terms.

    COOR can release  a global  threshold resource by  specifying a pair of
empty  parenthesis.  This means  that COOR will  stop using  that threshold
which  thus may  (should) be  used by  D0TCC to  perform  the best possible
trigger integrity tests. COOR may start using it again at any time, it will
be  automatically   reinitialized as  soon as  COOR  mentions it again in a
message.

    A maximum of one value is allowed inside any pair of parenthesis for
these commands.

       a)  EM Et Threshold:

             01234567 THRESHLD  EMETSUM 0(24000) 3(29000)

    For the Global Electro-Magnetic  Transverse Energy Sum carried over the
whole detector, this command will program the Threshold having the identity
number specified in front of a pair  of parenthesis with the minimum energy
value  specified inside the  parenthesis.  The thresholds  are specified in
units of MeV of global EM Et.

    The identity  number is an  integer in  the range from  0 to 31. COOR's
configuration file will show the id of the thresholds actually implemented.

       b)  HD Et Threshold:

             01234567 THRESHLD  HDETSUM 1(24000) 3(29000)

    For the Global  Hadronic  Transverse Energy Sum  carried over the whole
detector,  this  command will  program  the  Threshold  having the identity
number specified in front of a pair  of parenthesis with the minimum energy
value  specified inside the  parenthesis.  The thresholds  are specified in
units of MeV of global HD Et.

    The identity  number is an  integer in  the range from  0 to 31. COOR's
configuration file will show the id of the thresholds actually implemented.

       c)  TOT Et Threshold:

             01234567 THRESHLD TOTETSUM 1(24000) 3(29000)

    For the Global Total (=Electro-Magnetic+Hadronic) Transverse Energy Sum
carried over the  whole detector,  this command will  program the Threshold
having the identity number specified in front of a pair of parenthesis with
the minimum energy value  specified inside the  parenthesis. The thresholds
are specified in units  of MeV of global TOT Et.

    The identity  number is an  integer in  the range from  0 to 31. COOR's
configuration file will show the id of the thresholds actually implemented.

       d) Second Energy Lookup Thresholds.

    A second lookup may be made after the first lookup of Et for the EM and
HD  channels. This  second lookup  could be the   reconstructed Energy (not
scaled to its transverse component)  or an other Et lookup with a different
choice  of   lookup  cuts.  This  second   lookup is  noted  L2 and similar
thresholds and messages exist for this second lookup.

             01234567 THRESHLD  EML2SUM 1(24000) 3(29000)
             01234567 THRESHLD  HDL2SUM 1(24000) 3(29000)
             01234567 THRESHLD TOTL2SUM 1(24000) 3(29000)

       e)  MISS-Pt-THRES:

             01234567 THRESHLD MISPTSUM 1(24000) 3(29000)

    For the Global Missing Transverse Energy Sum carried over the whole
detector,  this command will  program the Threshold having the identity
number specified in front of a pair of parenthesis with the minimum energy
value  specified inside the  parenthesis. The thresholds are specified in
units of MeV of global Missing Pt.

    The identity number is an integer in the range from 0 to 31. COOR's
configuration file will show which thresholds are actually implemented.

       f)  EM Et Trigger Tower Count:

             01234567 THRESHLD  EMETCNT REF(2) 2 (1) 3(2)

    For  the   Global   Count   (carried  over  the   whole   detector)  of
Electro-Magnetic  Trigger  Towers above the  EM Et  reference set specified
with the  number within  the pair  of   parenthesis  directly following the
keyword REF,  this  command will program the  Threshold having the identity
number specified in  front of a pair of  parenthesis with the minimum count
specified inside  the parenthesis.  The thresholds  are specified in direct
count of Trigger Towers.

    The identity  number is an  integer in  the range from  0 to 31. COOR's
configuration file will show the id of the thresholds actually implemented.

    No provision is made to be able to  address Multiple Reference Sets  in
one message.

       g)  Total Et Trigger Tower Count:

             01234567 THRESHLD TOTETCNT REF(2) 2 (1) 3(2)

    For  the  Global Count   (carried over  the  whole  detector)  of Total
(Electro-Magnetic+Hadronic)  Trigger  Towers above the TOT Et reference set
specified with the number within the pair of parenthesis directly following
the  keyword  REF, this   command will  program  the  Threshold  having the
identity  number   specified in  front of a  pair of   parenthesis with the
minimum   count  specified  inside  the   parenthesis.  The  thresholds are
specified in direct count of Trigger Towers.

    The identity  number is an  integer in  the range from  0 to 31. COOR's
configuration file will show the id of the thresholds actually implemented.

    No provision is made to be able to  address Multiple Reference Sets  in
one message.


12.  SPECIFIC TRIGGERS VERSUS REFERENCE SETS IN LEVEL 1 JET LIST TO LEVEL 2

    The Level 1 Trigger system provides a "Jet List" for use by the Level 2.
A Level 2 Node will use the Trigger Towers in the Jet List(s) as seeds to
electron or jet finding algorithms.

    The Level 1 builds the lists by finding the Trigger Towers that
exceeded at least one of the Reference Sets.  There is one EM Et Jet list
including the contribution of all four EM Et (and associated HD Veto)
Reference Sets. And one TOT Et Jet List made from the four TOT Et
Reference Sets.

    Since four Reference Sets are merged in a list, the Level 2 needs to
know which towers in the list contributed to which Specific Trigger. Each
entry in the list is thus tagged with a 32 bit mask of Specific Triggers
(see D0 Note #967 for more details).

    The Level 1 will keep a set of eight Primary Masks (one per Reference
Set) specifying which Specific Triggers "USE" which Reference Set. The
messages described in this paragraph let COOR program the content of these
Primary Masks.

    "USING" a particular Reference Set is currently defined as (D0 note #967):

    The programming of the Specific Trigger requires at least 1 comparison
(either greater than or less than) on the number of Trigger Towers found
above the Reference Set (see D0 Note #967 for more details).

    The Level 1 will build an Entry Mask for each Trigger Tower found above
at least one of the Reference Sets.  The corresponding bit will be set high
in the Entry Mask for every Specific Trigger that met the two conditions
below:
         1) The Specific Trigger was "USING" at least one of the Reference
            Sets that the Trigger Tower passed (as specified by the
            Reference Set Primary Masks)
     and 2) The Specific Trigger fired for the current event.

    Note that before a Trigger Tower can become an entry in the Jet List its
entry mask must have at least one bit set. There are no duplicate entries.


       a)  EM Et Jet List

             01234567 ST_VS_RS  EM_LIST 0 ( 1 3 5 ) 2(1 4 6)

    The Specific Triggers specified inside the parenthesis will be
recognized as using the EM Et (and/or associated HD Veto) Reference set
specified by the number in front of the parenthesis. The bits
corresponding to the specified Specific Triggers will be set in the
corresponding Reference Set Primary Mask.

    Inside each set of parenthesis, all unspecified Specific Triggers are
recognized as not using the corresponding EM Et Reference Set. The bits
corresponding to the unspecified Specific Triggers will be cleared from the
corresponding Reference Set Primary Mask.

    All unspecified EM Et Reference Set Primary Masks are not modified.

    note: in order to remove one Specific Trigger from a Reference Set
Primary Mask it is necessary to re-specify the complete list, omiting the
Specific Trigger to remove.

       b)  TOT Et Jet List

             01234567 ST_VS_RS TOT_LIST 0 ( 1 3 5 ) 2(1 4 6)

    The Specific Triggers specified inside the parenthesis will be
recognized as using the TOT Et Reference set specified by the number in
front of the parenthesis. The bits corresponding to the specified Specific
Triggers will be set in the corresponding Reference Set Primary Mask.

    In each set of parenthesis, all unspecified Specific Triggers are
recognized as not using the corresponding TOT Et Reference Set. The bits
corresponding to the unspecified Specific Triggers will be cleared from the
corresponding Reference Set Primary Mask.

    All unspecified TOT Et Reference Set Primary Masks are not modified.

    Note: in order to remove one Specific Trigger from a Reference Set
Primary Mask it is necessary to re-specify the complete list, omiting the
Specific Trigger to remove.

       c)  Large Tile Jet List 

    The Large Tile extension to the Calorimeter Trigger can produce
Jet Lists in the same definition and format as the Trigger Tower EM Et or
TOT Et Jet Lists. The message described here will specify the Specific
Trigger usage of Large Tile Reference Sets and will provide the necessary
information for building these Large Tile Jet Lists.

             01234567 ST_VS_RS LRG_TILE 0 ( 1 3 5 ) 2(1 4 6)

    The Specific Triggers specified inside the parenthesis will be
recognized as using the Large Tile Reference set specified by the number in
front of the parenthesis. The bits corresponding to the specified Specific
Triggers will be set in the corresponding Reference Set Primary Mask.

    In each set of parenthesis, all unspecified Specific Triggers are
recognized as not using the corresponding Large Tile Reference Set. The bits
corresponding to the unspecified Specific Triggers will be cleared from the
corresponding Reference Set Primary Mask.

    All unspecified Large Tile Reference Set Primary Masks are not
modified.

    note: in order to remove one Specific Trigger from a Reference Set
Primary Mask it is necessary to re-specify the complete list, omiting the
Specific Trigger to remove.


13.  LEVEL 1.5 CALORIMETER TRIGGER PROGRAMMING

       a) Definitions

    The messages necessary to program the Level 1.5 Calorimeter Trigger are
devided in two classes, reflected by two separate message types:
        L1.5 CT Term requirement and programming (L15CTERM messages)
        L1.5 CT system and program control (L15CTSYS messages)

    The L1.5 Cal Trig Term contributes to the overall Level 1 and 1.5
Triggering System in the form of Level 1.5 Trigger Terms.  Each Crate of
L1.5 Calorimeter Trigger can provide up to 8 Level 1.5 Terms to the Level 1.5
Trigger Framework.  

    The requirements programmed for each L1.5 CT Term can be classified in 
four categories, reflected as four separate message subtypes.  Each one 
is further described in the operation summary below.
    Reference set for selection of Trigger Tower Candidates
    Local DSP Tool and parameter selection
    Global DSP Tool and parameter selection
    Frame Code services

    The syntax and definition are made here to allow the full flexibility of
8 independent L1.5 CT Term per L1.5 CT Crate, each having independent
Reference sets, Local and Global DSP Tools (i.e. algorithms) and
parameters.  In contrast, it is important to note that the initial
implementation of the L1.5 CT system will only allow a single L1.5 CT Term
with a fixed Local and Global Algorithm, with variable parameters.

    In each message, a particular Level 1.5 CT Term is specified by its 
L1.5 CT Crate Number, and its relative Term number in the crate.  The
first crate that will be implemented will be crate number 0.  A second crate
might be added to the system in the future, and would become crate number 1. 

    The particular term in the crate is identified by its relative number
in the crate with a number from 0 to 7.  Note that this L1.5 CT number is
most likely NOT the same as the Level 1.5 Framework Term number that will
receive the L1.5 CT Answer from this L1.5 CT Term.  COOR will need a table to
describe the correspondence between L1.5 CT Crate and Term Numbers and
which Level 1.5 Framework Term number they are connected to.

    Understanding the details of the messages described below requires 
some understanding of the operation and the structure of the Level
1.5 Calorimeter Trigger. 

    One way to summarise the work of the Level 1.5 Calorimeter is as a
Level 1.5 Trigger Subsystem that can confirm (or reject) one or more
Candidate Trigger Towers as a valid electron signal.  Note that the same
L1.5 Cal Trig (or a second crate) can also be used to work on confirming or
rejecting jet candidates.  The system structure also allows more complex
requirements to be made on the list of confirmed objects.  The system has
been designed with enough flexibility to allow these different options
without hardware modifications.

    When a beam crossing requires a Level 1.5 computation, the energy of 
all Trigger Towers is sent to the Level 1.5 CT.  The Transverse EM
Energy and the Tot (=EM+HAD) Transverse Energy of each Trigger Tower are
sent to the L1.5 CT.  

    The first task of the L1.5 CT is to identify the list of Trigger Towers
that are candidates for each L1.5 CT Term.  There is one independent such list
for each of the L1.5 CT Terms.  The Candidate Trigger Towers are identified
by applying a Reference Set to the energy of each Trigger Tower.  This can
be done to the EM or TOT enery depending on the type of object sought.
The energies in each Reference Set can be set uniformly over the whole
detector, but can also be arbitrarily specified differently for any subset of
Trigger Towers.  Note also that these L1.5 CalTrig Reference Sets are
independent from the L1 CalTrig Reference Sets, even though a logical
programming for a L1.5 CT Ref Set will duplicate the L1 CT Ref Set that was
used to select the event sent to the L1.5 CT.

    The second task of the L1.5 CT is to submit the candidates for each
L1.5 CT Term to the Tool algorithm and Parameters chosen for the L1.5 CT
Term.  This part of the L1.5 CT computation is called the Local Algorithm
and is executed by the Local DSP's.  Each of the 11 Local DSP's only
receives enough Trigger Tower Energy information to process the Trigger
Towers that it is responsible for.  The algorithm is designed to look in
the energy deposited in the candidate tower and its neighbors to recognize
the type of object sought (electrons or jets) and accept or reject the
candidate as a legitimate signal.  The Candidate Trigger Towers that
satisfy a L1.5 CT Term Local DSP Tool are then called Confirmed Objects.

    The third task of the L1.5 CT is to collect all the Confirmed Objects
and form a final answer for each L1.5 CT Term.   This part of the L1.5 CT
computation is called the Global Algorithm and is executed by the Global
DSP.  The Global DSP is the only processor that collects information 
covering the whole detector.  It only gets the list of confirmed objects
from the Local DSP's, and does not have access to the Trigger Tower
Energies. The trivial case for a Global Algorithm is to simply verify that
at least one of the candidates has survived to become a Confirmed Object. 

    The last task of the L1.5 CT in this summarized view is performed by
the Frame Code  and allows overriding a L1.5 CT Term Answer for a variable
fraction of the events.  This mechanism forces a positive answer for one of
every n events, and thus provides a monitoring sample of events (that would
have otherwise been rejected) to be passed to the acquisition system.  Note
that the  L1.5 CT cannot really force an event to be accepted.  It is the
Level 1.5 Framework that makes the final decision.  This decision might
include a contribution from other Level 1.5 Trigger Subsystems (e.g. L1.5
muon Trigger) that could reject the event.  When a pass_one_of_n counter
rolls over for any of the L1.5 CT Terms, all L1.5 CT Term Answers are
forced high for that event in order to increase the chances of passing the
event.

       b) L1.5 Cal Trig Term Reference Sets

01234567 L15CTERM   REFSET CRATE(0) TERM(2) TYPE(EM) SIGN_ETA(POS NEG) 
MAGN_ETA(1:20) PHI(1:32) THRESH(10000)

    This message specifies the Reference Set (or a portion of it) that
needs to be associated with a particular L1.5 CT Term.  The L1.5 CT Term is
identified by its crate ID specified as an integer (0 or 1) inside the
pair of parenthesis following the keyword "CRATE".  The L1.5 CT Term is
further identified by the relative term number within the crate specified
as an integer (from 0 to 7) inside the pair of parenthesis following the
keyword "TERM".

    The reference Set must be further described by its type "EM" or "TOT"
specified inside the pair of parenthesis following the keyword "TYPE".  This
type is used to select whether the reference set energies must be applied
to the EM Et or Tot Et Trigger Tower Energies. 

    The set of Trigger Towers for which this message programs the reference
energy is specified using the same syntax as for the Level 1 Trigger Tower 
Reference Set messagess (cf.  paragraph 9.f for  details).  It might take
more than one such message to describe a non uniform reference set.  When
several such messages are needed to describe the full Reference Set for one
L1.5 CT Term, the reference set type must agree in all the messages.

    The energy value to be programmed is specified inside the pair of
parenthesis following the keyword "THRESH".  It is specified as an integer
in units of MeV of z-corrected Transverse Energies.  The Trigger Control
Computer will perform the translation to the appropriate quantified value
that will be inclusive of the specified value.

    A given message can only refer to one and only one L1.5 CT Term.  The
keywords CRATE, TERM and TYPE, and their values must all be present, and in
this order, in each message.  They  must appear first, and before the
Trigger Tower Range and Threshold value.  More than one Trigger Tower Range
and corresponding Threshold can be specified in a single message (like for
the Level 1 Trigger Tower Reference Set messages), in which case the CRATE,
TERM and TYPE are not repeated.  

    This message only causes TCC to translate and re-format the specified
information.  TCC also loads it in dual port VME memories accessible to the
L1.5 CT Processors.  The acknowledgment message returned by TCC to COOR
for this message only testifies to the success of understanding the
request, and to the success of writing the dual-ported VME memory in the
L1.5 CT Crate.  In particular, the L1.5 CT is still idle at this time, and
does not try accessing or using this data until the START message defined
in 13.g below.

       c) L1.5 Cal Trig Term Local DSP Tool Definition

01234567 L15CTERM  LOC_DSP CRATE(0) TERM(2) USE_TOOL(657) WITH_PARAMS(1 2.00)

    This message specifies which Local DSP Tool algorithm needs to be
associated with a particular L1.5 CT Term and which set of parameters need
to be used with the Local algorithm for this L1.5 CT Term.  The L1.5 CT Term
is identified by its crate ID specified as an integer (0 or 1) inside the
pair of parenthesis following the keyword "CRATE".  The L1.5 CT Term is
further identified by the relative term number within the crate specified
as an integer (from 0 to 7) inside the pair of parenthesis following the
keyword "TERM".

    The Tool is identified by its unique Tool ID specified as an integer
inside the pair of parenthesis following the keyword "USE_TOOL".  The list
of parameters needed by the Tool to operate is specified inside the pair of
parenthesis following the keyword "WITH_PARAMS".  The same Tool ID may be
used for more than one L1.5 CT Term.  There is only one Tool allowed per
L1.5 CT Term.

    Parameter definitions are Tool dependent.  Different Tools might have a
different number and type of parameters.  The exact number and type of
parameters that are  defined for a tool must all be given a value.  There is
no provision for default values.  Successive parameters are separated by 
one or more blank character (space).  The only 2 types of parameter allowed
are integer and real numbers.  TCC will perform the binary translation to
integer or real format appropriate to the DSP architecture, but TCC has no
knowledge of which parameter should be integer or real numbers.  Thus a real
number must always include a decimal point to denote its type, even if the
real number value needs no decimal digits (i.e. "2.0" is preferred, but
"2." is ok, while "2" is not appropriate for a parameter of type real). 
Integer or real numbers may take negative values.  There may or may not be 
one or more blank characters separating the negative sign ("-") from the
aboslute value.  Real numbers cannot use the exponential form and must all
be expressed using only the characters "0" through "9", "." and "-".

    A given message can only refer to one and only one L1.5 CT Term.  The
keywords CRATE, TERM, and USE_TOOL, and their values must all be present,
and in this order, in each message.  They  must appear first, and before the
list of parameters.

    This message only causes TCC to translate and re-format the specified
information.  TCC also loads it in dual port VME memories accessible to the
L1.5 CT Processors.  The acknowledgment message returned by TCC to COOR
for this message only testifies to the success of understanding the
request, and to the success of writing the dual-ported VME memory in the
L1.5 CT Crate.  In particular, the L1.5 CT is still idle at this time, and
does not try accessing or using this data until the START message defined
in 13.g below.

       d) L1.5 Cal Trig Term Global DSP Tool Definition

01234567 L15CTERM GLOB_DSP CRATE(0) TERM(2) USE_TOOL(645) WITH_PARAMS(5 6.00)

    This message specifies which Global DSP Tool algorithm needs to be
associated with a particular L1.5 CT Term and which set of parameters need
to be used with the Global algorithm for this L1.5 CT Term. 

    The message syntax and parameter constraints are exactly the same as
for the Local DSP Tool Definition (cf. paragraph 13.c)


       e) L1.5 Cal Trig Term Frame Code Parameters 

01234567 L15CTERM FRAMECOD CRATE(0) TERM(2) PASS_ONE_OF(300) 

    This message specifies the Frame Code requirements  that need to be
associated with a particular L1.5 CT Term.  The L1.5 CT Term is identified
by its crate ID specified as an integer (0 or 1) inside the pair of
parenthesis following the keyword "CRATE".  The L1.5 CT Term is further
identified by the relative term number within the crate specified as an
integer (from 0 to 7) inside the pair of parenthesis following the keyword
"TERM".

    The mark and pass ratio is specified as an integer (greater than or
equal to 1) inside the pair of parenthesis following the keyword
"PASS_ONE_OF".  The L1.5 CT will keep updating a counter for each event that
required the computation of this L1.5 CT Term.  There is one separate
counter per L1.5 CT Term.  When any of the pass_one_of_n counters
reaches its defined value, all L1.5 CT Term Answers are forced high for
that event (in order to maximize the chances of passing the event).

    A given message can only refer to one and only one L1.5 CT Term. 
The keywords CRATE, and TERM, and their values must all be present, and in
this order, in each message.  They must appear first, and before the pass
one of n requirement.

    This message only causes TCC to translate and re-format the specified
information.  TCC also loads it in dual port VME memories accessible to the
L1.5 CT Processors.  The acknowledgment message returned by TCC to COOR
for this message only testifies to the success of understanding the
request, and to the success of writing the dual-ported VME memory in the
L1.5 CT Crate.  In particular, the L1.5 CT is still idle at this time, and
does not try accessing or using this data until the START message defined
in 13.g below.

       f) Specific Trigger versus L1.5 Cal Trig Term

01234567 L15CTERM ST_VS_TM CRATE(0) TERM(2) SPTRG(1 2 5 14)

    This message specifies the set of Specific Triggers that require the
computation of a particular L1.5 CT Term.   The L1.5 CT Crate will use this
information to determine which (if any) of its L1.5 CT Terms need
computation when a particular set of L1.5 Specific Trigger fired.  The L1.5
CT Term is identified by its crate ID specified as an integer (0 or 1)
inside the pair of parenthesis following the keyword "CRATE".  The L1.5 CT
Term is further identified by the relative term number within the crate
specified as an integer (from 0 to 7) inside the pair of parenthesis
following the keyword "TERM".

    When more than one L1.5 CT Terms are defined, the L1.5 CT Crate will
combine all the corresponding lists to find out if any of its L1.5 CT Terms
are needed, and decide which one(s) need evaluation.  A given Specific
Trigger may appear in lists for more than one L1.5 CT Term.

    The list of Specific Triggers is specified inside the pair of
parenthesis following the keyword "SPTRG".  One or more Specific Trigger may
be specified, each separated by one or more blank character (space).
All unspecified Specific Triggers cannot cause the specified L1.5 CT Term
to be evaluated.  This command does not accept negative numbers.

    A given message can only refer to one and only one L1.5 CT Term.  The
keywords, and their values, must all be present in each message.  The
keywords CRATE, and TERM, and their values must all be present, and in this
order, in each message.  They  must appear first, and before the list of
Specific Triggers.

    This message only causes TCC to translate and re-format the specified
information.  TCC also loads it in dual port VME memories accessible to the
L1.5 CT Processors.  The acknowledgment message returned by TCC to COOR
for this message only testifies to the success of understanding the
request, and to the success of writing the dual-ported VME memory in the
L1.5 CT Crate.  In particular, the L1.5 CT is still idle at this time, and
does not try accessing or using this data until the START message defined
in 13.g below.

       g) Start L1.5 Cal Trig System 

01234567 L15CTSYS    START CRATE(0) 

    The programming of the L1.5 CT system cannot be modified once the
system is running.  The proper sequence of events is for COOR to load the
L1.5 CT executable (cf. message below).  Then COOR can define all the L1.5 CT
Terms with their reference sets, tools and parameters.  TCC prepares the
data and requirements passed by COOR and loads the DSP and 68k memory.
During this time the L1.5 CT is waiting, and the L1 framework should be
PAUSEd.  COOR must use this message to ask the L1.5 CT to read and
check all the  parameters loaded by TCC and report on the success of this
initialization.   The actions taken by the L1.5 CT at this time are defined
in detail in other documents, but this phase, initiated by this START
message from COOR, includes verifying the existence of the requested Tools,
and making the Tools verify that the parameters passed for each L1.5 CT
Term are consistent with each corresponding Tool.  If this phase was
successful, the L1.5 CT Crate is now ready for the first event.

    Whenever the programming needs to be modified, COOR needs to start by
reloadingthe code (cf. message below), then define all the L1.5 CT Terms
again, and restart the crate.  This is still true when one L1.5 CT Term
was defined and the crate was started, and COOR needs to add the
definitions for another Term.

    This message only affects one L1.5 CT Crate at a time specified as an
integer (0 or 1) inside the pair of parenthesis following the keyword
"CRATE".  A given message can only refer to one L1.5 CT Crate. 


       h) Load L1.5 Cal Trig executables 

01234567 L15CTSYS LOADCODE CRATE(0) host_directory_name

    This message asks TCC to reload the executables of all Local DSP's,
Global DSP and 68k Engine Control code.  The files follow some fixed naming
convention to be defined later (but internal to TCC and L1.5 CT system).
COOR only needs to specify the directory where TCC will find the various
files.  The directory must be a valid directory name, and reside on the D0
cluster.  Logical names may be used, as long as they are defined system-wide
on the D0 cluster.

    This message only affects one L1.5 CT Crate at a time specified as an
integer (0 or 1) inside the pair of parenthesis following the keyword
"CRATE".  A given message can only refer to one L1.5 CT Crate.