LEVEL 1 SIMULATOR USER'S GUIDE                                3-DEC-1992 
==============================

I. INTRODUCTION
II. PROGRAM_BUILDER, D0USER, CALOR_OFF
III. BUILDING L1SIM
    III.1 REQUIREMENTS
    III.2 GENERATING D0USER CODE
    III.3 GENERATING THE L1SIM EXECUTABLE
IV. REQUIREMENTS PRIOR TO RUNNING L1SIM
V. RUNNING L1SIM
    V.1 DEFINING SYMBOLS AND LOGICALS
    V.2 OUTPUT EVENT FILE
    V.3 EVENT PROCESSING OPTIONS
    V.4 PROCESSING EVENTS
VI. SUMMARY FILE OUTPUT
VII. CHANGING PARAMETERS IN THE RCP FILE
VIII. SPECIFIC TRIGGER PRESCALING 
IX. DISABLING ENERGY LOOKUP Z-CORRECTION 
X. LEVEL 1.5
XI. MINIMUM-BIAS TRIGGERS
XII. GENERATING DUMPS OF TRGR BANKS
XIII. LOOKUP SYSTEM MANAGER
    XIII.1 NOISE
    XIII.2 DESIGN CHOICES
XIV. BLS GAIN CORRECTION
XV. FORCING THE STATE OF UNSIMULATED ANDOR TERMS
XVI. TRIGGER TOWER ENERGY SATURATION
XVII. ADDING ON TO L1SIM

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

I. INTRODUCTION
===============

    L1SIM is a program package that simulates the Level 1 Trigger System, and
performs the same computations offline using computer generated or real
ZEBRA event files as input. 

    L1SIM simulates the following Trigger Subsystems:

o   the Level 1 Calorimeter Trigger 
o   the Level 1 Muon Trigger 
o   the Level 1 Decision
o   the Level 1.5 Muon Trigger 
o   the Level 1.5 Decision 

    The Triggering requirements are programmed into the simulator using the
same set of directives COOR would give the Trigger Control Computer (TCC)
or Muon Trigger. COOR_sim allows the L1SIM user to create this set of
directives from his own desired configuration.

    As output L1SIM generates the simulated trigger decision and TRGR banks
which may be added to the output ZEBRA event file. 


II. PROGRAM_BUILDER, D0USER, CALOR_OFF
======================================

    L1SIM is not distributed as a standalone program, but as a library and
Program Builder Description file. It is necessary to use the
PROGRAM_BUILDER program to generate more source code and link files, and
then to actually link L1SIM prior to running it. 

    Either the D0USER or CALOR_OFF framework of the Program Builder can be
used by L1SIM. D0USER is an interactive framework allowing the user to
modify the default option at run time providing much of the interactive
user interface through COMPACK menus. The CALOR_OFF framework is not
interactive and thus more appropriate for batch jobs.  

    The rest of this document describes L1SIM in the D0USER framework. To
build an executable using the CALOR_OFF framework, follow the 
procedure described below, substituting CALOR_OFF for D0USER in the
instructions contained in this manual. Refer to the CALOR_OFF documentation
for details on running the program. 


III. BUILDING L1SIM
===================

    III.1 REQUIREMENTS
    ------------------

    Your node must have subscribed to the following products to allow
creation and support use of the L1SIM executable:

o   PBD: The Program Builder Description Files 
        including D0$PBD:L1SIM.PBD, D0USER_FRAME.PBD, CALOR_OFF_FRAME.PBD
   
o   PROGRAM_BUILDER: The D0 Program Builder Product 
        including D0$PROGRAM_BUILDER:PROGRAM_BUILDER.EXE
   
o   LEVEL1: The LEVEL1 library                 
        including D0$LEVEL1:LEVEL1.OLB, L1SIM.RCP, and other data files

o   CONFIGS: The Trigger Configuration file library                 
        including D0$CONFIGS$COOR_SIM:COOR_SIM.EXE, and other data files 

o   CALOR_OFF: The calorimeter offline library 
        including D0$CALOR_OFF:CAHITS.RCP and CALOR_OFF.OLB

    If some of these products are missing on your node, contact your 
local D0 Librarian or use a machine on one of the D0 clusters to build your
executable.


    III.2 GENERATING D0USER CODE
    ----------------------------

    Before creating the executable, Program Builder must first create the
necessary additional source code and link files. The following DCL command
will perform this task:

$ PBD/FRAME=D0USER/PACKAGE=L1SIM/ZEBCOM=1000000/ZEBSTP=1000000/PAWC=250000


    III.3 GENERATING THE L1SIM EXECUTABLE
    -------------------------------------

    The executable may then be linked with the command:

$ @L1SIM_D0USER.LNK

    This will produce an executable named L1SIM_D0USER.EXE.

    For more details, or directives to produce a debuggable version of the
program refer to D0$PROGRAM_BUILDER:PROGRAM_BUILDER.MEM
    

IV. REQUIREMENTS PRIOR TO RUNNING L1SIM
=======================================

    Several files must exist before L1SIM can be run:

o   L1SIM.RCP, the parameter file which defines the control parameters and
    the names of the other configuration files. This file is accessed by 
    the logical name L1SIM_RCP. By default L1SIM_D0USER.COM points to the
    distributed D0$LEVEL1:L1SIM.RCP. The parameters in this file point to
    other distributed configuration files. 

o   A COOR Message file, which is a list of commands COOR would send to
    the TCC node for the desired configuration. This file is generated from
    a set of Resource files and Trigger Definition files by the program
    COOR_sim. COOR_sim is distributed in D0$CONFIGS$COOR_SIM: as an
    executable image for VMS V5.x. It is not recommended to modify in any
    way the files produced by COOR_sim.   

    The syntax used in the TRIGGER.INFO message files is defined in the
    file D0$LEVEL1:COOR_TCC_MESSAGES.DOC.

    The default D0$LEVEL1:L1SIM.RCP uses the file
    D0$LEVEL1$DATA:EXAMPLE_TRIGGER.INFO which is an example of COOR message
    file corresponding to a very simple configuration.

    One can also build a COOR message file from a custom set of Trigger
    Definition files using COOR_SIM. The COOR Message file generated
    typically has the name TRIGGER.INFO. Note that when the actual Level 1
    Trigger is operating, the file corresponding to the current Level 1
    Trigger configuration can be found as
    D0::ONLINE:[COOR_EXEC]TRIGGER.INFO. Standard configurations are also
    included in D0$CONFIGS$COOR_SIM: For instructions on using COOR_SIM and
    how to create a Trigger Definition file, see the document
    D0$CONFIGS$COOR_SIM:COOR_SIM.DOC.

o   The Level 1 Trigger Resource file, an RCP file which defines the
    sources of the hardware Andor Terms. This file will also be created by
    COOR_sim. The resource file created by COOR_sim typically has the name
    TRIGGER.RES. Note that when the actual Level 1 Trigger is operating,
    the resource file corresponding to the current hardware can be found as
    D0::ONLINE:[COOR_EXEC]TRIGGER.RES.
    ****** note *******
    The default D0$LEVEL1$DATA:TRIGGER_RESOURCES.RCP is provided and 
    matches the official trigger configuration in the COOR input file
    D0$CONFIGS$SOURCE:TRIG_RESOURCES.CTL.  

o   The Lookup System Manager object file. The default points to the file
    D0$LEVEL1$DATA:CALORIMETER_TRIGGER.LSO, which is the official
    description of the Level 1 Lookup hardware. Other special files for
    limited coverage are also distributed in D0$LEVEL1$DATA. For more
    details, see the section LOOKUP SYSTEM MANAGER below. 

o   A BLS Gain Correction file, necessary only if the BLS Gain Correction
    factor is to be used in the current simulator run. The default does not
    use BLS gain correction. For more information, see the section BLS
    GAIN CORRECTION below. 

o   A ZEBRA event file input to D0USER and L1SIM. L1SIM uses either the
    CAEP bank or the CAD banks of each ZEBRA event to reconstruct the
    Calorimeter Trigger Tower Energy deposit. The additional option
    is available to use an existing TRGR bank as input. At least one of
    these banks must exist in an input event for L1SIM to be able to
    generate a TRGR bank.  

    CAEP banks and CAD banks are not equivalent even though they both
    contain information on the energy deposited in the Calorimeter. A CAEP
    bank is generated from CAD banks, but the energy deposits may have been
    subjected to a low energy cut, typically 0.1 GeV. As this cut is not
    performed on the data the Level 1 hardware receives, it is more
    accurate to run L1SIM on events containing CAD1 and CAD2 banks rather
    than on events containing CAEP banks.

    Gain corrections are applied to CAD bank data using routines from
    CALOR_OFF.  If the simulator is being run on real events, these gains
    will be retrieved from the DBL3 database.  To inhibit this correction, 
    set DO_GNSCOR to FALSE in your private copy of D0$CALOR_OFF:CAHITS.RCP
    or in a private RCP file with a CAHITS_RCPE bank (and logical name).

    ****** note *******
    L1SIM does not create a CAEP bank from CAD banks. L1SIM reads the
    information from the CAD banks using the routine CDTUPK and corrects
    for sampling fraction using the routine CGEV_GAIN initialized by
    CALOR_INI and CHTINI.  
    ****** note *******
    When the option is selected to read from TRGR banks, the Level 0 Fast
    Vertex is also read from the TRGR bank.

V. RUNNING L1SIM
================

    V.1 DEFINING SYMBOLS AND LOGICALS
    ---------------------------------

    Before running L1SIM, the command file L1SIM_D0USER.COM must be run.

$ @L1SIM_D0USER

This will define necessary symbols and logicals. L1SIM can then be run
with the command $ D0USER.

    V.2 EVENT PROCESSING OPTIONS
    ----------------------------

    Once running L1SIM, several options can be changed from their defaults
by selection the menu item "User Dialog" from the D0USER main menu:

o   Input Bank. L1SIM can read Calorimeter Trigger Tower Input Energy from
    either an existing TRGR bank, raw data CAD1/CAD2 banks, or CAEP banks.
    The option 'TRGR' uses an existing TRGR bank. Noise may not be added,
                      Level 0 Vertex is extracted from TRGR bank (NOT from 
                      ISAJET), or Level 0 Vertex may also be ignored.
    The option 'ANY'  implies a search order of TRGR, CAD, CAEP.
    The option 'NONE' will skip reading any bank, no input is applied to
                      the Calorimeter Trigger Simulator. The Cal Trigger
                      Tower Energies are not simulated No specific trigger
                      requiring calorimeter energy can fire. 


o   Trigger Tower Noise, if enabled, adds Gaussian noise to the energy
    deposited in each Trigger Tower. See the section NOISE below for
    more information. The default is to add noise.
    ****** note *******
    The Calorimeter Trigger and the Calorimeter Acquisition are not exposed
    to the same amount of noise. The feature described here is not
    equivalent to using Monte-Carlo events with noise introduced during 
    event generation. 

o   Level 0 Vertex. The Calorimeter Trigger normally uses the Level 0 Fast
    Vertex Information to select a Level 1 Lookup Page. This Lookup is used
    to correct the transverse energies. (cf. section on Lookup System
    Manager). L1SIM offers the option to ignore the Level 0 Information.
    This option forces the Level 1 to act as if the vertex is at z=0, 
    and always select the Center Level 1 Lookup Page.
    ****** note *******
    The Level 0 Fast Vertex Information is simulated by L1SIM after finding
    the vertex position from Isajet. L1SIM uses a simplistic geometric
    segmentation of the z-axis into Level 0 Bins.

o   Fast Trigger Simulation is a mode where the simulator runs faster but
    does not produce TRGR banks. The same information in the summary file
    is still produced. The amount of information in the dump files is
    reduced. The default is full simulation.

o   Prescaling Ratios may be applied to the Specific Triggers. This switch
    globally enables or disables the use of prescaling. See the section
    SPECIFIC TRIGGER PRESCALING below for more information. The default is
    no prescaler.

o   BLS Gain Correction can be applied to the energy deposits from the
    input events. See the section BLS GAIN CORRECTION below for more
    information. The default is no BLS gain correction.

o   Calorimeter Trigger and Framework programming information can be added
    to the standard summary file. The default is to have the programming
    information in the summary.

o   A Level 1.5 confirmation can be be produced for all events with one or
    more Level 1.5 Specific Triggers meeting their Level 1 Requirements.
    For more information see the section LEVEL 1.5 below. Note that this
    mode does NOT correspond to hardware operation.

    V.3 OUTPUT EVENT FILE
    ---------------------

    An output event file containing TRGR banks can be written by selecting
the option "Output Data Files" from the D0USER main menu. The default is to
write no event file.

    V.4 PROCESSING EVENTS
    ---------------------

    Once the user has changed any desired options, the menu item "Auto
Process" can be selected to begin processing events. The following are
example answers to the questions prompted for.

  Will you be reading files from tape? [N]> N

  Name of input file > FNALD0::MC_DATA$HROOT:[SAMPLE]K_18001_01.GEN

  Is input file in exchange mode? [N]:> N  (Typically, event files will not
                                            be in exchange mode)

  Store histograms ? 0=NO, 1=after each run, 2=end of job only > 0


VI. SUMMARY FILE OUTPUT
=======================

    At the end of each run L1SIM writes a summary file containing
histograms, Specific Trigger firing statistics, a listing of run control
parameters as read from L1SIM.RCP and L1SIM_RCPE and the User Dialog menu
option, and a listing of the programming information used in configuring
the simulator as read from the COOR message file and the resource file.
This file is named D0USER_(run #).OUT. The programming information listing
can be enabled and disabled by changing the parameter
PROGRAMMING_LISTING_DEFAULT using the file L1SIM.RCP or L1SIM_RCPE.

    The following HBOOK histograms are written to the summary file:

o //PAWC/L1SIM 1000 = Specific Trigger Hits.
o //PAWC/L1SIM 1001 = Weighted Specific Trigger Hits.
o //PAWC/L1SIM 1005 = Level 1.5 Specific Triggers submitted to Level 1.5.
o //PAWC/L1SIM 1011 = Count of Trigger Towers with EM energy deposit
o //PAWC/L1SIM 1012 = Count of Trigger Towers with HD energy deposit
o //PAWC/L1SIM 1013 = Count of Trigger Towers with TOT energy deposit
o //PAWC/L1SIM 1021 = Sum of EM Trigger Tower energy in GeV.
o //PAWC/L1SIM 1022 = Sum of HD Trigger Tower energy in GeV.
o //PAWC/L1SIM 1023 = Sum of TOT Trigger Tower energy in GeV.
o //PAWC/L1SIM 2001 = 2D Histogram of the sum of EM Trigger Tower energy 
                         vs. the sum of HD Trigger Tower energy. 
                         This energy is also given in GeV.


VII. CHANGING PARAMETERS IN THE RCP FILE
========================================

    In order to run L1SIM with your own trigger configuration, it is
necessary to follow one of two approaches to change parameters in the
default D0$LEVEL1:L1SIM.RCP. One approach is to use a private copy of 
D0$LEVEL1:L1SIM.RCP in a local directory. This requires redefining the
logical L1SIM_RCP, originally defined by L1SIM_D0USER.COM, to point to the
new file.

    A better approach is to use an RCP edit file in addition to the default 
D0$LEVEL1:L1SIM.RCP.  Create a file in your local directory containing the
following lines:

\START L1SIM_RCPE

\STOP

The name of this file is not important, but the DCL logical name L1SIM_RCPE
must be defined to the name of this file. L1SIM first loads the parameters
from L1SIM.RCP, and then redefines any parameters found in L1SIM_RCPE.

    To change a parameter found in the default L1SIM.RCP, copy using EVE
the definition  of the parameter from L1SIM.RCP and insert it into
L1SIM_RCPE between the \START and \STOP lines.  The definition may then be
edited.  

    For example, the following parameters in L1SIM.RCP must be changed to
run L1SIM with a different trigger definition than the default:

o   PROGRAMMING_FILE    The TCC message file produced by COOR_sim
o   RESOURCE_FILE       The resource file produced by COOR_sim 
o   LOOKUP_TABLE_FILE   The Lookup tables used by the Calorimeter Trigger

    The default setting for the options listed in paragraph V.2. can also be
modified using L1SIM_RCPE.

    Warning:
    ********
    The RCPE Software has some problems and some limitations. Please always
verify in your output listings that the intended action was indeed taken.
In particular, at the moment, RCP Edit can only overwrite existing entries.
It cannot create new entries or increase the size of a string or array.
There also seems to be some temporary buffer clearing problem, which
remembers the end of a longer string or array while a shorter string is
parsed. Use padding blanks and match L1SIM.RCP entry sizes for best results.


VIII. SPECIFIC TRIGGER PRESCALING 
=================================

    By default, L1SIM will ignore any prescaling of Specific Triggers. 
To enable prescaling, the parameter APPLY_PRESCALER_DEFAULT must be set to
.TRUE. either in L1SIM_RCP, L1SIM_RCPE or via the USER_DIALOG submenu of
D0USER. 

    The Prescaler Ratios are defined in the Trigger Definition files
read by COOR_sim for each Specific Trigger. 

    L1SIM does not behave exactly like the hardware in applying these
ratios. If the Prescaler Ratio for a Specific Trigger is set to N, the
hardware requires the Andor Network for the Specific Trigger to fire N
times before the Specific Trigger is allowed to fire. In L1SIM, this
prescaling is applied randomly. The Specific Trigger has a 1/N probability
of firing whenever its Andor Network fires.  

    This discrepancy has been intentionally introduced to prevent separate
Specific Triggers to be locked in phase by their prescaling ratios. 
Several external sources of dead-time for Specific Triggers exist in the
hardware that provoke such a desynchronization.  The randomness of the
prescaling will make up for these other sources of dead-times which have no
equivalent in L1SIM.


IX. DISABLING ENERGY LOOKUP Z-CORRECTION 
========================================

    Normally, the transverse energy read from each Trigger Tower is
corrected for the Z position of the interaction vertex before any
further computation or comparison is made on Trigger Tower Energies.
The Calorimeter Trigger normally uses the Fast Vertex Information from
the Level 0 and selects a Level 1 PROM Lookup Page. This Lookup is used
to correct the transverse energies. 

    For some studies, one might want to ignore the Level 0 information, and
force the Level 1 to act as if the vertex is at z=0. This mode corresponds
to  always selecting the Center Level 1 Lookup Page. To achieve this with
L1SIM one must set the RCP parameter FORCE_VERTEX_CENTER in L1SIM_RCP,
L1SIM_RCPE to .TRUE. or enable this option from the USER DIALOG menu of
D0USER.  

    For more  information on how the energy z-correction lookup normally
operates, see the section LOOKUP SYSTEM MANAGER below.

    ****** note *******
    The Level 0 Fast Vertex Information is simulated by L1SIM after finding
    the vertex position from Isajet. L1SIM uses a simplistic geometric
    segmentation of the z-axis into Level 0 Bins.

X. LEVEL 1.5
============

    Specific Triggers can be of two types: pure Level 1 Specific Triggers
or Level 1.5 Specific Triggers.

    A Level 1.5 Specific Trigger will receive 2 levels of requirements. It
receives normal Level 1 Requirements (as for every Specific Trigger), and
additionally requires decisions made by Level 1.5 subsystems. This 
confirmation by Level 1.5 introduces dead time into the system, so the
hardware waits for a Level 1.5 confirmation only if the event would not be
passed otherwise.  This means that a Level 1.5 confirmation is waited for
only if no pure Level 1 Specific Triggers fire and one or more Level 1.5
Specific Triggers meet their Level 1 Requirements. 

    By default, L1SIM behaves like the hardware in that it  does not
produce a  Level 1.5 confirmation on an event unless no pure Level 1
Triggers fire and one or more Level 1.5 Triggers meet their Level 1
requirements. In this case, all Level 1.5 Triggers which have met their
Level 1 requirements are assumed to fire. For special analysis, it is
possible to set a flag in L1SIM (from L1SIM_RCP, L1SIM_RCPE or from the
USER DIALOG menu item) to cause a Level 1.5 evaluation on every event where
a Level 1.5 Trigger meets its Level 1 requirements. If this flag is set
such events will be submitted to Level 1.5 even if a pure  Level 1 Specific
Trigger fires. Note that this mode does NOT correspond to hardware
operation.

    L1SIM does not behave exactly like the Level 1.5 hardware in only one
respect.  When a Level 1.5 confirmation is necessary for an event, L1SIM
completely determines the states of ALL the Level 1.5 Specific Triggers. 
In comparison, the hardware would not necessarily wait until the states of
all the Level 1.5 Specific Triggers are determined before accepting the
event.  It waits only until any one Level 1.5 Specific Trigger is confirmed
or all Level 1.5 Specific Triggers receive negative confirmations. 



XI. MINIMUM-BIAS TRIGGERS
=========================

    A Specific Trigger must have at least one Level 1 Requirement in order
to operate.  To define a minimum-bias Trigger, the requirement 

ZERO_BIAS REQUIRE

should be given to COOR_SIM in the Trigger Definition file. 



XII. GENERATING DUMPS OF TRGR BANKS
===================================

    To generate a formated dump of TRGR banks, accept the defaults in the
first menu presented by the "Define Dumps" item of the D0USER main menu,
and then answer Y to the question "Generate formated Dump of the TRGR
bank?".

    The next menu will prompt for which types of information to include in
the dump file.  Some items in the dump file are quite lengthy, so the user
has the option of omitting one or more of them.  The following menu is used
to select the sections to be included/excluded:

 Control Information                     Yes    No
 Event Summary Current Event             Yes    No
 Datablock Contents (PRTRGR)             Yes    No
 Event Summary Previous Event            Yes    No
 Andor Term Listing by Name              Yes    No
 Trigger Tower ADC Values in Counts      Yes    No
 Trigger Tower ADC Values in GeV         Yes    No
 Level 1 Datablock Raw Dump              Yes    No
 Trigger Tower Energy Deposited in GeV   Yes    No

    Control Information       
    -------------------       

    This section lists the simulation options which are enabled and the
names of the files which programming information was taken from.

    Event Summary Current Event        
    ---------------------------       

    This section gives a summary of the results of the Level 1 Calorimeter
and Level 1 Framework simulation. The Level 1 Datablock crate in the TRGR
bank contains information from both the current beam crossing and from the
previous beam crossing. This section takes its information from the current
event portion of the TRGR bank.

    Datablock Contents (PRTRGR)        
    ---------------------------       

    This section gives summary of the contents of the Level 1 Datablock
crate in the TRGR bank.  This information is produced by the routine
PRTRGR. For more information on the items in this crate see D0 Note 967.
see file D0$LEVEL1:D0_NOTE_967.DOC.

    Event Summary Previous Event        
    ----------------------------       

    This section is much like the current event summary (see above), except
that it gives the information from the previous event portion of the Level
1 Datablock.

    Andor Term Listing by Name        
    --------------------------       

    This section lists each known Andor Term by its physical number, along
with its logical name and its state. This logical name is the one used by 
COOR to represent the Andor Term. For Andor Terms generated by the Level 1
Calorimeter subsystem of L1SIM, the programming of the associated
comparators is also included.

    Trigger Tower ADC Values in Counts       
    ----------------------------------       

    This section lists the ADC value read for each Trigger Tower.  The
values are given in units of least counts (typically the scale is 
1/4 GeV per least count) and typically have an offset added.

    Trigger Tower ADC Values in GeV        
    -------------------------------       

    This section lists the ADC value read for each Trigger Tower given in
units of GeV. These values are given with all offsets removed.

    Level 1 Datablock Raw Dump        
    --------------------------       

    This section gives a hexadecimal dump of the contents of the Level 1
Datablock crate of the TRGR bank.  

    Trigger Tower Energy Deposited in GeV          
    -------------------------------------       

    This section lists the energy deposited in each Trigger Tower as read
from Calorimeter Banks.  The energy is given in units of GeV. This energy
will include noise generated by L1SIM if the noise simulation option is
enabled. Note that this section is meaningless if TRGR banks are used as
input to L1SIM.



    To view each file directly from the D0user program, answer Y to the
next question "Dump event to screen?". 

    The Total number of consecutive events dumped is controlled by NDUMP,
the number of events skipped before the first event is dumped is controlled
by NSKIP (e.g. to dump all events, pick a large NDUMP and NSKIP=0)

    D0user creates one file for each event dumped, with the name 
E_(run #)_(event #).DUMP.  

    The contents of the TRGR bank are defined in D0 Note 967. Note that the
dump of the programming information used to configure the simulator can be
found in summary file which is written out in the standard summary file
at the end of each run.

XIII. LOOKUP SYSTEM MANAGER
===========================

    The Lookup System Manager file contains the parameters used in
programming the Level 1 Lookup PROMs. The contents of this file reflect the
characteristics of the hardware.

    XIII.1 NOISE
    ------------

    If the NOISE option of the simulator is enabled (either by setting the
NOISE_DEFAULT parameter in L1SIM_RCP, L1SIM_RCPE or by enabling noise from
the User Dialog submenu), Gaussian noise is added to the energy deposited
in each Trigger Tower.  L1SIM obtains the standard deviation of the noise
for each tower from the Lookup System Manager object file. The standard
deviation of noise for each Trigger Tower can be found in an appendix of
this document.

    XIII.2 DESIGN CHOICES
    ---------------------

    Following is a list of all design choices implemented in the Trigger
hardware and the Lookup System Manager object file. 

o   The Energy signal received from the BLS cards is scaled to its transverse
    component before it is digitized assuming that the interaction vertex was
    at z=0. The output of the ADC is recorded in the TRGR bank. 

o   All towers use an ADC energy scale of 1/4 GeV per least significant bit.

o   A constant offset of 08 is included in the Trigger Tower Transverse
    Energy values of the TRGR bank.

o   The first energy lookup made in the Lookup PROMs is a z-corrected
    Transverse energy with low energy cut. The second lookup is a
    raw Transverse Energy with no cut.

o   All energy quantities are computed using 1/4 GeV per LSB, except for the
    Missing Pt computation and the Total Et Reference Sets which use 1/2
    GeV per LSB.

o   for all lookup types, the Low Energy Cut is bilateral and uses 
    +/- 2.5 sigmas of noise with a minimum cut of 0.5 GeV.

o   The zero energy response of each lookup PROMs is tuned to a minimum while
    preserving a correct lookup of the lowest negative energy read by the ADC.

o   7 Lookup pages are used for the First lookup, a single page is used for
    the second lookup. The 7 pages for the first lookup are chosen symmetric 
    around z=0. with one page centered at Z=0. 

o   The Level 0 Fast Vertex position is provided as a bin number
    (-15..0..+15). Each bin is 6.25 cm wide. Bin #0 is centered around z=0.

o   The 31 Level 0 bins are distributed in the 7 Lookup Pages as
    [-15,-10], [-9,-6], [-5,-2], [-1,+1], [2,5], [6,9], [10,15] 

o   The geometric center of each lookup page is used to compute the
    energy correction for vertex position of each page.

o   The Trigger Tower geometry has been computed from D0$STP:CAL_STPFILE.DAT 

o   The center of each Trigger Tower used in computing the energy
    correction for vertex position is the center of EM3 for EM towers, the 
    center of FH1 for hadronic towers, and the middle of EM3 and FH1 for TOT
    (EM+HD) towers.

o   The noise used in the low energy cut and noise simulation was computed from
    cell capacitances and cable length, it uses D0 note 459. see appendix for
    Trigger Tower noise values.


XIV. BLS GAIN CORRECTION
========================

    In the hardware, the signal produced by each Calorimeter Depth must be
corrected and summed into Trigger Towers before it is received by the Level
1 Calorimeter Trigger Front-End. This function is performed by the Base
Line Subtractor (BLS) cards. 

    Each calorimeter signal is individually corrected by the BLS to properly
contribute to its Trigger Tower Signal.  A compromise has been reached to
limit the number of different BLS cards. 

    The error caused by the deviation of the coefficient applied by a given
BLS from the ideal computed correction factor can be reproduced and
studied in the simulator. The parameter USE_BLS_GAIN_CORRECTION_DEFAULT
must be be enabled in L1SIM_RCP, L1SIM_RCPE or from the User Dialog menu.

    See L1UTIL_EXAMPLE_BLS_FILE.FOR as an example for creating your own BLS
correction file. The default file D0$LEVEL1$DATA:BLS.DAT introduces no
correction at the moment.


XV. FORCING THE STATE OF UNSIMULATED ANDOR TERMS
================================================

    In the official Specific Trigger definitions used at D0, triggers
typically have Level 1 requirements related to beam quality, pulsers, etc.,
which are not directly simulated by L1SIM.  However, L1SIM can be directed
to give these terms some constant state for every event. These terms may be
added to the RCP array FORCED_ANDOR_TERMS in the file L1SIM_RCP or
L1SIM_RCPE.  The array has the following format:

\ARRAY FORCED_ANDOR_TERMS
!    1234567890123456 use the max length of 16 char for L1SIM_RCPE overwriting
    'MRBS_LOSS       '  FALSE   ! andor term 121
    'MICRO_BLANK     '  FALSE   ! andor term 125
    'MIN_BIAS        '  TRUE    ! andor term 126
\END

The string is the logical name of the Andor Term as given in COOR's
resource file, and TRUE or FALSE is the desired state of the Andor Term.


XVI. TRIGGER TOWER ENERGY SATURATION
====================================

    The energy measured by a Trigger Tower in the Level 1 Hardware will
saturate at some energy value.  To simulate this effect, saturation values
may be given in the file L1SIM_RCP or L1SIM_RCPE.  The format of the array
is as follows:

\ARRAY TRIGGER_TOWER_SATURATION
!
!   Currently, the saturation values have only been estimated out to |ETA|=16.
!
!        EM Saturation in GeV   HD Saturation in GeV   |ETA|
!
                62.                     62.             ! 1
                62.                     62.             ! 2
                62.                     62.             ! 3
                62.                     62.             ! 4
                55.                     62.             ! 5
                48.                     62.             ! 6
                38.                     46.             ! 7
                29.                     40.             ! 8
                23.                     30.             ! 9
                19.                     28.             !10
                16.                     22.             !11
                12.                     18.             !12
                10.                     13.             !13
                 8.                     11.             !14
                 7.                      9.             !15
                 6.                      7.             !16
              1000.                   1000.             !17
              1000.                   1000.             !18
              1000.                   1000.             !19
              1000.                   1000.             !20
\END

The values given are the energy values in GeV at which Trigger Towers at
each ETA tend to saturate. Note that each value is applied to all towers
with the given ETA magnitude, and that values are given separately for the 
EM and HD towers at each |ETA|. Also note that since the energy values are
real numbers, they must be specified with a decimal point in the RCP file.
A value of 1000. GeV may be given to represent no saturation.

XVII. ADDING ON TO L1SIM
========================

    It is possible to add functionality to L1SIM. Additional computation
and analysis may be performed as part of the event processing without
modifying the LEVEL1 routines. 

    L1SIM is structured so that additional simulators for trigger subsystem
may be added easily. For more information, see the file
L1SIM_SUBSYSTEM.DOC

    Also refer to D0$D0USER:D0USER_GUIDE.MEM for a complete description of
the D0USER framework.




                                APPENDIX A

Sample Trigger Definition File
==============================
content of the file EXAMPLE.CFG: (user-written input to COOR_sim)
-------------------------------
Master Configuration File
This is a very simple test configuration.

@reqs:sptrg_15.trig
END_OF_CONFIG

content of the file SPTRG_15.TRIG:(user-written input to COOR_sim)
---------------------------------
Level 1 configuration file
Trigger on one or more EM towers with transverse energy over 5. GeV

SPEC_TRIG_15					sptrg_15

NUM_EM_TOWERS	1	REQS:EM_5.RS  REQS:NO_HAD_VETO.RS         REQUIRE

Content of the file EM_5.RS: (user-written input to COOR_sim)
---------------------------
 TT_ETA(-20:20)  TT_PHI(1:32)  Thresh_Et #  (5.00) GeV

Content of the file REQS:NO_HAD_VETO.RS: (user-written input to COOR_sim)
---------------------------------------
 TT_ETA(-20:20)  TT_PHI(1:32)  Thresh_Et #  (1000.00) GeV

Content of D0$LEVEL1$DATA:EXAMPLE_TRIGGER.INFO (output from COOR_sim)
----------------------------------------------
 Example output of COOR_sim for Specific Trigger #15 requiring at least one EM Trigger Tower with more than 5 GeV.
 
  SPECTRIG ANDORREQ  15( 176)
  SPECTRIG OBEYBUSY  15
  SPECTRIG OBEYLEV2  15
  SPECTRIG PRESCALE  15()
  SPECTRIG  RD_TIME  15( 100)
  THRESHLD  EMETCNT REF(0)   0(      1)
    REFSET     EMET SIGN_ETA(POS) MAGN_ETA(1:19) PHI(1:32) 0 (5000)    SIGN_ETA(NEG) MAGN_ETA(1:19) PHI(1:32) 0 (5000) 
    REFSET   HDVETO SIGN_ETA(POS) MAGN_ETA(1:19) PHI(1:32) 0 (1000000) SIGN_ETA(NEG) MAGN_ETA(1:19) PHI(1:32) 0 (1000000) 
  ST_VS_RS  EM_LIST  0(   15)


                                APPENDIX B

Sample L1SIM.RCP 
================
\START     L1SIM_RCP            ! Name of SRCP bank                             
\SIZE         77        51
!------------------------------------------------------------------------------
!   Name:       L1SIM.RCP
!------------------------------------------------------------------------------
!   Purpose:    Define RCP parameters for location of programming files and
!               default values of run parameters.
!
!   Created:     9-SEP-1991 Philippe Laurens, Steven Klocek
!                              L1C -> L1SIM
!
!   Version:     V2.0           OFFICIAL default version for L1SIM
!------------------------------------------------------------------------------
!   PROM LOOK_UP file name !
!------------------------------------------------------------------------------
 \ARRAY LOOKUP_TABLE_FILE
    'D0$LEVEL1$DATA:CALORIMETER_TRIGGER.LSO'
 \END
!------------------------------------------------------------------------------
!   Trigger Configuration File Name
!------------------------------------------------------------------------------
 \ARRAY PROGRAMMING_FILE
    'D0$LEVEL1$DATA:EXAMPLE_TRIGGER.INFO'
 \END
 \ARRAY RESOURCE_FILE
    'D0$LEVEL1$DATA:TRIGGER_RESOURCES.RCP'
 \END
!----------------------------------------------------------------------
!   BLS Gain Correction file
!----------------------------------------------------------------------
 \ARRAY BLS_GAIN_CORRECTION_FILE
    'D0$LEVEL1$DATA:BLS.DAT'
 \END
!------------------------------------------------------------------------------
!   Path Specification to CAEP banks.
!------------------------------------------------------------------------------
 \ARRAY PATH_DEFAULT
    'RECO'
 \END
!------------------------------------------------------------------------------
!   List Control parameters
!------------------------------------------------------------------------------
 PROGRAMMING_LISTING_DEFAULT  .TRUE.                 !Configuration File Listing
!------------------------------------------------------------------------------
!   Constants used by more than one package
!------------------------------------------------------------------------------
 FAST_DEFAULT   .FALSE.         !If TRUE, fast version of program invoked
 NOISE_DEFAULT  .TRUE.          !If TRUE, noise is added to channels.
 APPLY_PRESCALER_DEFAULT .FALSE. !If TRUE, apply the programmed prescaler to
                                 ! the Specific Triggers.
 BLS_GAIN_CORRECTION_DEFAULT .FALSE. !If TRUE, the BLS Gain Correction
                                     ! Coeffecient is taken into account
\STOP


                                APPENDIX C

Table of Calorimeter Trigger Tower Noise
========================================

 The noise in each Trigger Tower is given in MeV.
 The following is EM trigger tower noise
  EM:  ETA=  1  PHI= 1:16   77.   73.   70.   77.   83.   85.   91.   93.   95.   91.   86.   83.   77.   71.   73.   79.
             1  PHI=17:32   75.   79.   81.   94.   96.  103.  104.  110.  109.  105.  101.   96.   94.   81.   79.   75.
  EM:  ETA=  2  PHI= 1:16   78.   74.   71.   78.   84.   86.   92.   94.   96.   92.   87.   84.   78.   72.   74.   79.
             2  PHI=17:32   76.   80.   82.   95.   97.  104.  105.  111.  110.  105.  102.   97.   95.   82.   80.   76.
  EM:  ETA=  3  PHI= 1:16   80.   76.   73.   79.   85.   88.   94.   96.   97.   94.   88.   85.   80.   74.   76.   81.
             3  PHI=17:32   77.   82.   83.   96.   98.  105.  107.  113.  112.  107.  104.   98.   96.   83.   82.   77.
  EM:  ETA=  4  PHI= 1:16   82.   79.   76.   82.   88.   90.   96.   98.  100.   96.   91.   88.   82.   76.   78.   84.
             4  PHI=17:32   80.   84.   86.   99.  101.  108.  109.  115.  114.  109.  107.  101.   99.   86.   84.   80.
  EM:  ETA=  5  PHI= 1:16   86.   82.   80.   86.   92.   94.  100.  102.  104.  100.   95.   92.   86.   80.   82.   87.
             5  PHI=17:32   83.   88.   89.  102.  105.  111.  113.  119.  118.  113.  110.  104.  102.   89.   88.   83.
  EM:  ETA=  6  PHI= 1:16   72.   68.   66.   71.   77.   79.   84.   86.   87.   84.   80.   77.   72.   66.   68.   73.
             6  PHI=17:32   71.   75.   77.   88.   88.   94.   96.  101.  101.   96.   94.   88.   88.   77.   75.   71.
  EM:  ETA=  7  PHI= 1:16   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.
             7  PHI=17:32   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.   45.
  EM:  ETA=  8  PHI= 1:16  181.  180.  179.  180.  181.  183.  184.  185.  185.  184.  183.  181.  180.  179.  180.  181.
             8  PHI=17:32  183.  184.  185.  186.  188.  189.  190.  191.  191.  190.  189.  188.  186.  185.  184.  183.
  EM:  ETA=  9  PHI= 1:16  158.  156.  155.  156.  158.  159.  160.  161.  161.  160.  159.  158.  156.  155.  156.  158.
             9  PHI=17:32  159.  160.  161.  163.  164.  165.  166.  168.  168.  166.  165.  164.  163.  161.  160.  159.
  EM:  ETA= 10  PHI= 1:16  143.  142.  141.  142.  143.  145.  146.  147.  147.  146.  145.  143.  142.  141.  142.  143.
            10  PHI=17:32  145.  146.  147.  149.  150.  151.  152.  154.  154.  152.  151.  150.  149.  147.  146.  145.
  EM:  ETA= 11  PHI= 1:16  136.  135.  134.  135.  136.  138.  139.  140.  140.  139.  138.  136.  135.  134.  135.  136.
            11  PHI=17:32  138.  139.  140.  141.  143.  144.  145.  146.  146.  145.  144.  143.  141.  140.  139.  138.
  EM:  ETA= 12  PHI= 1:16  133.  132.  130.  132.  133.  134.  135.  137.  137.  135.  134.  133.  132.  130.  132.  133.
            12  PHI=17:32  134.  135.  137.  138.  139.  141.  142.  143.  143.  142.  141.  139.  138.  137.  135.  134.
  EM:  ETA= 13  PHI= 1:16  132.  130.  129.  130.  132.  133.  134.  136.  136.  134.  133.  132.  130.  129.  130.  132.
            13  PHI=17:32  133.  134.  136.  137.  138.  139.  141.  142.  142.  141.  139.  138.  137.  136.  134.  133.
  EM:  ETA= 14  PHI= 1:16  101.  100.   99.  100.  101.  102.  103.  104.  104.  103.  102.  101.  100.   99.  100.  101.
            14  PHI=17:32  102.  103.  104.  105.  106.  107.  108.  109.  109.  108.  107.  106.  105.  104.  103.  102.
  EM:  ETA= 15  PHI= 1:16   99.   99.   98.   99.   99.  100.  101.  102.  102.  101.  100.   99.   99.   98.   99.   99.
            15  PHI=17:32  100.  101.  102.  103.  104.  105.  106.  107.  107.  106.  105.  104.  103.  102.  101.  100.
  EM:  ETA= 16  PHI= 1:16   99.   98.   97.   98.   99.  100.  101.  102.  102.  101.  100.   99.   98.   97.   98.   99.
            16  PHI=17:32  100.  101.  102.  103.  104.  105.  106.  106.  106.  106.  105.  104.  103.  102.  101.  100.
  EM:  ETA= 17  PHI= 1:16   54.   54.   53.   54.   54.   55.   55.   56.   56.   55.   55.   54.   54.   53.   54.   54.
            17  PHI=17:32   55.   55.   56.   56.   57.   57.   58.   58.   58.   58.   57.   57.   56.   56.   55.   55.
  EM:  ETA= 18  PHI= 1:16   53.   52.   52.   52.   53.   53.   54.   54.   54.   54.   53.   53.   52.   52.   52.   53.
            18  PHI=17:32   53.   54.   54.   55.   55.   56.   56.   57.   57.   56.   56.   55.   55.   54.   54.   53.
  EM:  ETA= 19  PHI= 1:16   52.   51.   51.   51.   52.   52.   53.   53.   53.   53.   52.   52.   51.   51.   51.   52.
            19  PHI=17:32   52.   53.   53.   54.   54.   55.   55.   56.   56.   55.   55.   54.   54.   53.   53.   52.
  EM:  ETA= 20  PHI= 1:16    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
            20  PHI=17:32    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
  EM:  ETA= 21  PHI= 1:16    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
            21  PHI=17:32    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
  EM:  ETA= -1  PHI= 1:16   79.   73.   71.   77.   83.   86.   91.   95.   93.   91.   85.   83.   77.   70.   73.   77.
            -1  PHI=17:32   75.   79.   81.   94.   96.  101.  105.  109.  110.  104.  103.   96.   94.   81.   79.   75.
  EM:  ETA= -2  PHI= 1:16   79.   74.   72.   78.   84.   87.   92.   96.   94.   92.   86.   84.   78.   71.   74.   78.
            -2  PHI=17:32   76.   80.   82.   95.   97.  102.  105.  110.  111.  105.  104.   97.   95.   82.   80.   76.
  EM:  ETA= -3  PHI= 1:16   81.   76.   74.   80.   85.   88.   94.   97.   96.   94.   88.   85.   79.   73.   76.   80.
            -3  PHI=17:32   77.   82.   83.   96.   98.  104.  107.  112.  113.  107.  105.   98.   96.   83.   82.   77.
  EM:  ETA= -4  PHI= 1:16   84.   78.   76.   82.   88.   91.   96.  100.   98.   96.   90.   88.   82.   76.   79.   82.
            -4  PHI=17:32   80.   84.   86.   99.  101.  107.  109.  114.  115.  109.  108.  101.   99.   86.   84.   80.
  EM:  ETA= -5  PHI= 1:16   87.   82.   80.   86.   92.   95.  100.  104.  102.  100.   94.   92.   86.   80.   82.   86.
            -5  PHI=17:32   83.   88.   89.  102.  104.  110.  113.  118.  119.  113.  111.  105.  102.   89.   88.   83.
  EM:  ETA= -6  PHI= 1:16   73.   69.   67.   73.   77.   80.   85.   88.   87.   85.   80.   78.   72.   67.   69.   73.
            -6  PHI=17:32   72.   76.   77.   89.   89.   94.   96.  101.  101.   96.   95.   89.   89.   77.   76.   72.
  EM:  ETA= -7  PHI= 1:16   73.   70.   68.   73.   77.   78.   83.   84.   84.   83.   78.   77.   73.   68.   70.   73.
            -7  PHI=17:32   75.   78.   79.   88.   85.   89.   91.   94.   94.   91.   89.   85.   88.   79.   78.   75.
  EM:  ETA= -8  PHI= 1:16  188.  182.  179.  188.  196.  200.  209.  212.  212.  209.  200.  196.  188.  179.  182.  188.
            -8  PHI=17:32  192.  199.  201.  219.  214.  222.  226.  233.  233.  226.  222.  214.  219.  201.  199.  192.
  EM:  ETA= -9  PHI= 1:16  165.  158.  155.  164.  172.  176.  185.  189.  189.  185.  176.  172.  164.  155.  158.  165.
            -9  PHI=17:32  168.  175.  177.  196.  191.  199.  203.  210.  210.  203.  199.  191.  196.  177.  175.  168.
  EM:  ETA=-10  PHI= 1:16  151.  144.  141.  150.  158.  162.  171.  175.  175.  171.  162.  158.  150.  141.  144.  151.
           -10  PHI=17:32  154.  161.  163.  182.  177.  185.  189.  196.  196.  189.  185.  177.  182.  163.  161.  154.
  EM:  ETA=-11  PHI= 1:16  143.  137.  134.  143.  151.  155.  164.  168.  168.  164.  155.  151.  143.  134.  137.  143.
           -11  PHI=17:32  147.  154.  156.  175.  170.  178.  181.  189.  189.  181.  178.  170.  175.  156.  154.  147.
  EM:  ETA=-12  PHI= 1:16  140.  133.  130.  139.  148.  152.  161.  164.  164.  161.  152.  148.  139.  130.  133.  140.
           -12  PHI=17:32  144.  151.  153.  171.  167.  174.  178.  186.  186.  178.  174.  167.  171.  153.  151.  144.
  EM:  ETA=-13  PHI= 1:16  139.  132.  129.  138.  147.  151.  159.  163.  163.  159.  151.  147.  138.  129.  132.  139.
           -13  PHI=17:32  142.  149.  152.  170.  165.  173.  177.  184.  184.  177.  173.  165.  170.  152.  149.  142.
  EM:  ETA=-14  PHI= 1:16  106.  101.   99.  106.  112.  115.  122.  124.  124.  122.  115.  112.  106.   99.  101.  106.
           -14  PHI=17:32  109.  114.  116.  130.  126.  132.  135.  140.  140.  135.  132.  126.  130.  116.  114.  109.
  EM:  ETA=-15  PHI= 1:16  105.  100.   98.  104.  111.  114.  120.  123.  123.  120.  114.  111.  104.   98.  100.  105.
           -15  PHI=17:32  108.  113.  114.  128.  125.  130.  133.  139.  139.  133.  130.  125.  128.  114.  113.  108.
  EM:  ETA=-16  PHI= 1:16  104.   99.   97.  104.  110.  113.  120.  122.  122.  120.  113.  110.  104.   97.   99.  104.
           -16  PHI=17:32  107.  112.  114.  128.  124.  130.  133.  138.  138.  133.  130.  124.  128.  114.  112.  107.
  EM:  ETA=-17  PHI= 1:16   57.   55.   53.   57.   60.   61.   65.   66.   66.   65.   61.   60.   57.   53.   55.   57.
           -17  PHI=17:32   58.   61.   62.   69.   67.   70.   71.   74.   74.   71.   70.   67.   69.   62.   61.   58.
  EM:  ETA=-18  PHI= 1:16   55.   53.   52.   55.   58.   60.   63.   64.   64.   63.   60.   58.   55.   52.   53.   55.
           -18  PHI=17:32   57.   59.   60.   67.   65.   68.   70.   72.   72.   70.   68.   65.   67.   60.   59.   57.
  EM:  ETA=-19  PHI= 1:16   54.   52.   51.   54.   57.   59.   62.   63.   63.   62.   59.   57.   54.   51.   52.   54.
           -19  PHI=17:32   56.   58.   59.   66.   64.   67.   69.   71.   71.   69.   67.   64.   66.   59.   58.   56.
  EM:  ETA=-20  PHI= 1:16    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
           -20  PHI=17:32    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
  EM:  ETA=-21  PHI= 1:16    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
           -21  PHI=17:32    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.    0.
 The following is HD trigger tower noise
  HD:  ETA=  1  PHI= 1:16  298.  293.  289.  298.  306.  309.  317.  318.  320.  316.  310.  306.  299.  291.  293.  300.
             1  PHI=17:32  296.  301.  303.  319.  321.  329.  330.  338.  337.  331.  327.  320.  320.  303.  301.  294.
  HD:  ETA=  2  PHI= 1:16  308.  303.  299.  308.  316.  319.  327.  328.  330.  325.  320.  315.  309.  300.  303.  309.
             2  PHI=17:32  305.  311.  313.  329.  331.  339.  340.  348.  347.  341.  337.  330.  330.  313.  311.  304.
  HD:  ETA=  3  PHI= 1:16  325.  319.  316.  325.  333.  336.  344.  344.  347.  342.  337.  332.  326.  317.  320.  326.
             3  PHI=17:32  322.  328.  330.  346.  348.  355.  357.  364.  364.  358.  354.  347.  347.  330.  328.  321.
  HD:  ETA=  4  PHI= 1:16  329.  323.  320.  329.  337.  339.  347.  348.  351.  346.  340.  336.  330.  321.  324.  330.
             4  PHI=17:32  326.  331.  333.  349.  351.  359.  361.  368.  367.  361.  358.  350.  350.  333.  331.  325.
  HD:  ETA=  5  PHI= 1:16  182.  177.  176.  181.  187.  188.  193.  194.  196.  193.  189.  186.  182.  176.  178.  182.
             5  PHI=17:32  179.  182.  184.  195.  196.  201.  203.  207.  207.  203.  201.  196.  195.  184.  182.  179.
  HD:  ETA=  6  PHI= 1:16  201.  200.  199.  200.  201.  202.  203.  204.  204.  203.  202.  201.  200.  199.  200.  201.
             6  PHI=17:32  201.  203.  204.  205.  207.  208.  209.  210.  210.  209.  208.  206.  205.  204.  203.  201.
  HD:  ETA=  7  PHI= 1:16  371.  369.  367.  369.  371.  373.  375.  377.  377.  375.  373.  371.  369.  367.  369.  371.
             7  PHI=17:32  373.  375.  377.  379.  380.  382.  384.  386.  386.  384.  382.  380.  379.  377.  375.  373.
  HD:  ETA=  8  PHI= 1:16  288.  286.  284.  286.  288.  290.  292.  294.  294.  292.  290.  288.  286.  284.  286.  288.
             8  PHI=17:32  290.  292.  294.  295.  297.  299.  301.  303.  303.  301.  299.  297.  295.  294.  292.  290.
  HD:  ETA=  9  PHI= 1:16  225.  224.  223.  224.  225.  227.  228.  229.  229.  228.  227.  225.  224.  223.  224.  225.
             9  PHI=17:32  227.  228.  229.  230.  232.  233.  234.  235.  235.  234.  233.  232.  230.  229.  228.  227.
  HD:  ETA= 10  PHI= 1:16  262.  261.  260.  261.  262.  264.  265.  266.  266.  265.  264.  262.  261.  260.  261.  262.
            10  PHI=17:32  264.  265.  266.  268.  269.  270.  272.  273.  273.  272.  270.  269.  268.  266.  265.  264.
  HD:  ETA= 11  PHI= 1:16  262.  261.  260.  261.  262.  264.  265.  267.  267.  265.  264.  262.  261.  260.  261.  262.
            11  PHI=17:32  264.  265.  267.  268.  269.  271.  272.  274.  274.  272.  271.  269.  268.  267.  265.  264.
  HD:  ETA= 12  PHI= 1:16  244.  242.  241.  242.  244.  245.  246.  248.  248.  246.  245.  244.  242.  241.  242.  244.
            12  PHI=17:32  245.  246.  248.  249.  251.  252.  254.  255.  255.  254.  252.  251.  249.  248.  246.  245.
  HD:  ETA= 13  PHI= 1:16  236.  234.  233.  234.  236.  237.  239.  240.  240.  239.  237.  236.  234.  233.  234.  236.
            13  PHI=17:32  237.  239.  240.  242.  243.  244.  246.  247.  247.  246.  244.  243.  242.  240.  239.  237.
  HD:  ETA= 14  PHI= 1:16  223.  222.  220.  222.  223.  225.  226.  227.  227.  226.  225.  223.  222.  220.  222.  223.
            14  PHI=17:32  225.  226.  227.  229.  230.  232.  233.  235.  235.  233.  232.  230.  229.  227.  226.  225.
  HD:  ETA= 15  PHI= 1:16  210.  209.  207.  209.  210.  212.  213.  215.  215.  213.  212.  210.  209.  207.  209.  210.
            15  PHI=17:32  212.  213.  215.  216.  218.  219.  220.  222.  222.  220.  219.  218.  216.  215.  213.  212.
  HD:  ETA= 16  PHI= 1:16  202.  201.  199.  201.  202.  204.  205.  206.  206.  205.  204.  202.  201.  199.  201.  202.
            16  PHI=17:32  204.  205.  206.  208.  209.  211.  212.  214.  214.  212.  211.  209.  208.  206.  205.  204.
  HD:  ETA= 17  PHI= 1:16  118.  117.  116.  117.  118.  119.  119.  120.  120.  119.  119.  118.  117.  116.  117.  118.
            17  PHI=17:32  119.  119.  120.  121.  122.  122.  123.  124.  124.  123.  122.  122.  121.  120.  119.  119.
  HD:  ETA= 18  PHI= 1:16  115.  114.  114.  114.  115.  116.  117.  117.  117.  117.  116.  115.  114.  114.  114.  115.
            18  PHI=17:32  116.  117.  117.  118.  119.  119.  120.  121.  121.  120.  119.  119.  118.  117.  117.  116.
  HD:  ETA= 19  PHI= 1:16  113.  112.  111.  112.  113.  113.  114.  115.  115.  114.  113.  113.  112.  111.  112.  113.
            19  PHI=17:32  113.  114.  115.  116.  116.  117.  118.  118.  118.  118.  117.  116.  116.  115.  114.  113.
  HD:  ETA= 20  PHI= 1:16  106.  105.  105.  105.  106.  107.  108.  108.  108.  108.  107.  106.  105.  105.  105.  106.
            20  PHI=17:32  107.  108.  108.  109.  110.  110.  111.  112.  112.  111.  110.  110.  109.  108.  108.  107.
  HD:  ETA= 21  PHI= 1:16   73.   72.   72.   72.   73.   73.   74.   74.   74.   74.   73.   73.   72.   72.   72.   73.
            21  PHI=17:32   73.   74.   74.   75.   75.   76.   76.   77.   77.   76.   76.   75.   75.   74.   74.   73.
  HD:  ETA= -1  PHI= 1:16  300.  293.  291.  299.  306.  310.  316.  320.  318.  317.  309.  306.  298.  289.  293.  298.
            -1  PHI=17:32  294.  301.  303.  320.  320.  327.  331.  337.  338.  330.  329.  321.  319.  303.  301.  296.
  HD:  ETA= -2  PHI= 1:16  309.  303.  300.  309.  315.  320.  325.  330.  328.  327.  319.  316.  308.  299.  303.  308.
            -2  PHI=17:32  304.  311.  313.  330.  330.  337.  341.  347.  348.  340.  339.  331.  329.  313.  311.  305.
  HD:  ETA= -3  PHI= 1:16  326.  320.  317.  326.  332.  337.  342.  347.  344.  344.  336.  333.  325.  316.  319.  325.
            -3  PHI=17:32  321.  328.  330.  347.  347.  354.  358.  364.  364.  357.  355.  348.  346.  330.  328.  322.
  HD:  ETA= -4  PHI= 1:16  330.  324.  321.  330.  336.  340.  346.  351.  348.  347.  339.  337.  329.  320.  323.  329.
            -4  PHI=17:32  325.  331.  333.  350.  350.  358.  361.  367.  368.  361.  359.  351.  349.  333.  331.  326.
  HD:  ETA= -5  PHI= 1:16  182.  178.  176.  182.  186.  189.  193.  196.  194.  193.  188.  187.  181.  176.  177.  182.
            -5  PHI=17:32  179.  182.  184.  195.  196.  201.  203.  207.  207.  203.  201.  196.  195.  184.  182.  179.
  HD:  ETA= -6  PHI= 1:16  202.  199.  197.  203.  207.  210.  214.  217.  216.  215.  210.  208.  202.  197.  198.  203.
            -6  PHI=17:32  203.  207.  209.  220.  217.  222.  224.  228.  228.  224.  222.  217.  220.  209.  207.  204.
  HD:  ETA= -7  PHI= 1:16  362.  357.  354.  363.  369.  373.  379.  382.  382.  380.  373.  369.  362.  354.  356.  363.
            -7  PHI=17:32  364.  371.  373.  389.  383.  389.  392.  398.  398.  392.  389.  383.  387.  373.  371.  366.
  HD:  ETA= -8  PHI= 1:16  277.  273.  270.  278.  284.  287.  293.  296.  296.  294.  287.  284.  277.  270.  272.  278.
            -8  PHI=17:32  279.  285.  287.  302.  297.  303.  306.  311.  311.  306.  302.  297.  301.  287.  285.  281.
  HD:  ETA= -9  PHI= 1:16  218.  214.  211.  219.  224.  228.  234.  237.  237.  235.  228.  225.  218.  211.  213.  219.
            -9  PHI=17:32  220.  226.  228.  243.  238.  244.  247.  252.  252.  247.  243.  238.  242.  228.  226.  221.
  HD:  ETA=-10  PHI= 1:16  261.  255.  252.  261.  269.  273.  280.  284.  284.  282.  273.  270.  261.  252.  254.  261.
           -10  PHI=17:32  264.  271.  273.  292.  285.  293.  296.  303.  303.  296.  292.  286.  291.  273.  271.  265.
  HD:  ETA=-11  PHI= 1:16  254.  248.  245.  254.  261.  265.  272.  276.  275.  273.  265.  262.  254.  245.  247.  254.
           -11  PHI=17:32  256.  263.  265.  283.  277.  284.  287.  294.  294.  287.  283.  277.  282.  265.  263.  257.
  HD:  ETA=-12  PHI= 1:16  235.  230.  227.  236.  243.  247.  254.  258.  258.  256.  247.  244.  235.  227.  229.  236.
           -12  PHI=17:32  238.  245.  247.  266.  259.  266.  270.  276.  276.  270.  266.  260.  264.  247.  245.  239.
  HD:  ETA=-13  PHI= 1:16  228.  222.  219.  229.  236.  240.  247.  251.  251.  249.  240.  237.  228.  219.  222.  229.
           -13  PHI=17:32  231.  238.  240.  259.  252.  259.  263.  269.  269.  263.  259.  253.  257.  240.  238.  232.
  HD:  ETA=-14  PHI= 1:16  215.  209.  206.  216.  223.  227.  234.  238.  237.  235.  227.  223.  215.  206.  208.  216.
           -14  PHI=17:32  218.  225.  227.  245.  239.  246.  250.  256.  256.  250.  245.  239.  244.  227.  225.  219.
  HD:  ETA=-15  PHI= 1:16  202.  197.  194.  203.  210.  214.  222.  226.  225.  223.  214.  211.  202.  194.  196.  203.
           -15  PHI=17:32  205.  212.  214.  233.  226.  234.  237.  244.  244.  237.  233.  227.  232.  214.  212.  206.
  HD:  ETA=-16  PHI= 1:16  194.  189.  186.  195.  202.  207.  214.  218.  217.  215.  207.  203.  194.  186.  188.  195.
           -16  PHI=17:32  197.  204.  207.  225.  218.  226.  230.  236.  236.  230.  225.  219.  224.  207.  204.  198.
  HD:  ETA=-17  PHI= 1:16  114.  111.  109.  114.  118.  120.  123.  125.  125.  124.  120.  118.  114.  109.  110.  114.
           -17  PHI=17:32  115.  119.  120.  129.  125.  129.  131.  134.  134.  131.  129.  126.  128.  120.  119.  116.
  HD:  ETA=-18  PHI= 1:16  111.  108.  107.  111.  115.  117.  120.  122.  122.  121.  117.  115.  111.  107.  108.  111.
           -18  PHI=17:32  112.  116.  117.  126.  123.  126.  128.  131.  131.  128.  126.  123.  125.  117.  116.  113.
  HD:  ETA=-19  PHI= 1:16  108.  106.  104.  109.  112.  114.  118.  120.  120.  119.  114.  113.  108.  104.  105.  109.
           -19  PHI=17:32  110.  113.  114.  124.  120.  124.  126.  129.  129.  126.  124.  121.  123.  114.  113.  110.
  HD:  ETA=-20  PHI= 1:16  102.   99.   98.  102.  106.  108.  112.  114.  113.  112.  108.  106.  102.   98.   99.  102.
           -20  PHI=17:32  103.  107.  108.  117.  114.  118.  120.  123.  123.  120.  117.  114.  117.  108.  107.  104.
  HD:  ETA=-21  PHI= 1:16   64.   63.   62.   64.   66.   67.   69.   70.   70.   70.   67.   66.   64.   62.   63.   64.
           -21  PHI=17:32   65.   67.   67.   72.   70.   72.   73.   75.   75.   73.   72.   71.   72.   67.   67.   65.