WARNING: A Section of this document uses more than 80 characters per line.
         An escape sequence is included to direct the ANSI to postscript 
         translator to switch to small font. 
--------------------------------------------------------------------------------
                              D0 Note #967
                           Original:  4-JUN-1990 
                         Revision B: 17-DEC-1992 
                         Revision C: 13-JUL-1993        Draft

                FIRST LEVEL TRIGGER DATA BLOCK DESCRIPTION
                ------------------------------------------
                        Michigan State University
                     Philippe Laurens, MSUHEP::LAURENS

                        D0$LEVEL1:D0_NOTE_967.DOC
 
TABLE OF CONTENT
----------------                                                           Page

    1. INTRODUCTION .......................................................  2

    2. PURPOSE OF THE FIRST LEVEL TRIGGER DATA BLOCK ......................  2

    3. CONTENT OF THE FIRST LEVEL TRIGGER DATA BLOCK ......................  2

    4. TRANSFER TO ZEBRA BANK .............................................  2

    5. ADDITIONAL DATA IN ZEBRA BANK ......................................  3

    6. FIRST LEVEL TRIGGER CRATE HEADER ...................................  3

    7. DATA BLOCK LENGTH COUNT ............................................  6

    8. 2-BYTE ITEM TO 4-BYTE ZEBRA WORD TRANSLATION .......................  6

    9. ACCESS METHOD AND CODE TRANSPORTABILITY ............................  7

    10. UTILITIES IN ZEBRA_UTIL AND LEVEL1 ................................  7

    11. DETAILED CONTENT OF THE FIRST LEVEL TRIGGER DATA BLOCK ............  9

    12. MODIFICATIONS WITH RESPECT TO D0 NOTE 706 ......................... 17

    13. MODIFICATIONS WITH RESPECT TO ORIGINAL REVISION OF THIS NOTE ...... 18

APPENDIX I: ............................................................... 19

    JET LIST SERVICE of the Level 1 Trigger to the Level 2 Trigger

    A. DEFINITION ......................................................... 19

    B. TOWER ELIGIBILITY .................................................. 19

    C. FORMAT ............................................................. 20

    D. INCOMPLETE LIST .................................................... 20

    E. ORDERING ........................................................... 21

    F. IMPLEMENTATION ..................................................... 21

    G. EXAMPLE OF CONVERSION FROM RELATIVE ADDRESS TO ETA, PHI INDICES .... 21

APPENDIX II:  DATA BLOCK FORMAT IN VME .................................... 23


                                                                        Page 2

    1. INTRODUCTION
    ---------------

    This note describes the First Level Trigger Data Block.  This note 
supersedes the appendix of D0 Note 706.

    The First Level Trigger Data Block covers both (1) the First Level
Trigger Framework and (2) the Level 1 Calorimeter Trigger.

    Additional documentation relating to the First Level Trigger Framework
can be found in D0 Notes 328, and 705, and relating to the Level 1
Calorimeter Trigger in D0 Note 706.

    2. PURPOSE OF THE FIRST LEVEL TRIGGER DATA BLOCK
    ------------------------------------------------

    The First Level Trigger Data Block is used in: (1) test and diagnostics,
(2) passing information about the event to the Level 2 and other offline
analysis programs, and (3) monitoring the performance of the trigger
hardware and trigger programming.

    3. CONTENT OF THE FIRST LEVEL TRIGGER DATA BLOCK
    ------------------------------------------------

    The information in the First Level Trigger Data Block will include: (1)
all inputs to the Framework and Calorimeter Trigger, (2) all outputs, (3)
some intermediate results, (4) some dynamic scaler counts, (5) information
about the previous event (this shows history in the case of input data, and
counter increment in the case of scalers), (6) the Jet Lists derived
from the rest of the data block, (7) the absolute time in ACnet BCD
format, (8) some special scaler counts projected on the 6 particle bunches
in the ring, and (9) a set of foreign scalers provided as a service of
level 1 system.

    4. TRANSFER TO ZEBRA BANK
    -------------------------

    The First Level Trigger Data Block is: (1) generated by the Trigger
hardware, (2) transferred to the First Level VME Crate, (3) read
out by a Data Cable Driver (VBD) on the Data Cable #0, and (4) sent to the
Level 2 System where (5) it is inserted in the "TRGR" Zebra Bank.

    Most of this information is directly generated by the First Level
Trigger hardware. The only exceptions are the Jet Lists and the absolute
time which are filled in by the Level 1 Transfer Program running on a VME
processor board in the First Level VME Crate before the data block is
transferred to Level 2.


                                                                        Page 3

    5. ADDITIONAL DATA IN ZEBRA BANK
    --------------------------------

    The Data Cable #0 is (typically) read out for every event that passes
the First Level Trigger. Additional auxiliary data (e.g. pulser
programming) is currently being read out in the same VME crate as the First
Level Trigger Data Block. In the current configuration at D0 Hall this
auxiliary data is always read at a fixed location after the First Level
Trigger Data Block in the "TRGR" Zebra Bank. This auxiliary data is not
described in this document and is expected to migrate to another crate on
the same Data Cable #0. The First Level Trigger Data Block will then become
the only information read out from the First Level Trigger VME Crate.

    Other detector systems with separate VME crates and their associated
Data Cable Driver Cards will probably also be read out on the same Data
Cable #0 (e.g. the Level 0 Trigger). The "TRGR" Zebra Bank will then
contain additional information not described by this document. In such a
case, there is no guarantee that the First Level Trigger Data Block will
appear as the first data in the TRGR Bank.

    It is strongly advised to use pointers, offsets, and symbolic names
(FORTRAN PARAMETER = compilation constants) to access any data section
within the First Level Trigger Data Block. The location of the First Level
Trigger Data Block within the TRGR Bank should always be obtained from the
routine GZFIND_CRATE in the ZEBRA_UTIL library (cf. routine header for
details).

    6. FIRST LEVEL TRIGGER CRATE HEADER
    -----------------------------------

    This document will concentrate on the "detector dependent" part of the
data from the First Level Trigger VME crate. The Crate header and trailer
structure appearing in the Zebra Bank around the First Level Data Block is
defined in detail in the D0 Note 968 about the Raw Data Structure For D0.
The description of the format of the header will be partially repeated here.

    IMPORTANT: In order to simplify this description of the information in
the Zebra Bank, the first longword of the First Level Trigger Crate Header
in the Zebra Bank is arbitrarily given the number #1. The location of this
word can easily be obtained using GZFIND_CRATE in the ZEBRA_UTIL library.


                                                                        Page 4

                        ----------------------------
   Longword #1          |   Header Length Count    |
                        ----------------------------
   Longword #2          |        SYNC Word         |
                        ----------------------------
   Longword #3          |     Controller Word      |
                        ----------------------------
   Longword #4          |      Version Number      |
                        ----------------------------
   Longword #5          |      Revision Number     |
                        ----------------------------
   Longword #6          |   Spec Trig Fired Mask   |
                        ----------------------------
                        ----------------------------
   Longword #7          |        Word Count        |
                        ----------------------------
   Longword #8          | L1 Data Block First Word |
                                    .
                                    .
                                    .
   Longword # 2714      | L1 Data Block Last Word  |
                        ----------------------------
                        ----------------------------
                        |     Additional Data      |
                        ----------------------------
                        ----------------------------
                        |      Crate Trailer       |
                        ----------------------------

    The 32-bit longword #1 is the header length count (not including this
word) which will be 5 in the case of the First Level Trigger Data Block.

    The longword #2 is the SYNC word.  The most significant 16 bits of this
longword are the least significant 16 bits of the Trigger Number for this
event. The Lower 16 bits are all set high (FFFF in hex).

    The longword #3 is the Controller Word. The most significant 8 bits are
the Crate ID, which is 11 for the First Level Trigger VME Crate. The other
24 bits are currently set to 0.

    The longword #4 is the Version Number. As described in D0 Note 968, the
most significant 3 bits have a special meaning standard to the whole
experiment.
                     Bit  31 (MSB) = Sign Bit = 0
                     Bit  30       = 0 For D0
                                   = 1 For NWA
                     Bit  29       = 0 For Data
                                   = 1 For MonteCarlo
                     Bit 0-28      = Version Number (Integer)


                                                                        Page 5

    The 29 bit Version Number is used to describe the format of the  data
provided by the First Level Trigger. This is the key to decode the meaning,
position, order and format of each word of the First Level Trigger Data
Block section of  the "TRGR" Zebra  Bank.  This document describes the
format at D0; it is not yet clear if the data block at NWA will be able to
use the same format. The data blocks built according to this document will
have the version number 9. Subsequent revisions and updates made to this
document will result in an increase in this Version Number.

    The header longwords #5 and #6 are "Detector Dependent" words as
described in D0 note 968.

    The longword #5 is a Revision Number. The 4 bytes of this longword are
each assigned an individual meaning:

        Bit 24-31     = VME Transfer Program Rev Number  (0-255)
        Bit 16-23     = COMINT PROMs Revision Number     (0-255)
        Bit  8-15     = Lookup System Revision Number    (0-255)
        Bit  0-7      = Trigger Hardware Revision Number (0-255)

     These Revision Numbers complement the Version Number appearing in
longword #4 of the header.  These Revision Numbers characterize objects
that contributed to the content or gathering of the First Level Trigger
Data Block. The Version Number (longword #4) is expected to be changed in
very rare occasions. These Revision  Numbers (longword #6) might be updated
more often, without impact on the format of the data block, thus without
changing the Version Number.

    The "Trigger Hardware Revision Number" will be incremented whenever a
change or addition is made to the hardware.

    The "Lookup System Revision Number" will be incremented whenever the
content of the Energy Lookup PROMs of the Calorimeter Trigger is modified.

    The "COMINT PROMs Revision Number" will be incremented whenever the PROMs
used to collect the data block are modified.

    The "VME Transfer Program Revision Number" will be incremented whenever
the VME based program that synchronizes the readout of the data and the
building the Jet Lists is modified.

    The longword #6 is a 32 bit mask of the Specific Trigger Fired Pattern.
It is also the last word of the header structure. A given bit will be set
high if the corresponding Specific Trigger fired for this beam crossing:

                     Bit  31 (MSB)      = Specific Trigger #31
                     Bit  0  (LSB)      = Specific Trigger #0


                                                                        Page 6

    7. DATA BLOCK LENGTH COUNT
    --------------------------

    The longword #7 is reserved for a data block length count. It is also
the first longword of the Data Block appearing after the header.

    Warning: The level 1 crate is currently read by its VBD card as a
series of smaller sections. The longword #7 does not correspond to the length
of the whole data block but to the length of the first section read by the
VBD card.

    The rest of the information of the First Level Trigger Data Block,
starting with longword #8, is not made of 32-bit quantities which makes it
impossible to simply describe as a list of zebra word. It is a highly non
homogeneous collection of some 1, 2, 3, 4, or 5 byte quantities, mostly
unsigned numbers, with some bit masks, some energies, some scaler counts,
some multi-byte quantities are contiguous, some are interspersed with blank
bytes, etc.

    It is best defined by the list of 5414 2-byte items described in
paragraph 11.

    8. 2-BYTE ITEM TO 4-BYTE ZEBRA WORD TRANSLATION
    -----------------------------------------------

    In the "TRGR" Zebra Bank, the two 2-byte items numbered #1 and #2 in
the list below fill the 4-byte longword #8 in the Zebra Bank, the two items
#3 and #4 fill longword #9, and so on. As mentioned above, the first
longword of the First Level Trigger Crate Header was arbitrarily given the
number #1 in the Zebra Bank (use GZFIND_CRATE to find the location of this
word).

    In the TRGR Zebra Bank :

        - The LOW BYTE of an ODD numbered 2-byte item from the list below
          is the FIRST (least significant) byte of the corresponding Zebra
          Bank 4-byte longword.
          If N was the number (odd) of this 2-byte item, then [(N+1)/2]+7
          is the number of the corresponding Zebra 4-byte longword.
          (e.g. the first byte of Zebra longword #274 is the low byte of
          item #533 which is EM Et of the Trigger Tower at eta=1,phi=1 ).

        - The HIGH BYTE of the same ODD numbered item will be the SECOND byte
          of the same Zebra longword.
          (e.g. the second byte of Zebra longword #274 is the high byte of
          item #533 which is EM Et of the Trigger Tower at eta=1,phi=17 ).

        - The LOW BYTE of the EVEN numbered item directly following this odd
          numbered item will be the THIRD byte of the same Zebra longword.
          (e.g. the third byte of Zebra longword #274 is the low byte of
          item #534 which is EM Et the Trigger Tower at eta=1,phi=2 ).

        - The HIGH BYTE of the same EVEN numbered item will be the FOURTH
          (most significant) byte of the same Zebra longword.
          (e.g. the fourth byte of Zebra longword #274 is the high byte of
          item #534 which is EM Et of the Trigger Tower at eta=1,phi=18 ).

                                                                        Page 7

    9. ACCESS METHOD AND CODE TRANSPORTABILITY
    ------------------------------------------

    Accessing the trigger data by first, second, third, or fourth byte of a
Zebra Bank longword is the only transportable method for writing offline
code. Care must also be taken to use a transportable scheme for accessing a
byte in a 32-bit word (e.g. use EQUIVALENCE between INTEGER and BYTE
quantities and D0$PARAMS:BYTE_ORDER.PARAMS to address the individual bytes).

    10. UTILITIES IN ZEBRA_UTIL AND LEVEL1
    --------------------------------------

    A number of utility routines related to the Level 1 data block are
available in the D0 library LEVEL1.

PRTRGR (in ZEBRA_UTIL)
    This routine will print the contents of the TRGR bank. It follows the
    argument conventions of a standard PRXXXX routine (cf.
    D0$DOCS:ZEBRA_RULES.MEM and D0$DOCS:PRXXXX_EXAMPLE.DOC). The IFL
    argument which defines the amount of printing can be used to select a
    Data Block summary only, ADC counts by tower only, or both.

    At the moment PRTRGR only prints the information related to the Level 1
    block. PRTRGR needs to be upgraded to also include all other subsystems
    on Data Cable 0 that contribute to the TRGR bank.

TRGR_DISP.PBD (In D0$PBD)
    This is a display and dump program builder package for producing more
    elaborate unpacking of the Level 1 data than the simple PRTRGR routine.
    cf. D0$LEVEL1:L1SIM_TOOLS.DOC.

L1UTIL_ADC_COUNT_UNPACK and L1UTIL_TRGR_ADC_UNPACK  (in D0$LEVEL1)
    Both of these routines unpack the ADC bytes of a TRGR bank into an
    array whose indices are Trigger Tower coordinates.
    L1UTIL_ADC_COUNT_UNPACK returns ADC counts, L1UTIL_TRGR_ADC_UNPACK
    returns energies.

L1EXTRACT_items     (in D0$ZEBRA_UTIL)
    There is a series of routines in ZEBRA_UTIL to extract various items 
of Level 1 data from the TRGR bank. If you something not currently covered
by these routines, contact MSUHEP::LAURENS.
The current list of such routines is
        L1EXTRACT_2ND_LKP_ENERGIES
        L1EXTRACT_ACNET_TIME
        L1EXTRACT_ANDOR_TERM
        L1EXTRACT_BEAMX_SCALER
        L1EXTRACT_GLOBAL_TOWER_COUNTS
        L1EXTRACT_JET_LIST
        L1EXTRACT_L0_FAST_Z_DATA
        L1EXTRACT_L0_FAST_Z_SCALERS
        L1EXTRACT_L15_SCALERS
        L1EXTRACT_L1_FIRED_SCALERS
        L1EXTRACT_MOMENTUM
        L1EXTRACT_SPTRG_EXPOS_SCALERS
        L1EXTRACT_SPTRG_FIRED_SCALERS
        L1EXTRACT_TRANSV_ENERGIES
        L1EXTRACT_TRGTWR_ADC_ENERGY
        L1EXTRACT_L15_STATUS
        L1EXTRACT_LIVEX_SCALERS

                                                                        Page 8

L1UTIL_GET_FOREIGN_SCALER       (in D0$ZEBRA_UTIL)
    This routine will return the value of a selected 5-byte scaler from the
    Foreign Scaler portion of the Data Block in a TRGR bank.

L1UTIL_SCALER_SUBTRACT          (in D0$LEVEL1)
    Many quantities in the Level 1 Data Block are 5-byte scalers. This
    routine will return a signed 4-byte difference between two 5-byte
    quantities. A and B are arrays of 2 integers each.

L1UTIL_WHERE_WORD               (in D0$LEVEL1)
    This routine aids in the conversion from the 16-bit item address
    given for quantites in D0 Note 967 to the 32-bit item address needed
    for use with ZEBRA banks.

L1UTIL_JET_LIST_BUILDER         (in D0$LEVEL1)
    This routine can reconstruct an EM Et or Tot Et Jet list of arbitrary
    length, only using the content of the TRGR bank for input. This routine
    can be used by a Level 2 processing node when the Jet List in the Data
    Block has saturated.

[15m
                                                                                                     Page 9

    11. DETAILED CONTENT OF THE FIRST LEVEL TRIGGER DATA BLOCK
    ----------------------------------------------------------
-------------------------------------------------------------------------------------------------------------
 BYTE     ITEM     |
 OFFSET   NUMBER   |
(hex)    (decimal) | LOW BYTE                                                |  HIGH BYTE              
 ---      -------  | --------                                                |  ---------              
-------------------------------------------------------------------------------------------------------------
CURRENT BEAM CROSSING                                                                                  
---------------------                                                                                  
0000          1    |                                                         |                         
.   10t+1:10t+5    | TRIGGER COUNT SPEC. TRIG. t (5 bytes,low 1st)  (t=0:31) |  NOT ASSIGNED           
.   10t+6:10t+10   | ENABLE  COUNT SPEC. TRIG. t (5 bytes,low 1st)  (t=0:31) |  NOT ASSIGNED           
027E        320    |                                                         |                         
                   |                                                         |                         
0280        321    |                                                         |                      
.                  | EVENT TRANSFER NUMBER       (5 bytes,low 1st)           |  NOT ASSIGNED        
.                  | This number will also appear in the event HEAD bank as  |                      
.                  | words +7 (low 24 bits) and +8 (high 16 bits).           |                      
.                  | The Transfer Count scaler will increment only when an   |
.                  | event is actually transfered to the Level 2 system      |
.                  | (i.e. a Level 1 Specific Trigger fires that does not    |
.                  | need L1.5 confirmation or else a Level 1 Specific       |
.                  | Trigger fires that does need L1.5 confirmation and      |
.                  | it is confirmed by L1.5). The Transfer Count will NOT   |
.                  | increment in response to triggers that are rejected     |
.                  | at Level 1.5 (i.e. triggers that did not result in the  |
.                  | transfer of an event to the L2 system).                 |
.                  | The lower 4 bits of this number are the lower 4 bits    |
.                  | of the Trigger-Acquision Synchronization (TAS) Number.  |
.                  | The TAS number will appear in all Crate Headers,        |
.                  | the Crate Trailers, and in the Sequencer Trailers.      |
0288        325    |                                                         |                       
                   |                                                         |                       
028A        326    |                                                         |                       
.                  | START DIGITIZE NUMBER       (5 bytes,low 1st)           |  NOT ASSIGNED         
.                  | The Start Digitization Count scaler will increment      |
.                  | each time the Trigger Framework sends out               |
.                  | Start Digitization signals to the Front-End Systems.    |
.                  | The lower 12 bits of this number are the upper 12 bits  |
.                  | of the Trigger-Acquision Synchronization (TAS) Number   |
0292        330    |                                                         |
                   |                                                         |
0294        331    |                                                         |
.                  | LEVEL 1.5 CYCLE COUNT       (5 bytes,low 1st)           |  NOT ASSIGNED
.                  | This number increments for every event that receives    |
.                  | a level 1.5 confirmation or rejection                   |
029C        335    |                                                         |
                   |                                                         |
029E        336    |                                                         |
.                  | POTENTIAL LEVEL 1.5 COUNT   (5 bytes,low 1st)           |  NOT ASSIGNED
.                  | This number increments for every event where            |
.                  | AT LEAST ONE Specific Trigger requiring Level 1.5 fired.|
.                  | Such an event will cause a Level 1.5 cycle only if      |
.                  | ALL Specific Triggers that fired for this beam crossing |
.                  | require Level 1.5, thus making the level 1.5            |
.                  | confirmation of the event necessary.                    |
02A6        340    |                                                         |
                   |                                                         |
02A8        341    |                                                         |
.                  | BEAM CROSSING NUMBER SCALER (5 bytes,low 1st)           |  NOT ASSIGNED
02B0        345    |                                                         |
                   |                                                         |
02B2        346    |                                                         |
.                  | GATED BEAM CROSSING NUMBER  (5 bytes,low 1st)           |  NOT ASSIGNED
02BA        350    |                                                         |
                   |                                                         |
02BC        351    |                                                         |
.                  | LEVEL 0 GOOD COUNT          (5 bytes,low 1st)           |  NOT ASSIGNED
.                  | This scaler counts the beam crossings where the         |
.                  | Level 0 Good signal was found asserted. The Level 0     |
.                  | Good Signal results in the selection of a vertex        |
.                  | correction factor for the Level 1 Calorimeter Trigger   |
02C4        355    |                                                         |
                   |                                                         |
02C6        356    |                                                         |
.                  | 1 SCALER, NOT ASSIGNED YET (5 bytes,low 1st)            |  NOT ASSIGNED
02CE        360    |                                                         |
                   |                                                         |

                                                                                                     Page 10
02D0        361    |                                                         |
.         361+n    | FSTD FOR SPECIFIC TRIGGERS 4n+0 thru 4n+3       (n=0:7) |  NOT ASSIGNED
.                  |       LSB bit #0 Spec. Trig. 4n+0 enabled               |
.                  |           bit #1 Spec. Trig. 4n+1 enabled               |
.                  |           bit #2 Spec. Trig. 4n+2 enabled               |
.                  |           bit #3 Spec. Trig. 4n+3 enabled               |
.                  |           bit #4 Spec. Trig. 4n+0 ANDOR fired           |
.                  |           bit #5 Spec. Trig. 4n+1 ANDOR fired           |
.                  |           bit #6 Spec. Trig. 4n+2 ANDOR fired           |
.                  |       MSB bit #7 Spec. Trig. 4n+3 ANDOR fired           |
02DE        368    |                                                         |
                   |                                                         |
02E0        369    |                                                         |
.         369+n    | ANDOR INPUT TERMS 8n..8n+7 FOR SP. TRIG. 0 -15 (n=0:31) |  NOT ASSIGNED 
.         401+n    | ANDOR INPUT TERMS 8n..8n+7 FOR SP. TRIG. 16-31 (n=0:31) |  NOT ASSIGNED 
.                  |       LSB is Andor Input Term 8n                        |
.                  |       MSB is Andor Input Term 8n+7                      |
.                  | note: All Specific Triggers will receive the SAME       |
.                  | 256 andor input terms. The same 256 andor input terms   |
.                  | will thus appear twice in the data block.               |
035E        432    |                                                         |
                   |                                                         |
0360        433    |                                                         |
.         433+n    | FRONT-END BUSY ON TRIG-ACQ CABLES 8n thru 8n+7  (n=0:3) |  NOT ASSIGNED 
.         437+n    | FRONT-END BUSY ON TRIG-ACQ CABLES 8n thru 8n+7  (n=0:3) |  NOT ASSIGNED 
.         441+n    | FRONT-END BUSY ON TRIG-ACQ CABLES 8n thru 8n+7  (n=0:3) |  NOT ASSIGNED 
.         445+n    | FRONT-END BUSY ON TRIG-ACQ CABLES 8n thru 8n+7  (n=0:3) |  NOT ASSIGNED 
.                  |       LSB is front end busy 8n                          |
.                  |       MSB is front end busy 8n+7                        |
.                  | note: The SAME 32 Front-End Busy signals appear         |
.                  | four times in the data block.                           |
037E        448    |                                                         |
                   |                                                         |
0380        449    |                                                         |
.         449+n    | SPEC TRIG FIRED 8n thru 8n+7                    (n=0:3) |  NOT ASSIGNED
.         453+n    | SPEC TRIG FIRED 8n thru 8n+7                    (n=0:3) |  NOT ASSIGNED
.         457+n    | SPEC TRIG FIRED 8n thru 8n+7                    (n=0:3) |  NOT ASSIGNED
.         461+n    | SPEC TRIG FIRED 8n thru 8n+7                    (n=0:3) |  NOT ASSIGNED
.                  |       LSB is spec. trig. 8n                             |
.                  |       MSB is spec. trig. 8n+7                           |
.                  | note: The same 32 Specific Trigger Fired signals appear |
.                  | four times in the data block.                           |
039E        464    |                                                         |
                   |                                                         |
03A0        465    |                                                         |
.         465+n    | START DIGITIZE ON TRIG-ACQ CABLES 8n thru 8n+7  (n=0:3) |  NOT ASSIGNED
.                  |       LSB is cable 8n                                   |
.                  |       MSB is cable 8n+7                                 |
03A6        468    |                                                         |
                   |                                                         |
03A8        469    |                                                         |
.         469+n    | FRONT END BUSY DISABLE SPEC. TRIG. 8n thru 8n+7 (n=0:3) |  NOT ASSIGNED
.                  |       LSB is spec. trig. 8n                             |
.                  |       MSB is spec. trig. 8n+7                           |
03AE        472    |                                                         |
                   |                                                         |
03B0        473    |                                                         |
.         473+n    | 2ND LEVEL DISABLE SPEC. TRIG. 8n thru 8n+7      (n=0:3) |  NOT ASSIGNED
.                  |       LSB is spec. trig. 8n                             |
.                  |       MSB is spec. trig. 8n+7                           |
03B6        476    |                                                         |
                   |                                                         |
03B8        477    | RESERVED                                                |  NOT ASSIGNED
                   |                                                         |
03BA    478:480    | Et EM    (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
03C0    481:483    | Et HAD   (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
                   | note: The scale currently chosen for Et EM and Et HAD   |
                   | is 1/4 GeV per least count, but could be redefined      |
                   | if the need arises.                                     |
03C6    484:486    | Px Total (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
03CC    487:489    | Py Total (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
                   | note: The sign bit of Px and Py will be the 24th bit    |
                   | (i.e. the MSB of the 3rd byte).                         |
                   | note: The scale currently chosen for Px and Py          |
                   | is 1/2 GeV per least count (but could be redefined).    |
03D2        490    |                                                         |
.             .    | RESERVED                                                |  NOT ASSIGNED
03D8        493    |                                                         |
                   |                                                         |

                                                                                                     Page 11
03DA    494:496    | Et Total (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
                   | note: The scale currently chosen for Et Total           |
                   | is 1/4 GeV per least count (but could be redefined).    |
03E0        497    | Missing Pt (1 byte, saturates at 255)                   |  NOT ASSIGNED
                   | note: The scale currently chosen for Missing Pt         |
                   | is 1/2 GeV per least count. This means that anything    |
                   | bigger and including 127.5 GeV is represented by 255.   |
03E2        498    |                                                         |
.             .    | RESERVED                                                |  NOT ASSIGNED
03E4        499    |                                                         |
03E6    500:502    | L2 EM    (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
03EC    503:505    | L2 HD    (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
03F2    506:508    | L2 Total (3 bytes, low 1st, signed 2's complement)      |  NOT ASSIGNED 
                   | note: The mnemonic L2 refers to second lookup quantity. |
                   |       The existence and definition of second lookup     |
                   |       quantities will depend on the programming of the  |
                   |       energy lookup system.                             |
                   |                                                         |
03F8    509:510    | EM Et Reference Set #0 final count (2 bytes, low 1st)   |  NOT ASSIGNED
03FC    511:512    | EM Et Reference Set #1 final count (2 bytes, low 1st)   |  NOT ASSIGNED
0400    513:514    | EM Et Reference Set #2 final count (2 bytes, low 1st)   |  NOT ASSIGNED
0404    515:516    | EM Et Reference Set #3 final count (2 bytes, low 1st)   |  NOT ASSIGNED
                   |                                                         |
0408    517:518    | Total Et Reference Set #0 final count (2 bytes, low 1st)|  NOT ASSIGNED
040C    519:520    | Total Et Reference Set #1 final count (2 bytes, low 1st)|  NOT ASSIGNED
0410    521:522    | Total Et Reference Set #2 final count (2 bytes, low 1st)|  NOT ASSIGNED
0414    523:524    | Total Et Reference Set #3 final count (2 bytes, low 1st)|  NOT ASSIGNED
                   |                                                         |
0418        525    | Level 0 Fast Vertex Information                         |  NOT ASSIGNED
                   |     LSB bit #0 is Bin Number, data bit #0 LSB           |
                   |         bit #1 is Bin Number, data bit #1               |
                   |         bit #2 is Bin Number, data bit #2               |
                   |         bit #3 is Bin Number, data bit #3               |
                   |         bit #4 is Bin Number, data bit #4 MSB (sign bit)|
                   |         bit #5 is the GOOD bit                          |
                   |         bit #6 Reserved                                 |
                   |     MSB bit #7 Reserved                                 |
                   | Note: The lower 5 bits (1:5) form a 2's complement      |
                   |       signed integer specifying the Number of the       |
                   |       Level 0 Bin containing the interaction vertex.    |
                   |       For details on the meaning of the Level 0 Bins    |
                   |       and the Good bit, refer to the description of     |
                   |       the Level 0 Fast Vertex Position service          |
                   |       to the First Level Calorimeter Trigger.           |
                   |                                                         |
041A        526    |                                                         |
.                  | Reserved for more Level 0 information                   |  NOT ASSIGNED
041E        528    |                                                         |
                   |                                                         |
0420        529    | Level 1.5 Status for this event                         |  NOT ASSIGNED
.           529    |     LSB bit #0: Potential L1.5 Event                    |
.                  |                 i.e. at least one L1.5 Sp.Trg Fired     |
.                  |         bit #1: Skip Level 1.5 Cycle                    |
.                  |                 i.e. at least one L1.5 Sp.Trg Fired and |
.                  |                      at least one pure L1 Sp.Trg Fired  |
.                  |         bit #2: Skip Level 1.5 Cycle (same as bit #1)   |
.                  |         bit #3: Start Level 1.5 Cycle (see note below)  |
.                  |                 i.e. at least one L1.5 Sp.Trg Fired and |
.                  |                      no pure L1 Sp.Trg Fired            |
.                  |         bit #4: RESERVED                                |
.                  |         bit #5: RESERVED                                |
.                  |         bit #6: RESERVED                                |
.                  |     MSB bit #7: RESERVED                                |
.                  | note: Bit #3 of item 529 found high signals that        |
.                  |       a Level 1.5 Cycle was performed for this event    |
.                  |       and further Level 1.5 information is available    |
.                  |       for this event in items 4987:5058.                |
.                  |       Bit #3 of item 529 found low signals that         |
.                  |       a Level 1.5 Cycle was NOT performed for this event|
.                  |       and the Level 1.5 information in items 4987:5058  |
.                  |       corresponds to an earlier event that caused       |
.                  |       a Level 1.5 Cycle.                                |
.       530:532    |     RESERVED                                            |
0426        532    |                                                         |
                   |                                                         |
0428    533:534    | Reserved for Intermediate Word Count
                   |                                                         |

                                                                                                     Page 12
042C        535    | EM Et TRIGGEr TOWER ADC                                 |
.     518+16e+p    | EMTT(eta,phi)=(+e,p)                    (e=1:20;p=1:16) |  EMTT(eta,phi)=(+e,p+16)
06AA        854    |                                                         |
                   |                                                         |
06AC        855    | EM Et TRIGGER TOWER ADC                                 |
.     838+16e+p    | EMTT(eta,phi)=(-e,p)                    (e=1:20;p=1:16) |  EMTT(eta,phi)=(-e,p+16)
092A       1174    |                                                         |
                   |                                                         |
092C       1175    | HAD Et TRIGGER TOWER ADC                                |
.    1158+16e+p    | HADTT(eta,phi)=(+e,p)                   (e=1:20;p=1:16) |  HADTT(eta,phi)=(+e,p+16)
0BAA       1494    |                                                         |
                   |                                                         |
0BAC       1495    | HAD Et TRIGGER TOWER ADC                                |
.    1478+16e+p    | HADTT(eta,phi)=(-e,p)                   (e=1:20;p=1:16) |  HADTT(eta,phi)=(-e,p+16)
0E2A       1814    |                                                         |
                   | note: All energy values are scaled to Et assuming       |
                   |       the interaction was centered at z=0.              |
                   | note: All energy values built in the data block are     |
                   |       positively biased with a constant offset.         |
                   |       The offset currently chosen is 8 (but could be    |
                   |       redefined in the future) meaning that an ADC count|
                   |        of 8 corresponds to an energy deposit of 0 GeV.  |
                   | note: The scale currently chosen for the Trigger Tower  |
                   |       energies is 1/4 GeV per least count               |
                   |       (but could be redefined in the future).           |
-------------------------------------------------------------------------------------------------------------
0E2C  1815:1816    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
PREVIOUS BEAM CROSSING
----------------------
0E30       1817    |
.                  |
.                  | The same information as above is available for the beam crossing 
.                  | directly preceding the  event that caused the First Level Trigger to fire.
.                  |
1C5A       3630    |
-------------------------------------------------------------------------------------------------------------
1C5C  3631:3632    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Reserved, (Formerly EM Et JET LIST)
--------
1C60       3633    | 
.                  | Reserved (130 items)
1D62       3762    |
-------------------------------------------------------------------------------------------------------------
1D64  3763:3764    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Reserved, (Formerly TOTAL Et JET LIST)
--------
1D68       3765    | 
.                  | Reserved (130 items)
1E6A       3894    |
-------------------------------------------------------------------------------------------------------------
1E6C  3895:3896    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Masks of Jet Patterns
---------------------
1E70       3897    |
.                  | Pattern information for EM Et (and associated Hadronic Veto) Threshold Reference set #0 
.                  | and Trigger Towers:
.                  |
.     3895+2e+n    | EMTT(eta,phi)=(+e,8n+1:8n+8)            (e=1:20;n=0:1)  | EMTT(eta,phi)=(+e,8n+17:8n+24)
.                  | LSB bit #0 phi = 8n+8                                   |  LSB bit #0 phi = 8n+24
.                  |     bit #1 phi = 8n+7                                   |      bit #1 phi = 8n+23
.                  |     bit #2 phi = 8n+6                                   |      bit #2 phi = 8n+22
.                  |     bit #3 phi = 8n+5                                   |      bit #3 phi = 8n+21
.                  |     bit #4 phi = 8n+4                                   |      bit #4 phi = 8n+20
.                  |     bit #5 phi = 8n+3                                   |      bit #5 phi = 8n+19
.                  |     bit #6 phi = 8n+2                                   |      bit #6 phi = 8n+18
.                  | MSB bit #7 phi = 8n+1                                   |  MSB bit #7 phi = 8n+17
.                  | Note: A bit is set high in a given pattern when the corresponding Trigger Tower 
.                  |       (eta,phi) had simultaneously:
.                  |       - an EM Et that cleared its assigned threshold from the EM Et 
.                  |         Threshold Reference set #0,
.                  |       - and an HD Et that did not clear its assigned threshold from the HD Veto 
.                  |         Threshold Reference Set #0,
.                  |       which were both programmed by COOR.
.     3935+2e+n    | EMTT(eta,phi)=(-e,8n+1:8n+8)             (e=1:20;n=0:1) | EMTT(eta,phi)=(-e,8n+17:8n+24)
.                  | LSB bit #0 phi = 8n+8                                   |  LSB bit #0 phi = 8n+24
.                  | .                                                       |  .
.                  | MSB bit #7 phi = 8n+1                                   |  MSB bit #7 phi = 8n+17
1F0E       3976    |                                                         |
                   |

                                                                                                     Page 13
1F10       3977    |
.                  | The Pattern information for EM Et (and associated Hadronic Veto) 
.                  | Threshold Reference set #1 follows the same format and ordering as Reference set #0.
1FAE       4056    |
                   |
1FB0       4057    |
.                  | The Pattern information for EM Et (and associated Hadronic Veto) 
.                  | Threshold Reference set #2 follows the same format and ordering as Reference set #0.
204E       4136    |
                   |
2050       4137    |
.                  | The Pattern information for EM Et (and associated Hadronic Veto) 
.                  | Threshold Reference set #3 follows the same format and ordering as Reference set #0.
20EE       4216    |
                   |
                   |
20F0       4217    |
.                  | Pattern information for TOT Et Threshold Reference set #0 and Trigger Towers:
.                  |
.     4215+2e+n    | TOTTT(eta,phi)=(+e,8n+1:8n+8)            (e=1:20;n=0:1) |TOTTT(eta,phi)=(+e,8n+17:8n+24)
.                  | LSB bit #0 phi = 8n+1                                   |  LSB bit #0 phi = 8n+17
.                  |     bit #1 phi = 8n+2                                   |      bit #1 phi = 8n+18
.                  |     bit #2 phi = 8n+3                                   |      bit #2 phi = 8n+19
.                  |     bit #3 phi = 8n+4                                   |      bit #3 phi = 8n+20
.                  |     bit #4 phi = 8n+5                                   |      bit #4 phi = 8n+21
.                  |     bit #5 phi = 8n+6                                   |      bit #5 phi = 8n+22
.                  |     bit #6 phi = 8n+7                                   |      bit #6 phi = 8n+23
.                  | MSB bit #7 phi = 8n+8                                   |  MSB bit #7 phi = 8n+24
.                  | Note: A bit is set high in a given pattern when the corresponding Trigger Tower 
.                  |       (eta,phi) had a Total (=EM+HD) Et that cleared its assigned threshold 
.                  |       from the Total Et Threshold Reference set #0 which was programmed by COOR.
.                  | Note: the bit ordering inside each byte is reversed compared to the one used 
.                  |       for the EM Et information above.
.     4255+2e+n    | TOTTT(eta,phi)=(-e,8n+1:8n+8)            (e=1:20;n=0:1) |TOTTT(eta,phi)=(-e,8n+17:8n+24)
.                  | LSB bit #0 phi = 8n+1                                   |  LSB bit #0 phi = 8n+17
.                  | .                                                       |  .
.                  | MSB bit #7 phi = 8n+8                                   |  MSB bit #7 phi = 8n+24
218E       4296    |                                                         |
                   |
2190       4297    |
.                  | The Pattern information for TOT Et Threshold Reference set #1
.                  | follows the same format and ordering as Reference set #0.
222E       4376    |
                   |
2230       4377    |
.                  | The Pattern information for TOT Et Threshold Reference set #2
.                  | follows the same format and ordering as Reference set #0.
22CE       4456    |
                   |
22D0       4457    |
.                  | The Pattern information for TOT Et Threshold Reference set #3
.                  | follows the same format and ordering as Reference set #0.
236E       4536    |
-------------------------------------------------------------------------------------------------------------
2370  4537:4538    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Reserved (Formerly TRD Hot Tower Table Information)
--------
2374       4539    |
.                  | Reserved (320 items)
25F2       4858    |
-------------------------------------------------------------------------------------------------------------
25F4  4859:4860    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Specific Trigger programming information used in building the Jet Lists
-----------------------------------------------------------------------
25F8       4861    |
.     4861+4r+n    | (n=0:3,r=0:3)                                                   |  NOT ASSIGNED
.                  | 8-bit mask showing which of the Specific Triggers 8n thru 8n+7  |
.                  | were programmed with at least one comparison on the count       |
.                  | of Trigger Towers above the EM Et Threshold Reference Set #r.   |
.                  |    LSB is Specific Trigger 8n                                   |
.                  |    MSB is Specific Trigger 8n+7                                 |
2616       4876    |                                                                 |
                   |                                                                 |
2618       4877    |                                                                 |
.     4877+4r+n    | (n=0:3,r=0:3)                                                   |  NOT ASSIGNED
.                  | 8-bit mask showing which of the Specific Triggers 8n thru 8n+7  |
.                  | were programmed with at least one comparison on the count       |
.                  | of Trigger Towers above the TOT Et Threshold Reference Set #r.  |
.                  |    LSB is Specific Trigger 8n                                   |
.                  |    MSB is Specific Trigger 8n+7                                 |
2636       4892    |                                                                 |
                   |

                                                                                                     Page 14
2638       4893    |
.                  | Reserved (18 items) Formerly for masks of Specific Triggers that fired 
.                  | and were programmed with at least one comparison on the count of Trigger Towers 
.                  | above an EM or Tot Et Threshold Reference Set 
265A       4910    |
                   |
265C       4911    |
.     4911+4r+n    | (n=0:3,r=0:7)                                                   |  NOT ASSIGNED
.                  | 8-bit mask showing which of the Specific Triggers 8n thru 8n+7  |
.                  | were programmed with at least one comparison on the count       |
.                  | of Large Tiles above the Large Tile Threshold Reference Set #r. |
.                  |    LSB is Specific Trigger 8n                                   |
.                  |    MSB is Specific Trigger 8n+7                                 |
269A       4942    |
-------------------------------------------------------------------------------------------------------------
269C  4943:4944    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Large Tile Jet Patterns
-----------------------
26A0       4945    |
.                  | Pattern information for Large Tile Threshold Reference set #0 and Large Tiles:
.                  |
.     4945+e       | LT( eta, phi ) = (+4e+1 & -4e-1, all_phis)     (e=0:4)  |  NOT ASSIGNED 
.                  | LSB bit #0 eta = +4e+1, phi =  1                        |
.                  |     bit #1 eta = +4e+1, phi =  9                        |
.                  |     bit #2 eta = +4e+1, phi = 17                        |
.                  |     bit #3 eta = +4e+1, phi = 25                        |
.                  |     bit #4 eta = -4e-1, phi =  1                        |
.                  |     bit #5 eta = -4e-1, phi =  9                        |
.                  |     bit #6 eta = -4e-1, phi = 17                        |
.                  | MSB bit #7 eta = -4e-1, phi = 25                        |
.                  | Note: LT( +e, p ) represents the Large Tile made up of the 32 Trigger towers with 
.                  |       eta in the range +e:+e+3 (or -e:-e-3 for negative eta) and phi in the range p:p+7 
.                  |       The notation convention is thus to label a Large Tile by the lowest Trigger Tower 
.                  |       |eta| and phi indices that it covers (instead of introducing a new index system)
.                  | Note: A bit is set high in a given pattern when the corresponding Large Tile 
.                  |       (eta,phi) had a Total (=EM+HD) Et that cleared its assigned threshold 
.                  |       from the Large Tile Reference set #0 which was programmed by COOR.
218E       4949    |                                                         |
                   |                                                         |
2190       4950    |
.                  | The Pattern information for Large Tile Threshold Reference set #1..7
.                  | follows the same format and ordering as Reference set #0.
.                  |                                                         |
.     4950:4954    | Jet Pattern for Large Tile Threshold Reference set #1   |  NOT ASSIGNED 
.     4955:4959    | Jet Pattern for Large Tile Threshold Reference set #2   |  NOT ASSIGNED 
.     4960:4964    | Jet Pattern for Large Tile Threshold Reference set #3   |  NOT ASSIGNED 
.     4965:4969    | Jet Pattern for Large Tile Threshold Reference set #4   |  NOT ASSIGNED 
.     4970:4974    | Jet Pattern for Large Tile Threshold Reference set #5   |  NOT ASSIGNED 
.     4975:4979    | Jet Pattern for Large Tile Threshold Reference set #6   |  NOT ASSIGNED 
.     4980:4984    | Jet Pattern for Large Tile Threshold Reference set #7   |  NOT ASSIGNED 
.                  |                                                         |
26EE       4984    |                                                         |
-------------------------------------------------------------------------------------------------------------
26F0  4985:4986    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Level 1.5
---------
26F4       4987    | The following 4 scalers were captured                   |
.                  | AFTER the conclusion of the last Level 1.5 Cycle        |
.     4987:4991    | Level 1.5 Dead Crossings Count     (5 bytes,low 1st)    |  NOT ASSIGNED
.     4992:4996    | Level 1.5 Pass Count               (5 bytes,low 1st)    |  NOT ASSIGNED
.     4997:5001    | Level 1.5 Fail Count               (5 bytes,low 1st)    |  NOT ASSIGNED
.     5002:5006    | Level 1.5 Time out Count           (5 bytes,low 1st)    |  NOT ASSIGNED
271A       5006    |                                                         |
                   |                                                         |
271C       5007    |                                                         |
.                  | Same 4 scalers as for items 4987:5006 but captured      |  NOT ASSIGNED 
.                  | BEFORE the beginning of the same Level 1.5 Cycle        |  
2742       5026    |                                                         |
                   |                                                         |

                                                                                                     Page 15
2744       5027    | The following states were captured                      |
.                  | AFTER the conclusion of the last Level 1.5 Cycle        |
.        5027+n    | Level 1.5 Specific Trigger Fired  8n thru 8n+7  (n=0:1) |  NOT ASSIGNED
.                  |       LSB is Level 1.5 Fired for Specific Trigger 8n    |
.                  |       MSB is Level 1.5 Fired for Specific Trigger 8n+7  |
.        5029+n    | Level 1.5 Control/Status Data                   (n=0:1) |  NOT ASSIGNED
                   |       LSB bit# 0 reserved                               |
                   |       MSB bit#15 reserved                               |
.        5031+n    | Level 1.5 Sp. Trigger Confirmed   8n thru 8n+7  (n=0:1) |  NOT ASSIGNED
.                  |       LSB is Level 1.5 Confirmed for Sp. Trigger 8n     |
.                  |       MSB is Level 1.5 Confirmed for Sp. Trigger 8n+7   |
.        5033+n    | Level 1.5 Sp. Trigger Rejected    8n thru 8n+7  (n=0:1) |  NOT ASSIGNED
.                  |       LSB is Level 1.5 Rejected for Sp. Trigger 8n      |
.                  |       MSB is Level 1.5 Rejected for Sp. Trigger 8n+7    |
.        5035+n    | Level 1.5 Answer                  8n thru 8n+7  (n=0:3) |  NOT ASSIGNED
.                  |       LSB is Answer State for Level 1.5 Term 8n         |
.                  |       MSB is Answer State for Level 1.5 Term 8n+7       |
.        5039+n    | Level 1.5 Done                    8n thru 8n+7  (n=0:3) |  NOT ASSIGNED
.                  |       LSB is Done State for Level 1.5 Term 8n           |
.                  |       MSB is Done State for Level 1.5 Term 8n+7         |
2762       5042    |                                                         |
                   |                                                         |
2764       5043    |                                                         |
.                  | Same states as for items 5027:5042 but captured         |  NOT ASSIGNED
.                  | for the beam crossing directly preceding                |  
.                  | the conclusion of the same Level 1.5 Cycle              |
2782       5058    |                                                         |
-------------------------------------------------------------------------------------------------------------
2784  5059:5060    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Absolute Time
-------------
                   | This absolute time is obtained over a vertical interconnect from the same Goodwin-Shea 
                   | front-end crate where the Level 1 VME Transfer Program Central also reads the Central 
                   | Detector pulser programming information (this information is appended to the end of 
                   | the L1 Data Block, not described in this document).
                   |
                   | No attempt is made by the Level 1 VME Transfer Program to interpret this data or to 
                   | check its validity as it passes through the L1 VME crate.
                   |
                   | The time is in ACnet BCD time format that is read from the Goodwin-Shea front-end crate 
                   | in two 32 bit words. These two longword are byte ordered in the L1 Data Block so that 
                   | they are in the proper format to be used as input to Fritz Bartlett's time 
                   | conversions routines on either a VMS or VAXELN system.
                   |
                   |         Zebra Longword N                     Zebra Longword N+1
                   |  ---------------------------------    ---------------------------------
                   |  MSB                           LSB    MSB                           LSB
                   |  ---------------   ---------------    ---------------   ---------------
                   |  | Day  | Hour |   | Year | Month|    | 15 Hz| 2 KHz|   |Minute|Second|
                   |  ---------------   ---------------    ---------------   ---------------
                   |    Byte   Byte       Byte   Byte        Byte   Byte       Byte   Byte
                   |     #4     #3         #2     #1          #4     #3         #2     #1
                   |
2788       5061    | Month  BCD encoded byte                                 | Year   BCD encoded byte
278A       5062    | Hour   BCD encoded byte                                 | Day    BCD encoded byte
278C       5063    | Second BCD encoded byte                                 | Minute BCD encoded byte
278E       5064    | 2 KHz  BCD encoded byte                                 | 15 Hz  BCD encoded byte
                   |                                                         |
2790       5065    |                                                         |
.                  | reserved for more Time information                      |  NOT ASSIGNED
279E       5072    |                                                         |
-------------------------------------------------------------------------------------------------------------
27A0  5073:5074    | Reserved for Intermediate Word Count
-------------------------------------------------------------------------------------------------------------
Additional Level 1 Scalers
--------------------------
27A4       5075    |                                                         |
.     5075:5079    | VME Transfer Program idle            (5 bytes, low 1st) |  NOT ASSIGNED
.     5080:5084    | Data Block Builder Busy                   (5 b,low 1st) |  NOT ASSIGNED 
.     5085:5089    | VME Transfer Program Prepare Data         (5 b,low 1st) |  NOT ASSIGNED 
.     5090:5094    | VME Trnsf Program Wait for free VBD Buffer(5 b,low 1st) |  NOT ASSIGNED 
.     5095:5099    | VME Trnsf Program Wait while VBD DMA Reads(5 b,low 1st) |  NOT ASSIGNED 
.     5100:5104    | VME Transfer Program Display Information  (5 b,low 1st) |  NOT ASSIGNED 
.                  | These scalers monitor the performance of the transfer of the Level 1 data to the 
.                  | Level 2 System. Each scaler is gated by its corresponding acquisition state, 
.                  | and incremented at the resolution of the beam crossing period (i.e. 3.5 musec)
27DE       5104    |                                                         |
                   |                                                         |

                                                                                                     Page 16
27E0       5105    |                                                         |
.  5b+5100:5b+5104 | LEVEL 1 FIRED for BUNCH #b  (5 bytes,low 1st)   (b=1:6) |  NOT ASSIGNED
.                  | Bunch b=1,2,..6 corresponds to bunch P1,P2,..P6         |
281A       5134    |                                                         |
                   |                                                         |
281C       5135    |                                                         |
.  5b+5130:5b+5134 | LEVEL 0 GOOD  for BUNCH #b  (5 bytes,low 1st)   (b=1:6) |  NOT ASSIGNED
.                  | Bunch b=1,2,..6 corresponds to bunch P1,P2,..P6         |
2856       5164    |                                                         |
                   |                                                         |
2858       5165    |                                                         |
.                  | LEVEL 1.5 SKIP COUNT                  (5 bytes,low 1st) |  NOT ASSIGNED
.                  | This Scaler increments for every Level 1.5 Cycle        |
.                  | that resulted  in the confirmation of an event          |
.                  | and its transfer to Level 2                             |
2860       5169    |                                                         |
                   |                                                         |
2862       5170    |                                                         |
.                  | DATA BLOCK BUILDER CYCLE COUNT         5 bytes,low 1st) |  NOT ASSIGNED
.                  | This Scaler increments for every New Data Block         |
.                  | Started by the Level 1 Data Block Builder.              |
286A       5174    |                                                         |
                   |                                                         |
286E       5175    |                                                         |
.                  | 4 SCALERS, reserved                   (5 bytes,low 1st) |  NOT ASSIGNED
.                  |  #1 is a copy of item 331:335  Level 1.5 Cycle Count    |
.                  |  #2 is a copy of item 336:340  Level 1.5 Potential Count|
.                  |  #3 is a copy of item 351:355  Level 0 Good Count       |
.                  |  #4 is a copy of item 356:360  Spare                    |
2892       5194    |                                                         |
-------------------------------------------------------------------------------------------------------------
Miscellaneus Other Foreign Quantities Scaled by Level 1
-------------------------------------------------------
2894       5195    | 44 SCALERS, NOT ASSIGNED YET
.  5415-5n:5419-5n | Foreign Scaler #n           (5 bytes,low 1st)  (n=1:44) |  NOT ASSIGNED
2A4A       5414    |                                                         |
-------------------------------------------------------------------------------------------------------------

[13m                                                                        Page 17

    12. MODIFICATIONS WITH RESPECT TO D0 NOTE 706
    ---------------------------------------------

- Change column name "first byte" to "low byte",
  and "second byte" to "high byte".

- Remove mention of the first unused item, and decrement the hexadecimal
  column by 02. This column is now the address offset with respect to the
  address of item #1 (in VAX memory only!).

- Modify numbering of Specific Triggers to start with number 0
  instead of 1, in items #1:320, #362:368, and in the Jet lists.

- Assign beam crossing scaler to item #341:345.

- Assign second lookup energy quantities to item #500:508.

- Move final trigger tower count items up by one item to #509:524.

- Assign Level 0 Vertex Information to item #525.

- Reserve items for Level 1.5 information.

- Reduce the reserved eta index coverage from +/- 24 to +/- 20.

- Align the beginning of the sections of energy values to zebra bank longwords.

- Change the definition of the Jet Lists, changed from two to eight lists.

- Modify the jet list format: the 16-bit relative address of each entry.
  is zero-extended to 32 bits so that one entry in a list can correctly fill
  two zebra bank longwords.

- Add a blank 16 bit item in the Jet Lists sections for alignment
  of each section, of the number of entries, and of each entry
  to a Zebra Bank 32 bit longword.

- Add section about programming of Specific Triggers. This section contains
  input parameters used to build the jet lists.


                                                                        Page 18

    13. MODIFICATIONS WITH RESPECT TO ORIGINAL REVISION OF THIS NOTE
    ----------------------------------------------------------------

- The Level 1 crate ID in TRGR bank is now 11 (was 1)

- Swap header longwords #5 and #6 in order to preserve trigger mask as
last word of the Level 1 Crate Header.

- The Energy offset in trigger tower ADC section is 8 (was 0)

- All global energies are 3 bytes of signed quantities, except for Missing
  Pt which is 1 byte unsigned.

- Rename item 321 from Trigger Number to Event Transfer Number and
  mention it is copied to the HEAD bank.

- Add Start Digitize Number at item 326 (was labeled reserved)

- Add Level 1.5 Cycle Count at item 331 (was labeled reserved)

- Add Potential Level 1.5 Count at item 336 (was labeled reserved)

- Add Gated Beam Crossing Scaler at item 346 (was labeled reserved)

- new Super Tower entry to Specific Trigger Programming data section

- new data section for Super Tower Jet Masks

- new data section for Level 1.5

- fill items 529:532 (were marked reserved for Level 1.5)

- new data section for Absolute Time

- new data section for additional Level 1 Scalers

- new data section for Other Foreign Quantities Scaled by Level 1

- refer to GZFIND_CRATE as a mean to access the first word of the Level 1
  Crate Header in the TRGR bank.

- refer to D0$PARAMS:BYTE_ORDER.PARAMS, FORTRAN BYTE and EQUIVALENCE, and
  scrap the section about VAX specific access method (due to the new,
  less restrictive D0 coding standards)

- add introduction to related utility routines of ZEBRA_UTIL and LEVEL1


    14. MODIFICATIONS WITH RESPECT REVISION B OF THIS NOTE
    ------------------------------------------------------

- The VME Transfer Program no longer builds the EM and Tot Et jet list (items
  #3633..3894 and #4893..4910 are now reserved). Instead, the Level 2 nodes,
  and/or any offline software interested in the jet list should call the
  routine L1UTIL_JET_LIST_BUILDER to create an EM or Tot Et Jet List. Note that
  all the information needed to create the list is included in the raw data.
  The Jet patterns are in items #3897..4536 and the Specific Trigger
  programming information is in items #4861..4892. 

- The Large Tile (formerly called reserved for Super Tower) Pattern is now
  defined in detail in items #4945..4984

- The Large Tile programming of Specific Triggers (formerly called reserved for
  Super Tower) is now defined in detail in items #4911..4942 

- Increase Version number from 5 to 9


                                                                        Page 19
                                APPENDIX I
                                ----------

                           THE JET LIST SERVICE
                           --------------------
                          of the Level 1 Trigger
                          to the Level 2 Trigger

                          D. Edmunds, P. Laurens,
                          J. Linnemann, H. Weerts

                             Revised 4-JUN-1990



    A. DEFINITION
    -------------

    The Calorimeter Trigger is designed to provide a set of jet candidates
to the Level 2 Trigger. This information is included in the First Level
Trigger Data Block, thus making it accessible to the Level 2 Node
processing the event. The towers in The Jet lists will be used by the
Level 2 System as input candidates to more elaborate algorithms.

    There is a total of two Jet Lists. One list of candidates is for EM Et
jets and is a merged result from the four EM Et Threshold (and associated
HD Veto) Reference Sets. One list of candidates is for Total (EM+HAD) Et
jets and is a merged result from the four Total Et Threshold Reference
Sets.

    B. TOWER ELIGIBILITY
    --------------------

    For a given Trigger Tower to appear in the EM Et Jet List it must have
an EM Et energy deposit greater than the threshold assigned to this
particular Trigger Tower in any of the four EM Et Threshold Reference Sets,
and it must also have an HD Et energy deposit smaller than the threshold
assigned to this particular Trigger Tower in the HD Veto Reference Set
associated with the EM Et Reference Set.

    For a given Trigger Tower to appear in the Total Et Jet List it must
have a Total (=EM+HD) Et energy deposit greater than the threshold assigned
to this particular Trigger Tower in any of the four Total Et Threshold
Reference Sets.

    Additionally, an EM Et (respectively Total Et) Reference Set that was
not used in the programming of any of the Specific Triggers that fired for
a given event will not contribute to the EM Et (respectively Total Et) Jet
List built for this event.

    The entries in each list will be ordered in Et with some restrictions
stated further in this document.

                                                                        Page 20

    C. FORMAT
    ---------

    Each list will start at a fixed address within the First Level Trigger
Data Block section of the "TRGR" Zebra Bank, but will have a number of
entries varying between 0 and 16.

    Each Jet List section in the First Level Trigger Data Block starts with
one 32 bit longword introducing the list.

    The first longword in a Jet list section should be parsed one byte at a
time. The first (least significant) byte forms an integer which is a count
of the number of entries in the list. This number can vary from 0 to 16.
The second byte will hold a flag describing whether the list is complete
for this event: the bit #7 (MSB) of this second byte will be set to one
when the list is incomplete.

    The rest of the list is made of 2*N longwords, with N equal to the low
byte of the first longword as described above. There are two longwords for
each tower candidate in the list.

    The first longword of an entry shows which Specific Triggers were
depending on this particular Trigger Tower to trigger for this event. This
first longword constitutes a 32 bit mask where bit #0 (LSB) corresponds to
Specific Trigger #0, and bit #31 (MSB) to Specific Trigger #31. A
particular bit is set to one in the mask when the corresponding Specific
Trigger: (1) fired for this beam crossing, and (2) was programmed with at
least one comparison on the count of Trigger Towers above one of the
Threshold Reference Sets cleared by this Trigger Tower candidate.

    The second longword of an entry specifies the relative byte address (in
VAX memory) of the EM Et of the Trigger Tower in the Data Block with
respect to the tower at (eta,phi)=(1,1). This relative address will only
range from 0 to 1279(=2*20*32-1). On VAX hardware, this relative address
can directly be used as an address offset with respect to the address of
the byte of EM Et energy of the Trigger Tower at (eta,phi)=(1,1). An
example of a subroutine converting this relative address to eta and phi
indices is given below.

    D. INCOMPLETE LIST
    ------------------

    Under normal conditions, the Trigger Towers in a Jet List will be
exactly the ordered list of all the towers with the highest energy deposits
that satisfied at least one of the Reference Sets. In order to remain
within the available processing time (before dead time is introduced), the
search for the highest towers will be aborted as soon as a new tower
candidate is found that saturates the list. When a search is aborted the
truncated list may not hold the towers with the highest energies, but the
first towers found before the search was aborted.

    Aborting the computation of one list does not prevent finishing the
computation of the other list.

                                                                        Page 21

    E. ORDERING
    -----------

    When the list was completed on time, it is also ordered in decreasing
EM Et (or Total Et) energy. That is the tower with the greatest energy
deposit is the first entry in the list. When the list is tagged as
incomplete, no attempt is made at ordering the entries.

    The ordering is performed on the energy quantities available in the
data block, namely the uncorrected Trigger Tower Transverse Energies
(calculated for an interaction vertex at the center of the detector). This
is a restriction existing on the meaning of the jet list: the towers are
selected on their vertex-corrected Et (based on the Fast Vertex Data from
the Level 0 Trigger), but ordered only on their uncorrected Et.

    F. IMPLEMENTATION
    -----------------

    This service will be implemented using a microprocessor on a VME module
accessing the first half of the First Level Trigger Data Block (data
corresponding to the beam crossing generating the jet lists). The
processing can start while the Data Block Builder is still writing the
second half of the data block (data dealing with the previous beam
crossing).

    G. EXAMPLE OF CONVERSION FROM RELATIVE ADDRESS TO ETA, PHI INDICES
    ------------------------------------------------------------------

      SUBROUTINE CONVERT_ADDRESS_TO_INDICES ( RELATIVE_ADDRESS,
     &                                        ETA, PHI )
C
C----------------------------------------------------------------------
C-   Purpose and Methods : Computation of eta and phi indices
C-                         of a Trigger Tower from the one dimensional
C-                         index given in a Level 1 jet list.
C-
C-   Inputs  : the relative address describing a Trigger Tower in a Jet List
C-
C-   Outputs : ETA and PHI Trigger Tower Indices.
C-
C-   Note : Better performance could be achieved by replacing
C-          the integer multiplications by bit field manipulations.
C-
C----------------------------------------------------------------------
C
      IMPLICIT    NONE
C
C       Arguments
C
      INTEGER     RELATIVE_ADDRESS, ETA, PHI
C
C       Local Variables
C
      INTEGER     SIGN_ETA, MAGN_ETA, WORK_ADDRESS
C

                                                                        Page 22
C       Compilation Constants
C
      INTEGER     POS_E, NEG_E
      PARAMETER ( POS_E = 0, NEG_E = 1 )
      INTEGER     ETA_COVERAGE, FIRST_NEGATIVE_ETA
      PARAMETER ( ETA_COVERAGE = 20,
     &            FIRST_NEGATIVE_ETA = 32 * ETA_COVERAGE )
C NOTE: The compilation constant ETA_COVERAGE would have to be changed
C       if the eta range covered in the Level 1 Data Block becomes
C       different from the current range of [-20..-1], [1..20]
C
C-------------------------------------------------------------------------
C       Executable Code
C
C       First find the sign of ETA. The positive eta indices come first.
C       Note: This section SHOULD be upgraded to verify that the relative
C       address is in the range from 0 to ( 2*32*ETA_COVERAGE - 1)
C
      IF ( RELATIVE_ADDRESS .GE. FIRST_NEGATIVE_ETA ) THEN
        SIGN_ETA = NEG_E
        WORK_ADDRESS = RELATIVE_ADDRESS - FIRST_NEGATIVE_ETA
      ELSE
        SIGN_ETA = POS_E
        WORK_ADDRESS = RELATIVE_ADDRESS
      END IF
C
C       The magnitude of the ETA index ranges from 1 to ETA_COVERAGE.
C       The eta index is monotonically increasing in magnitude after
C       each of the 32 phi values.
C
      MAGN_ETA = WORK_ADDRESS / 32
      WORK_ADDRESS = WORK_ADDRESS - 32 * MAGN_ETA
      MAGN_ETA = MAGN_ETA + 1
C
C       The PHI index ranges from 1 to 32.
C       even addresses cover PHI (1:16), odd addresses cove PHI (17:32)
C       cf. description of the Level 1 Trigger Data Block
C
      PHI = WORK_ADDRESS / 2
      IF ( ( WORK_ADDRESS - 2 * PHI ) .EQ. 0 ) THEN
        PHI = PHI + 1
      ELSE
        PHI = PHI + 17
      END IF
C
C       Final computation of ETA
C
      IF ( SIGN_ETA .EQ. POS_E ) THEN
        ETA = + MAGN_ETA
      ELSE
        ETA = - MAGN_ETA
      END IF
C
      RETURN
      END

                                                                        Page 23



                               APPENDIX II
                               -----------



                         DATA BLOCK FORMAT IN VME
                         ------------------------




    The First Level Trigger Data Block is built by the First Level Trigger
in VME memory. A VBD card (formerly called Data Cable Driver) will transfer
the data block from VME memory to VAX memory. The transfer is performed one
32-bit integer at a time and preserves the value of the transferred 32-bit
integers.

    The VME and VAX architectures however happen to store the 4 bytes of a
32-bit integer in opposite sequence in memory. The order of the bytes compared
between VME and VAX memory will thus appear locally reversed inside each
32-bit longword of the Zebra Bank.

    In order to produce the data block format defined by this document for
the VMS Zebra Bank, the data block must be built somewhat scrambled in VME
memory.

    The data block built in VME space only needs to match the target VMS
format by sub-sections.  The VBD card can then be directed to fetch and
concatenate a list of separate blocks of data in VME memory to produce the
final data block actually received by the Level 2 Nodes.