## Slide 1: P-ONE-1: System Overview and Digitization Update
Rob Halliday and Nathan Whitehorn

## Slide 2: System Design Philosophy
We are building the next-generation Optical Module that we really want:
Fast Full Waveform Digitization
Full bandwidth of optical fiber, power savings of copper
  Redundancy from having both available
Sub-nanosecond timing synchronization
On-OM data and trigger pre-processing

## Slide 3: (Very) High Level Block Diagram
x16
Digitizer
Data Handling and Processing + Slow Control
(FPGA)
Fiber Data and Timing Board
Copper Timing and Data Transfer Block
Power Supply/
DC-DC Conv.
Power To All OM Components
Cable Elements
PMTs
Calibration Devices

## Slide 4: Scenario: A DOM Floods
Kraken attacks, DOM floods

## Slide 5: Scenario: A DOM Floods
DOM floods
Current spikes at MJB – DOM is cut-off

## Slide 6: Scenario: A DOM Floods
Current spikes at MJB – DOM is cut-off
Reconfigure Timing I/Os
Pass Leader token
Resume Operations

## Slide 7: Digitizer
AD9083
Fast ADC meant for low power consumption applications such as cell tower beamforming and “electronic support measures”
16 Channels
12 bit and 16 bit modes
1.2W at our likely settings
  <100mw per channel average on all settings
250 Megasamples per second (200MSPS for us)
Built-in front-end filtering
x16

## Slide 8: Brains of the operation
PolarFire MPFS250T from Microchip
Low power modern FPGA and Processing System
16 High Speed Data (SerDes, 12.7 Gbps) Lanes
~1.7W Estimated Power Consumption
Plenty of General Purpose Inputs/Outputs for Timing/Data/Calibration
Quad Core Processor for data handling, slow control, etc.

## Slide 9
Timing Interface
Leader Timing/Data Board
Power Block
ADIN Switchceiver
(ADIN2111)
AD Clock Buffer
(AD4680E)
Upgoing 10MHz + PPS
Downgoing PPS
Timing Control Switch
10Base-T1L
Fiber From MJB
Power
Power To All DOM Components
Data
ADC (AD9083)
SPI
JESD204B Data
8GB+ DDR4
(2-5s Lookback)
AD Clock Synchronizers
(AD9546)
JESD204B CLK + Sysref
Microchip
FPGA + SoC
(MPFS-250T)
P-OM Block Diagram
PPS+10MHz
JESD Sysref

## Slide 10: FPGA + Digitizer
Development Updates

## Slide 11: Cast of Characters
PCIe x16 Connector
FMC connector
MPFS-ICICLE board
ADC AD9083 Eval. Board
Custom Adapter Board
Data over JESD204B Link
Slow Control over SPI Link

## Slide 12: Basic Steps
FPGA Bitstream
Instantiate Reference Design
Instantiate JESD204B block
Build Bitstream
Adapter Board
Identify needed connections
Build Design in KiCad
Print Prototype Board
Operating Software
Build Reference Linux
Add ADC Drivers
Add write-out abilities, either to SD or network
Build modified Linux

## Slide 13: Digitization Adapter Board
MPFS-ICICLE board
ADC AD9083 Eval. Board

## Slide 14: Digitization Development Boards
MPFS-ICICLE board
ADC AD9083 Eval. Board

## Slide 15: Layout of board
SerDes Lanes
Timing Outputs
Timing Outputs
Slow Control
Power Enable Jumper
PCI-E connector
ADC Eval Board Seat

## Slide 16: Instantiating JESD204B
Learning new (to me/us) Microchip development environment for FPGA gateware (“Libero”)
Using canned JESD204B core
Once correctly connected, move on to building linux with drivers

## Slide 17: Next step: Buy the (not-cheap) license
Was really hoping we could “try before we buy”
Looks like we will need to buy a license

## Slide 18: Conclusions
Digitization Development:
  Need to double check and order adapter board
  Time to buy the FPGA dev license (or get free!)
Once built:
  Record some pulses and determine timing resolution
  Measure approximate power usage
Mid future:
  Decide on power supply (Michael had suggestion)
  Layout prototype board using interface specs
Steady progress continues!